## Slide 1: UE Power Saving and Wakeup Mechanism
CATT
RP-172373
3GPP TSG RAN Meeting #78
Lisbon, Portugo, December 18-21, 2017

## Slide 2: NR System Design - UE Power Saving
UE power saving had been considered in the beginning of NR system design
  System design considers UE power consumption
Most UE power consumptions are on the system monitoring for potential data arrival
  IDLE mode UEs: UE will wake up periodically to decoding paging indication and retrieve paging information based on configured DRX cycle
  CONNECTED mode UEs - active state PDCCH decoding dominate power consumption in LTE[Ref: R1-166368 UE Power Consideration based on Days-of-Use, Qualcomm]
    UE decodes PDCCH every subframe with most of time no grant for its transmission
    High speed network access and robust data arrival have the results of no one is scheduled for services in large fraction of time.
    Time of usage – quiet time in the night.

## Slide 3: NR Power Saving features
NR-PDCCH monitoring –
  UE-specific DL control information monitoring occasions at least in time domain can be configured
    Network could configure longer duration for NR-PDCCH monitoring to reduce the power consumption on monitoring
      Tradeoff in access delay when traffic arrives
During NR study , UE power saving study on UE DL reception energy consumption with focus on DoU
  UE decoding power consumption in the physical layer DL control blind decoding in lack of grant
  UE decoding power consumption in the slot with the data
  UE decoding power consumption in the data reception process
  UE decoding power consumption in the measurement
  UE decoding power consumption in the Search Space
  UE power reduction techniques also should be studied
Enhance DRX – support multiple service with different service requirements

## Slide 4: UE Power Saving with On-demand Access
On-demand Access – UE remains in sleeping mode unless it is triggered
  UL data arrival from higher layer: UE will wake up and request for UL transmission
  Wakeup by network – Network wakes up UE on demand
    Arrival of DL data
    System information change
Power saving –
  UE wakes up only being triggered by wakeup signals with extended sleeping mode
DL data
t
Wakeup signals
Sent by gNB
UE waking up
Paging
PDCCH decoding
PDSCH decoding
Complete data reception
UE backs to sleep
UE sleeping
UE sleeping

## Slide 5: UE Wakeup Mechanism
UE Wakeup mechanism –
  Wakeup signal is sent on-demand
    Wakeup signals are sent when DL data arrives
      Low power or passive circuit
    DRX cycle is used to keep the UE within registration area
      DRX cycle could be extended to minutes to allow UE long sleep.
  Wakeup signal is sent along with DRX cycle
    Low-complexity wakeup signals, such as sequence-based signals, are sent before the ON period of DRX cycle
      UE perform detection of wakeup signals through peak detection of correlation function
      UE will wake up if wakeup signals is detected
      UE continues sleeping through ON period of DRX cycle if not receiving wakeup signals.

## Slide 6: Micro Sleep for CONNECTED Mode UEs
Less than 10% of UE PDCCH decoding with positive CRC
  90% power consumption on large number of blind decoding could be saved through UE micro sleep
Micro-sleep for CONNECTED mode UE in active reception –
  UE goes to micro sleep once finishing DL data reception
    Control mechanism to indicate the end of DL data transmission
    No PDCCH decoding
  Wakeup signal is sent to indicate DL scheduling grant for UEs.
    Wakeup signals are sent when new DL data arrives before scheduling
      Low complexity wakeup signals are sent before PDCCH decoding
    UE would decode PDCCH when it receives Wakeup signals
      Minimize the number of blind decoding
  UE performs channel tracking and CSI/RRM measurements in the background
    UE implementation choice to meet the performance requirements during micro sleep

## Slide 7: UE Wakeup Signals
Wakeup signal receiver – a front-end device with low or no power consumption
  Low power circuit
  Passive circuit: similar to RFID or ETC (Electrical Toll Collection) receiver
    Backscattering technology at the reciever –
      Highly reactive RF front end to stimulate the electromagnetic wave of the received signals from the gNB. The
      RF power is converted into DC power to power the control logic of wakeup trigger

## Slide 8: UE Wakeup System Design
Wakeup system design - wakeup signals and physical channel
  Wakeup signals - narrow band signals and waveform with high transmitted power
  Physical channel structure
    Inband wakeup channel – NR system have a specific physical channel (s) to transmit the wakeup signals
      Waveform does not need to be compatible with NR waveform – similar to NR-PSS/SSS with embedded physical channel
    Out-of-band physical channel – Wakeup physical channel is not part of data carrier
      Could be designed universally for all systems, such as NR, LTE, NB IoT, eMTC, …
        Flexibility in multi-mode UE wakeup.
      Using lower frequency band for wakeup signal for mmWave data carrier for improved coverage

## Slide 9: Wakeup Signals Design
Wakeup Signal Performance
  Receiver sensitivity – identify the required energy received to trigger wake up mechanism at UE receiver
    Passive circuit – compute the energy accumulation of back scattering technology
    Low power circuit – compute the energy required for the wakeup signal detection and power consumption in the detection
  Link budget – identify the coverage area based on a given Tx power and receiver sensitivity
    Tx power and PSD would be used for wakeup signal design
    Wakeup signals
      UE-specific wakeup signals : distinct signals for each UE
      Group wakeup signals:
    Wakeup strategy – similar to paging strategy, with UE registration
      Wakeup signals broadcasting area
      Blanket broadcast or sequential broadcast

## Slide 10: Wakeup Signals Type
Single tone beacon – no additional information
Multi-tone beacon – information extracted from the comb of beacons
  Multi-tone transmission in time or frequency (comb of color tones)
ON/OFF keying – single tone signal with modulated signals with embedded information, e.g., UE ID
ON-OFF keying
Multi-tone beacon
Single Tone beacon

## Slide 11: Wakeup Strategy Along with Wakeup Signals
Wakeup strategy with given wakeup signal design
  UE-specific wakeup – large number of distinct wakeup signals
    Wakeup signals alone could single out a specific UE for data arrival
  Group wakeup – small number of wakeup signals
    Wakeup signals along with paging indication to identify
Wakeup signals broadcasting strategy
  Single cell wakeup signals broadcasting
    UE tracking – UE register on new camping cell after long DRX
      Drawback: DRX cycle could be not too long to lose track of UE
  Group of cells wakeup signals broadcasting
    UE tracking within a group of cells – UE update the location when moving to new group of cells
  Implicit broadcasting – similar to paging without UE updated location
    Broadcast on the registration area.

## Slide 12: Higher Layer Procedures in Support of UE Wakeup
DRX enhancement with UE wakeup signals
  DRX cycle design for single cell or group of cells wakeup strategy
    Identify UE tracking strategy
  DRX cycle design for implicit broadcast strategy
    Extended UE sleeping cycle and UE registration area design
      UE mobility as the dependent variable
Paging enhancement with UE wakeup signals
  Paging mechanism along with reception of group wakeup signals
    Enhanced paging procedure with wakeup signals
    Need for Paging acknowledgement design
      Paging acknowledgement design
  Paging strategy –
    Working with wakeup strategy

## Slide 13: Conclusion
On-demand access provides an mechanism for UE power saving
  UE wakeup mechanism to wake up UE right after data arrival
    Minimizing UE periodic wakeup to check for paging or data arrival
    Reducing PDCCH monitoring
    Optimizing DRX
  Study of UE wakeup mechanism
    Wakeup signal and waveform design
    Channel design and operation
    Enhancement of paging and DRX