## Slide 1: Motivation for New WID: L2 UE-to-Network Relaying for IoT Devices
3GPP TSG RAN Meeting #78 RP-172451
Lisbon, Portugal, 18-21 December 2017
Document for: Discussion
Agenda Item: 10.1.1

## Slide 2: Contents
Background in 3GPP
Justification of SI/WI
Objectives of SI/WI

## Slide 3: Background in 3GPP
FeD2D study item completed this quarter
Achieved good results in studying a Layer 2 based UE-to-network relay architecture
  The studied architecture allows the network to manage the remote device as a full participant in the 3GPP ecosystem (“identify, address, and reach”)
  Enhancements to the sidelink are investigated with a focus on enhanced reliability, and suitability for unicast communication
IoT use cases were considered and the studied enhancements can be applied to IoT devices
  Many IoT features (CIoT optimisations, attachment without PDN, non-IP data) are transparent for a L2 relaying architecture
  PSM works for the remote UE (not the relay UE)
  Support of eDRX has some impact for the relay UE, to listen during the remote UE’s PTW

## Slide 4: Justification of SI/WI
The burgeoning population of IoT devices stand to benefit from relaying
  In real IoT deployments, a nontrivial fraction of devices experience deep coverage holes
  Need to maintain network connectivity for such devices, while conserving battery power
  Should offer services in a manner comparable to direct communication
  Data security should be guaranteed end to end between device and network, as it is today between a UE and the network
  Corresponding control and signalling procedures would be needed
  CIoT optimisations need to be supported
  The existing support for L3/IP relaying by PC5 does not meet the above criteria
  Remote device appears to the eNB as a bearer of the relay device, without its own separate identity
  Security cannot be assured between the network and the remote device (the relay UE has visibility into the remote UE’s data)
  Cannot easily support CIoT optimisations
Thus there is a need to specify a layer 2 based architecture that addresses these deficiencies, as studied in the FeD2D study item

## Slide 5: Justification of SI/WI
To support the unicast communication for relay, sidelink requires some enhancements
  As studied under FeD2D
  Further efficiency enhancements including DRX, link adaptation
  Efficiency for unicast requires power control instead of constant power broadcast transmission
  Support for bandwidth limited remote UEs, in keeping with the IoT objective of the WI
  RAN4 needs to specify core and performance requirements

## Slide 6: Objectives of SI/WI
The detailed objectives of the work item are to specify support for the following functionalities:
  Specify a layer 2 based UE-to-network relaying architecture following SA2 assumptions, including methods for E-UTRAN to identify, address, and reach an evolved Remote UE (i.e. eRemote UE) via an evolved ProSe UE-to-Network Relay UE (i.e. eRelay UE).
    Protocol stacks for relaying, including adaptation layer
    Signalling and procedures for the needed functionalities (security, connection management, access control, idle mode operation including DRX on sidelink)
  Specify LTE sidelink enhancements with efficient sidelink operation and low complexity/cost & low energy eRelay/eRemote functionality suitable for eMTC and NB-IoT UEs:
    Synchronisation enhancements including support of SLSS/PBCH format for 1 PRB bandwidth
    Discovery enhancements including support of 1 PRB bandwidth
    Unicast communication including enhancements for link adaptation, power control, and resource allocation
    Support of resource pool suitable for remote UEs with bandwidth limitation to 6 PRBs or 1 PRB
    RAN4 core and performance requirements

## Slide 7: Thank you !