## Slide 1
LTE URLLC support of high synchronization accuracy
www.huawei.com
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18-21, 2017
Agenda Item: 10.6.4
Huawei, HiSilicon
RP-172456
Notes: 讲解：
我希望向大家汇报三方面的情况。
行业趋势与华为战略
2013年经营业绩
未来（行业有希望，运营商选择我们，员工热情奋斗）

## Slide 2
Background
Factory automation and smart grid are two important use cases for URLLC [TR 22.804]
  Time synchronization is important for UEs to enable URLLC application.
  Time synchronization between UEs is essential to cooperation in discrete manufacturing and measurement in smart grid.
  Time synchronization via 3GPP network is low cost and it can support mobility

## Slide 3
Scenario1
Factory automation or automation control
  More and more mobile robots are used for flexible manufacturing , which could support mobility and reduce cost of cable deployment
  Different UEs are required to cooperate at exactly the same time as shown in Figure below. Any unsynchronized actions between the UEs may lead to a damage or interruption in the production line with possibly huge financial loss and safety problem.

## Slide 4
Scenario2
Smart grid
  Determination of fault location in high-voltage lines is very important for system stability in distribution electricity.
  Electricity fault will generate two electricity waves, the two UEs record the time of receiving the wave and send the time to the server.
  Fault location can be detected by the reported time of the two UEs
  More accurate time synchronization means more accurate fault location detection

## Slide 5
Discussion
eNB performs as the common time source so that time synchronization between UEs can be realized by time synchronization between UE and eNB
Assuming that the physical layer is not enhanced, the target accuracy of time synchronization between UE and eNB can be in µs level, e.g., +/-1.5us.

## Slide 6
Discussion
Solution 1: SIB16 enhancement
  In existing LTE system, SIB16 provides time information with limited accuracy. More accurate time information can be added in addition to support the high synchronization accuracy.
Solution 2: Dedicated RRC signaling.
  Transfer the high synchronization accuracy time information of a specific reference point via dedicated RRC signaling.

## Slide 7
Proposal
Support the absolute time synchronization between UE and eNB with an accuracy of µs level for URLLC scenarios.
Include the objective into the WID of LTE URLLC in Rel-15.

## Slide 8
Copyright©2015 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !