## Slide 1
Cross-link interference management and mitigation for NR in Rel-15
www.huawei.com
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18-21, 2017
Agenda Item: 9.2.1
Huawei, HiSilicon
RP-172479
Notes: 讲解：
我希望向大家汇报三方面的情况。
行业趋势与华为战略
2013年经营业绩
未来（行业有希望，运营商选择我们，员工热情奋斗）

## Slide 2
Status on duplexing flexibility and CLI mitigation
“Dynamic” DL/UL operation is an essential integral of NR design. CLI design progressed well but de-prioritized in RAN#77.
The completed NR frame structure design cohesively supports duplexing flexibility
  FDD operation on a paired spectrum
  Different transmission directions in either part of a paired spectrum
  Semi-static TDD operation on an unpaired spectrum
  Dynamic TDD operation on an unpaired spectrum
Significant L1 design efforts spent to support dynamic TDD operation, e.g. L1 dynamic slot format indicator, UE behaviour for handling RRC and L1 indicated DL/UL resource assignments, etc.
Cross link interference mitigation progressed well before RAN#77, e.g. details of UE-to-UE interference mitigation
  Cross-link interference mitigation was de-prioritized in RAN#77

## Slide 3
Necessity of CLI management in Rel-15
If UE-UE CLI management is not supported in Rel-15, Rel-15 and Rel-16 UEs still have UE-UE interference, which degrades both Rel-15 and Rel-16 UEs’ performance
If UE-UE CLI management is supported in Rel-15, UE-UE interference can be controlled from the very beginning, which ensures the forward compatibility
  Lessons learned from LTE eIMTA
Delaying UE-UE CLI management to Rel-16 will cause forward compatibility issues.
Feature | 5%-tile DL UPT (Mbps) | DL Average UPT (Mbps) | 5%-tile UL UPT (Mbps) | UL Average UPT (Mbps)
All UEs not supporting UE-UE CLI | 9.11 | 52.26 | 4.26 | 36.16
50% UEs supporting UE-UE CLI and the other 50% UEs do not | 12.66 | 61.16 | 4.42 | 39.86
All UEs supporting UE-UE CLI | 19.7 | 71.09 | 5.52 | 42.92
Detailed assumption can be found in appendix

## Slide 4
Spec impact of UE-UE CLI management in Rel-15
Additional specification work for UE-UE CLI mitigation in Rel-15 can be well defined with a reasonable scope
UE-UE CLI Management | Aspects | Potential Spec Impacts
RS Transmission | Measurement RS | Good convergence on reusing SRS
 | Timing Adjustment | Specify the Tx timing of SRS for CLI measurement
 | Tx Power | Allow configuration of multiple sets of parameters using the agreed SRS power control
RS Reception | IMR Configuration | Configuration of IMR for better UE-UE interference measurement
Reporting | Reporting Content | For both RSRP and RSSI UE-UE CLI measurement, mostly reuse existing RSRP and RSSI reporting framework

## Slide 5
Summary
“Dynamic” DL/UL operation is an essential integral of NR design. CLI design progressed well but de-prioritized in RAN#77
Delaying UE-UE CLI management to Rel-16 will cause forward compatibility issues
Additional specification work for UE-UE CLI mitigation in Rel-15 can be well defined with a reasonable scope
Proposal: Complete the UE-to-UE CLI mitigation in Rel-15, starting from the existing agreements

## Slide 6
Copyright©2015 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !

## Slide 7
Simulation Assumptions
Parameters | Assumptions
Layout | Single layer Indoor floor: (3 TRP per 120m x 50m)
Inter-BS distance | 40m
Minimum BS-UE (2D) distance | 0m
Minimum UE-UE (2D) distance | 3m
Carrier frequency | 4GHz
Simulation bandwidth | 20MHz per CC for 4GHz
Channel model | Follow TR 38.802
Penetration loss | Follow TR 38.802
BS Tx power | 24 dBm PA scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 24 dBm
UE Tx power | Maximum 23 dBm
BS antenna configuration | (M,N,P,Mg,Ng)=(4,4,2,1,1) (dH,dV)=(0.5,0.5)λ
BS antenna configuration | Ceiling-mount, Follow TR 38.802
Parameters | Assumptions
BS antenna height | 3m
BS antenna element gain + connector loss | 5dBi
BS antenna tilt | 90deg
BS receiver noise figure | 5dB
UE antenna elements | 2Tx and 2Rx
UE antenna configuration | Follow TR 38.802
UE antenna height | 1.5m
UE antenna gain | Follow the modeling of TR36.873
UE receiver noise figure | 9 dB
Traffic model | FTP traffic model 3 with packet size 0.5Mbytes DL: UL=1:1
UE distribution | For FTP traffic model 3: 10 users per TRP 100% indoor (3km/h)
UE receiver | MMSE-IRC
BS receiver | MMSE-IRC
UE association | based on RSRP measurement
Transmission mode | SU-MIMO