## Slide 1: On the interest of more flexible resource allocation for efeMTC
ORANGE, AT&T, Verizon, Ericsson
3GPP TSG RAN#78 18-21 December 2017 Lisbon, Portugal | TDoc RP-172503 Agenda Item 5.1

## Slide 2: Background
It has been shown in RAN1 [1, 2] that the activation of LTE-M support on a cell using Ressource Allocation Type 1 can create the reduction of up to 6,8% of spectrum utilisation and an unneeded throughput reduction for legacy LTE user
  In Downlink, this is due to the misalignement between RBG and LTE-M Narrowband, that neutralize up to 3 PRB and, for system bandwidth of 15 and 20 MHz, to inconsistancy between RBG and Narrowband size
  In Uplink, when only one UE need to be scheduled, this is due to the band fragmentation created by the allocation of the narrowband
More flexibility of the downlink resource allocation mechanism for BL UE would help to avoid or at least significantly reduce the above-mentioned degradations
Example of misalignment of narrowband and RBG, that neutralize 3 PRBs (leading to 6,8% reduction of spectrum utilization) of a 10 MHz LTE system bandwidth

## Slide 3: Background
Complexity and power consumption reduction required for BL-UE have been achieved thanks to several compromises among which one is the confinement of the MPDCCH into the narrowband
Those performances remain key factors for IoT applications
The increase of downlink / uplink resources allocation flexibility should not be made at the expense of significant increase of UE complexity or energy consumption.

## Slide 4: Proposals
Proposal 1: Consider the specification of a more flexible Uplink/Downlink resource allocation mechanism for BL-UE in Rel. 15
  add the mechanism within the scope of the existing efeMTC Rel15 WID
Proposal 2: Take the necessary approach so that this flexibility increase doesn't lead to significantly increased UE complexity or energy consumption.

## Slide 5: References
R1-1721286 – “On the interest of more flexible resource allocation for efeMTC”, source: Orange & ATT, 3GPP-RAN WG1 Meeting #91
R1-1712988 - “Flexible PDSCH/PUSCH resource allocation for MTC”, source: Ericsson , 3GPP TSG-RAN WG1 Meeting #90