## Slide 1: NR High-Reliability URLLC scope for RAN1/RAN2
Ericsson
RP-172817
Ag 9.2.1

## Slide 2: Background
Current WID captures (RP-172115):
Support of ultra-reliable part of URLLC [RAN1, RAN2, RAN4]
  Identify techniques to meet the URLLC requirements set forth by [TR38.913] starting after RAN#76
  Conduct corresponding URLLC specific normative work after RAN#78 for the selected techniques

## Slide 3: Status RAN1
PDCCH
  Compact DCI in DCI format 0_0 and 1_0
  Support of aggregation level 16 targeting high reliability and coverage
HARQ/Scheduling
  Data channel repetition for dynamic assignment/grant and for configured grant
    Factors 1, 2, 4 and 8
  Repetition on UCI on PUCCH over multiple slots
    Factors 1, 2, 4 and 8
  Configured UL grant and short SR periodicity
    Mainly low latency but also related to high reliability
  For UCI on PUSCH, beta offset selection based on DCI
  PUSCH frequency hopping
MCS/CQI table design
  Separate CQI table for URLLC
    Work remaining
  Two target BLER for MCS table design
    Work remaining
DL preemption
  Low latency but also related to high reliability

## Slide 4: RAN1 scope
Proposed scope in RAN1:
  Specify, CQI table and MCS table design targeting high reliability
    Based on the following identified need from RAN1 (RAN1 #90bis)
      Agreement:
        N separate CQI table(s) are supported for URLLC
          Downselect the value of N between 1 or 2
        Two target BLER are supported for URLLC
          Note: RRC signalling is used by gNB to select one of the two target BLER
          Note: The configuration of target BLER or CQI table is part of CSI report setting
  Study and specify if gains are identified
    Define a new DCI format(s) that has a smaller DCI payload size than DCI format 0-0 and DCI format 1-0 unicast data
    For a given carrier, PDCCH repetitions over same or multiple PDCCH monitoring occasion(s) of the same or multiple CORESET and search space
    Handle UL multiplexing of transmission with different reliability requirements (including the potential need for UL UE pre-emption)

## Slide 5: RAN1 topics (No consensus to include, but contributions allowed)
No consensus to include
  PUSCH UCI dropping rules considering URLLC data in PUSCH
  For configured UL grant and repetition, the UE may repeat always for K repetitions
  Aperiodic CSI on short PUCCH
  Channel coding for control and data targeting high reliability
  Explicit HARQ-ACK feedback for configured UL grant
  Beta offset(s) for UCI handling targeting very low code rate on data on PUSCH
  Robust URLLC UCI (CQI) mapping in PUSCH
  PUCCH/PUSCH increase the accumulated TPC power control step size

## Slide 6: RAN2 scope
Status:
  RAN2 has discussed and progressed on data duplication already before RAN#77. In RAN#77 data duplication was put on hold due to prioritization of Option 3 completion.
Proposed scope in RAN2:
  RAN2 should continue work on data duplication in DC and CA after RAN#78 as long as Option 3 and Option 2 have been discussed
    Note: Completion of data duplication in NR-NR DC is dependent on the general completion of NR-NR DC
    Note: For Q1 data duplication is only discussed in the user plane session
  In addition, RAN2 should discuss L2/L3 impacts of other RAN1 URLLC features, if any. Discussion takes place once RAN1 has progressed the work