## Slide 1
Motivation for Study on Enhancement for High Layer CU-DU Split
Source: China Telecom, CATT
3GPP TSG RAN Meeting #79 RP-180147
Chennai, India, March 19 - 22, 2018
Agenda Item: 9.1.4
Document for: Discussion

## Slide 2: Background
For high layer function split, it was agreed to standardize option 2-1 in Release 15.Based on the current standardization progress and new requirements in future NSA/SA network deployment, the enhancement for high layer CU/DU split should be studied in Rel-16,which are:
Handover Enhancement
01
Resource Utilization improvement
to avoid the unnecessary resource utilization for inter-gNB-DU duplicated transmission/fast re-transmission
02
System Capacity Enhancement
Intra-gNB CA could not be supported if the two cells are located in different DUs
Support of multiple Connection
03
to reduce the interruption time during Intra-gNB/inter-gNB-DU handover procedure
to introduce HO assistant information (e.g., Load Status report) provided by gNB-DU

## Slide 3
Since NR cell would be deployed in HF with continuous coverage, the handover between DUs may happen frequently. The interruption time during inter-gNB-DU handover procedure would impact the system performance seriously.
  How to reduce the handover interruption time for inter-gNB-DU scenario should be studied
For intra-CU/inter-cell handover, gNB-CU decides the target SpCell. Since gNB-CU doesn’t have the load status of each cell, gNB-CU may select a cell that is overloaded and the selected SpCell may be rejected by the gNB-DU.
In this case, extra delay for handover preparation would be introduced which would impact the overall performance of the handover procedure. If the handover is urgent, handover failure may happen since the suitable target SpCell could not be found promptly.
Handover Enhancement
to reduce the interruption time during Intra-gNB /inter-gNB-DU handover procedure
to introduce HO assistant information (e.g., Load Status report) provided by gNB-DU

## Slide 4: Resource Utilization improvement
For duplicated transmission within two DUs, duplicated resources would be allocated to the UE which maybe unnecessary, especially for DRB with AM mode.
For intra-gNB/ inter-gNB-DU fast re-transmission scenario, if some RLC PDU segments are lost in one leg, currently, the whole PDCP PDU will be re-transmitted in another leg. Similarly, in case of duplication transmission, currently, the discard mechanism only focus on PDCP PDU.
However, it is possible that other part of the data which share the same PDCP SN has already been transmitted successfully in the first leg. In this case, it is not necessary to re-transmit these data to save radio resources..
Inter-gNB-DU Duplicated Transmission
to further optimize radio resource utilization for duplicated transmission and fast re-transmission should be considered

## Slide 5: System Capacity Enhancement
For SA scenario, CA is an attractive technology to improve user's experience
With the introduction of CU/DU split, there may be cases that two adjacent gNB-DUs have overlapping coverage and so they may have the chance to aggregate for better performance.
Considering the coverage performance of sub-6 GHz is much more than that of above 6GHz, therefore the inter-gNB-DU CA scenario will be also existed in 5G era.
The potential solution should be transparent to UE
Currently, one gNB may include multiple gNB-DUs, it is not supported for one UE to connect to two or more gNB-DUs at the same time in EN-DC/NGEN-DC scenario.
However, considering the requirement of 5G,i.e.the target for peak data rate should be 20Gbps for downlink and 10Gbps for uplink, it is beneficial that UE could utilize the resources in two gNB-DUs to enable the high rate data transmission.
Support of inter-gNB-DU CA
Support of multiple
gNB-DUs connectivity
Based on the existing CU/DU architecture, further enhancement on how to support inter-gNB-DU CA is needed
Support of multiple gNB-DUs connectivity should be considered.

## Slide 6: Objective of this Study Item
The objectives of this SI are to:
  Identifying detailed solutions to reduce the interruption time during Intra-gNB/inter-gNB-DU handover procedure
  Identifying detailed solutions to introduce HO assistant information (e.g., Load Status report) provided by gNB-DU
  Identifying detailed solutions to minimize the utilization of radio resource for inter-gNB-DU duplicated transmission /fast re-transmission.
  Identifying detailed solutions to support intra-gNB/inter-gNB-DU CA to aggregate radio resources from two gNB-DUs for better performance.
  Identifying detailed solutions to support multiple gNB-DUs connectivity for EN-DC/NGEN-DC scenario.
  Study the necessary protocol functions and/or messages related to the possible identified solutions.
Time Budget: Jun,2018~Dec,2018

## Slide 7
Thanks For
Your Attention