## Slide 1: Summary on moderated e-mail discussion regarding flexible/full duplex SIDs
LG Electronics Inc.
3GPP RAN#79
Chennai, India, March 19-22
Agenda 9.1.1
RP-180323

## Slide 2
Background (Objectives related to Flexible Duplex)
RP-172483:
  Uplink enhancements (and potential Rel-15 leftovers) [RAN1, RAN2, RAN4]
    [UE-UE CLI management and mitigation]
  Specify conditions for paired spectrum allowing flexible duplex operation, i.e.
    Allowing SRS in DL part of a paired spectrum
    Allowing low power BS transmission in UL part of a paired spectrum

## Slide 3
Background (Objectives related to Flexible Duplex)
RP-172636:
  The main objectives of this work are to study enhanced mechanisms for duplexing flexibility and supporting full duplex in both paired and unpaired spectrum. The feasibility and benefits of interference mitigation and resource sharing mechanisms to support flexible resource adaptation of NR-cells in co-channel and adjacent legacy FDD/TDD spectrums will be evaluated for both unpaired and paired spectrum.
  To study enhanced mechanisms for providing better duplexing flexibility in unpaired and paired spectrum. Development scenarios and use cases of Rel-15 NR SI/WI are the starting point for the discussions (for both unpaired and paired spectrum in co-channel and adjacent channel scenarios). The detailed objectives are:
  Identify and evaluate the enabler for advanced cross-link interference mitigation schemes, e.g. cross-link interference cancellation receivers, cross-link interference measurement, and cross-link interference coordination.[RAN1, RAN4]
    It is assumed that downlink and uplink resources in a band can be multiplexed in TDM manner.
  Identify additional physical layer impacts (if any) to support enhanced duplexing flexibility [RAN1]

## Slide 4
Background (Objectives related to Full Duplex)
RP-172636
To study mechanisms and benefits for providing full duplex operations in unpaired and paired spectrum. The detail objectives are:
  Identify deployment scenarios and use cases, and evaluate the benefits of full duplex (i.e., simultaneous DL/UL transmission on the same resource and/or DL/UL multiplexed in a FDM manner) with or without interference mitigation/cancellation/coordination techniques in such scenarios [RAN1].
  Study potential interference mitigation/cancelation/coordination techniques to allow downlink and uplink at a band in FDM manner (e.g., guard band configuration) and/or full duplex capability at gNB, (e.g., self-interference cancellation, cross-link interference mitigation/coordination techniques among UEs in the same cell) [RAN1, RAN4]
  The study consider scenarios where all or only a subset of gNBs in the network are capable of full duplex operation.
  Study Flexible and Full Duplex Radio (FDR) concept for adaptive resource allocation with legacy cellular systems including TDM/FDM. [RAN1]
  Study techniques to identify potential FDR served users within the network region [RAN1 or RAN3]
  Study new assistant techniques to enhance link performance and resource management efficiency of Flexible and Full Duplex Radio. [RAN 1]
  Identify additional physical layer impacts necessary to support full duplex operations. [RAN1]

## Slide 5
Comments/Discussions on Flexible Duplex
Coexistence among operators in the same or adjacent bands should be ensured (Telecom Italia, Softbank)
Regarding flexible duplex in paired spectrum
  Lower priority compared to unpaired spectrum (Softbank, Qualcomm, ZTE, Telecom Italia)
    Concerns include regulatory restriction, coexistence issue, etc.
  Equal priority to unpaired spectrum (KT, China Telecom, Huawei, LG)
    Use cases on underutilized uplink were mentioned.
  Suggestions to split discussion into sub-topics on flexible duplex in unpaired, flexible duplex on paired and full duplex (Nokia, Intel, Ericsson, Samsung)
  Common design on flexible duplex in both paired and unpaired spectrum (VIVO, Huawei, LG)
RAN3 scope on interference coordination (Nokia)
Clarification on potential techniques beyond CLI measurements is needed (Ericsson, MediaTek)
Proposals
  Add objectives on coexistence mechanism among operators in the same or adjacent bands
  Add RAN3 as a working group in coexistence study for interference coordination schemes
  Further discuss any clarification on objectives on flexible duplex is necessary assuming enabling techniques for flexible duplex in paired and unpaired spectrum are common (e.g., frequency bands, clarification on enabling techniques for CLI beyond CLI measurements)

## Slide 6
Discussion on Full Duplex
There were a few comments that work on full duplex is not urgent.
Proposals:
  Further discuss whether to separate flexible duplex and full duplex in different WID/SIDs or down-scope full duplex work

## Slide 7
Updated Objectives on Flexible Duplex (Proposed)
The main objectives of this work are to study enhanced mechanisms for duplexing flexibility and supporting full duplex in both paired and unpaired spectrum. The feasibility and benefits of interference mitigation and resource sharing mechanisms to support flexible resource adaptation of NR-cells in co-channel and adjacent legacy FDD/TDD spectrums will be evaluated for both unpaired and paired spectrum. The proposed study will cover the following objectives:
To study enhanced mechanisms for providing better duplexing flexibility in unpaired and paired spectrum. Development scenarios and use cases of Rel-15 NR SI/WI are the starting point for the discussions. The detailed objectives are:
  Identify and evaluate the enabler for advanced cross-link interference mitigation schemes, e.g. cross-link interference cancellation receivers, cross-link interference measurement, and cross-link interference coordination.[RAN1, RAN4, RAN3]
    It is assumed that downlink and uplink resources in a band can be multiplexed in TDM manner.
    Coexistence among different operators in the same or adjacent bands should be considered
  Identify additional physical layer impacts (if any) to support enhanced duplexing flexibility [RAN1]