## Slide 1
RP-180354
Nokia, Nokia Shanghai Bell
RAN#79
Chennai, India, 19 - 22 March, 2018
Motivation for New WID on Further enhancements for Extended Coverage GSM for Cellular IoT (EC-GSM-IoT)

## Slide 2: Background
As per the feasibility study on ultra-low complexity Cellular IoT systems in 3GPP TR 45.820 the battery lifetime of CIoT devices identifies a key objective and thus optimization of the energy consumption is needed for leveraging Cellular IoT technologies.
In particular, further optimisation of idle mode tasks of CIoT devices such as page monitoring and system information acquisition is required.
With new CIoT use case requirements, in particular low latency for infrequent network commands, the energy consumption in idle mode considerably increases due to the need for more frequent page monitoring, thus requiring additional energy saving procedures for page monitoring.
Similar improvements are introduced in Rel-15 for LTE-M and NB-IoT. Thus support of procedures improving battery lifetime is also required for EC-GSM-IoT as a member of the 3GPP technologies for CIoT.
On Enhanced Coverage Restriction, introduced on NAS level in Rel-14, liaisons have been exchanged with SA2 and CT1 to receive guidance. At RAN6#7 it was agreed to introduce the functionality on AS level in Rel-14, hence it has been removed from the WI objectives vs. RP-172525 submitted to RAN#78.

## Slide 3
The battery lifetime estimation in 3GPP TR 45.820 assumes that the device in idle mode is using PSM and thus ignores the energy consumption due to wake-up for paging occasions (see entry “No-EDRX” in Figure 1).
However, when having an eDRX configuration activated, the battery lifetime considerably reduces along the reduction of the eDRX cycle length, see Figure 1.
Further optimization of idle mode tasks by enhancements of the current procedures are thus required to improve the battery lifetime, in particular for configurations with shorter eDRX cycle.
Figure 1 - Battery life time for various eDRX cycles
Traffic profile: 1 MAR (220 Bytes) / Day.
Impact of eDRX cycle length on battery lifetime

## Slide 4
For idle mode MS with low mobility, receiving infrequent network commands, the major component of energy consumption is System Information (SI) acquisition in the new cell prior to page monitoring.
  The energy consumption for SI acquisition during cell reselection, assuming one cell-change/30 minutes, is approximately 40% of the energy consumption for a single MAR, for a traffic profile with MAR (50 Bytes)/2 hours (use case: tracking device reporting its location every 2 hours once).
  With mobility rate of 2 cell changes/hour, the battery lifetime drops from 14.1 years to 5.2 years considering the energy consumption for SI acquisition after cell reselection.
  If SI acquisition is optimized, the battery lifetime can be improved up to 35% for mobility scenario of 2 cell changes/hour, assuming a traffic profile of 1 MAR (50 Bytes)/2 hours, i.e. to 7 years [1].
  Note: Above figures are based on initial estimation of energy consumption for 4 EC SI messages on EC-BCCH assuming MS in CC2 coverage condition.
Thus following enhancements to SI acquisition for mobility scenarios will be investigated:
  Maintaining common system information related to idle mode across a group of cells (e.g. cells in the same Routing Area)
  Providing paging group organization related information on the common control channel in addition to SI on broadcast channel to avoid the need for SI acquisition in the new cell after synchronization to cell.
Proposed Work Area: System Information Acquisition Enhancements

## Slide 5
For further energy saving, a new Coverage Class specific paging indication channel to indicate the presence of a paging block in the control multi-frame will be investigated, with following characteristics:
  The channel is mapped onto one or two bursts only.
  The presence of a paging request is indicated by a single bit or few bits allowing for robust detection of the device in extended coverage condition.
  On evaluating the content of the paging indication channel, the MS moves back to deep sleep in case of no present page or continues to read the paging block in case of present page.
  The energy consumption assuming MS in CC4 coverage condition is evaluated to be around 25% [1].
  Due to transmission of the new paging indication channel in the control multi-frame, only a small reduction in EC-AGCH capacity for CC1 devices is observed (4%).
Proposed Work Area: Enhancement due to Paging Indication Channel

## Slide 6
Battery lifetime optimisation for idle mode MS in low mobility scenarios can be achieved by reduced time for SI acquisition after cell reselection.
  If SI acquisition during mobility is optimised for traffic and mobility profile of the tracking device, the battery lifetime can be improved up to 35% for MS in CC2 coverage condition (see slide 4).
By introducing a paging indication channel, the MS energy consumption for paging reception can be considerably reduced,
  up to 25% from current energy consumption level for Rel-13 for MS in CC4 coverage condition (see slide 5).
Both enhancements can be implemented for both Rel-13 and Rel-14 EC-GSM-IoT devices as optional feature.
The accompanying WID is submitted in [2].
[1] R6-180020 On Further Energy Saving for EC-GSM-IoT, Nokia, Nokia Shanghai Bell, RAN6#7
[2] RP-180066 New WID on Further enhancements for Extended Coverage GSM for support of Cellular Internet of Things (EC-GSM-IoT), source: RAN6, RAN#79
Benefits