## Slide 1: Motivation for Rel-16 New WID on “Further Enhancements to Support for Aerial Vehicles in LTE”
3GPP TSG RAN Meeting #79
Chennai, India, March 19-22, 2018
RP-180370

## Slide 2: Background
Rel-15 SI on Enhanced Support for Aerial Vehicles completed in Dec. 2017
Rel-15 New WID on “Enhanced LTE Support for Aerial Vehicles” was approved in Dec. 2017, with a limited scope:
  Improved mobility performance and interference detection
  Indication of UE’s airborne status and indication of the UE’s support of UAV related functions
  UL power control enhancements
In the SI performance enhancements for high speed scenario in TR 36.878
  Identify the essential procedure enhancement under high speed train scenario if needed
  Handover procedure enhancement
  Interference coordination procedure enhancement

## Slide 3: Business value, applications, and use case requirements
Future applications for UAVs
Power distribution tower inspection
Package delivery
Flying cameras to send back videos or pictures
 | Agriculture | Inspection on Grid, Oil and Gas and BS | Safety and Aerial | Transport+ Shipment | Others
Typical attitude | <20m | <1000m | <300m | End point：<120m ; Branch：3000m; Trunk line：6000m | 300m~5000m
Command & Control | One way 50ms；60-100 kbps (UL/DL)；Up to 10-3 Packet Loss Rate |  |  |  | 
High data rate & larger BW | 1K HD | 1K HD | 1K~4K HD |  | 
 | (1) 1K HD video：2M/8Mbps (12/60fps); 4k HD video：30M/60Mbps(30/60fps); 8k video：100Mbps~200Mbps(30/60fps) |  |  |  | 
MNO：Achieve 100% access to UAV market
Communication service $ value by 2025:
  $100/year for civil UAV (85%) ~$4.6 bn
  $1000/year for commercial UAVs (15%) ~$8.2 bn
LTE is a ready-made network to establish this new cellular communications market

## Slide 4: Frequent HO and increased HO failure rate
2X more handover due to cell fragmentation
2X-15X more HOF due to high interference at 100m
Simulation result
Chart: Handover rate(HO/UE/Sec) - Uma
| 0m | 50m | 100m
3Km/h | 0.036206 | 0.018575 | 0.023728
30Km/h | 0.057785 | 0.11154 | 0.12281
60Km/h | 0.0975 | 0.19171 | 0.23186
160Km/h | 0.2302 | 0.38643 | 0.45798
Chart: HOF rate(%) - Uma
| 0m | 50m | 100m
3Km/h | 0.059358 | 0.58442 | 0.87616
30Km/h | 0.17116 | 0.72316 | 0.8875
60Km/h | 0.26811 | 0.78117 | 0.91431
160Km/h | 0.45828 | 0.85813 | 0.93386
Coverage Fragmentation
Normal Coverage

## Slide 5: Severe interference to aerial UEs (DL) and terrestrial UEs (UL)
Severe UL interference to ground UEs
0 0.1 1 3 5
Aerial number per cell
increase of Thermal (dB)
UL power control on aerial UEs will limit interference to ground UEs at the cost of reducing aerial UEs’ throughput
Still high UL interference among aerial UEs
Severe DL interference for aerial UEs
Geometry SINR (dB)
CDF
*Case 1: 0 aerial UEs and 15 terrestrial UEs per sector
*Case 5: 5 aerial UEs and 10 terrestrial UEs per sector

## Slide 6: Similar Issues for High-Speed Train and Massive D-MIMO
DL interference in distributed massive MIMO
Frequent HO and severe
interference for high speed train
Handover procedure enhancement
Interference coordination procedure enhancement

## Slide 7: Rel-16 objectives for HO enhancement and interference mitigation
Introduce enhanced support for reduction of cell re-selection, connected-mode handovers, and handover failure rate for highly mobile devices
  Solutions may be applicable to UEs as aerial vehicles (as studied in TR 36.777) and high-speed trains scenarios (as studied in TR 36.878).
Introduce enhanced support for interference mitigation on CRS and DL control channels in the presence of strong interference from multiple transmitters
  The transmitters can be macro cell sites to serve aerial UEs, or TPs cooperating in massive MIMO