## Slide 1
Motivation for new WI on NB-IoT evolution and even further enhancements
www.huawei.com
3GPP TSG RAN Meeting #79
Chennai, India, March 19-22, 2018
Agenda Item: 10.1.1
Huawei, HiSilicon
RP-180372
Notes: 讲解：
我希望向大家汇报三方面的情况。
行业趋势与华为战略
2013年经营业绩
未来（行业有希望，运营商选择我们，员工热情奋斗）

## Slide 2
Justification
NB-IoT introduced a new air interface optimized for LPWA to enable an ultra-low cost UE for IoT services. After enhancements in Rel-14 and Rel-15, NB-IoT supports additional functions and scenarios. Power consumption and latency requirements also continue to drive enhancements.
Positioning: E-CID and OTDOA
Multi-cast: SC-PTM
Capacity: Paging and RACH on non-anchor carrier
Peak data rate: extended TBS and 2 HARQ
Mobility: optimization for RRC connection re-establishment
Wake-up signal
Early data transmission during RACH procedure
TDD
Small cell
Stand-alone + in-band/guard-band for multi-carrier
etc.

## Slide 3
Justification
NB-IoT has been deployed and demonstrated competent for sensor report use cases e.g. metering. Nowadays, it is also used to provide services other than sensor report such as shared bicycle, smart streetlight etc. which may have different traffic model, latency/power consumption, capacity and mobility requirements. In some use cases e.g. underground gas pipeline monitor may have extreme coverage requirement beyond 20dB extension. There are also some non-3GPP competitions providing more simpler solution than 3GPP for some of the IoT use cases which may result in lower power consumption even they can not provide telecom level service.
      In Rel-16, NB-IoT can continue to further improve the power consumption, latency, capacity, mobility, coverage etc. to fulfil more strict requirements of new use cases. Additionally, considering the nature of long lifecycle for IoT service deployment and 5G NR will finished its first version in Rel-15, it is the right time to consider NB-IoT connecting to 5G-CN in Rel-16. Furthermore, some operators plan to deploy both NB-IoT and eMTC onwards mMTC, technical convergence also can be considered in Rel-16 which saves cost for the operators.

## Slide 4
Power consumption and latency even further reduction
Motivation
UE power consumption is mainly due to the duration of UE Rx/Tx on-time. In Rel-15, an NB-IoT UE in RRC_IDLE mode can transmit ‘early data’ in Msg3.
Signaling overhead in NB-IoT can still be reduced by comparison to some non-3GPP technologies, whilst still providing a telecoms-grade service
Continue to bear down on power consumption and latency simultaneously to support wide range of IoT applications from all spheres
Main features
UE in RRC_IDLE can transmit data before Msg3 without UL grant
UE in RRC_CONNECTED can transmit data without UL grant or with simplified control less grant
Waveform other than SC-FDMA (e.g. FDMA) requiring less-orthogonality and allowing more-relaxed TA alignment between different UEs can be studied

## Slide 5
More dynamic access and scheduling
Motivation
Introducing UL transmission without grant will lead to colliding transmissions between UEs. Handling of multiplexing on a shares resource needs to be introduced to deal with this.
New use cases e.g. shared bicycle or smart streetlight may have new traffic characteristics of denser report than daily report sensors which requires more system resource.
  Relying on static or semi-static configuration of more resource to handle the unexpected application traffic is not efficient. Dynamic schemes for multi-user resource sharing would improve the efficiency of the system.
NB-IoT does not have DL CSI. Introducing aperiodic downlink CSI report (with minimum power consumption) to the network improves resource utilization efficiency as UE numbers grow
Main features
Schemes for UL multi-user multiple access on shared resource, e.g. frequency or time domain CDM, MU-MIMO without increase the number of antennas at the UE)
Enhanced eNB receiver to detect multiple users in a resource
Aperiodic downlink CSI report with minimum additional power consumption.

## Slide 6
More efficient paging for dense IoT deployment
Motivation
IoT devices are often deployed as groups with a common application, e.g. smart streetlights. These may be controlled, e.g. on/off by the IoT application layer with a tight response-time window after being paged. The application layer message can be very small in such cases, but sent to many UEs.
Using the MBMS service is not efficient to serve such small size DL command message transmissions, and requires many network nodes to be deployed.
Main features
Support mapping between user groups and group RNTIs.
Efficient transmission of paging commands, and other DL transmissions, to groups of UEs

## Slide 7
NB-IoT connectivity to 5G-CN
Motivation
Standalone NR will be standardized in Rel-15, with the 5G-CN deployment. It will be beneficial to support NB-IoT connecting to 5G-CN considering the long lifecycle of IoT service.
Main features
Similar work as undertaken in WI “LTE Connectivity to 5G Core Network (5G-CN)” with focus on NB-IoT.

## Slide 8
Mobility further enhancement to support handover
Motivation
Rich LPWA applications benefit from (enabled by) handover. e.g. low-end wearable devices for old people and children tracking (no voice support), pet tracking, logistics/assets tracking
Handover is an essential cellular feature which competes with unlicensed LPWA technology
Some chipset vendors plan to replace GPRS products by NB-IoT
NB-IoT already supports NRSRP/NRSRQ measurement and report in Msg5 recently
Introduce handover as an optional feature for NB-IoT to support better mobility
Main features
Procedure simplification, e.g. no dedicated signaling for measurement control and report
Handover decision based on at least measurement results in Msg5

## Slide 9
Deep convergence of CIoT
Motivation
NB-IoT is decoupled with eMBB and has minimum system bandwidth of 0.2MHz. It enables a low cost UE with low data rate. Meanwhile, eMTC is coupled with eMBB and has minimum system bandwidth 1.4MHz with medium data rate.
Running 2 IoT networks brings more complexity and OPEX (network planning, duplicated system information, etc), there is a chance for convergence.
Deep convergence of the two technologies to a unified IoT network, which supports both low cost UE and diverse IoT use cases. It maintains decoupling with eMBB cell and MNO’s OPEX can be reduced.
The system can be flexibly deployed in less than 1.4MHz spectrum. (e.g. real requirement from one operator in RP-172282) and coexistence with NR by flexibly sharing the resource.
Reuse existing UE chipset industry (NB-IoT and eMTC) including dual mode UE, only software update needed.
Main features
UE is able to access from NB-IoT anchor carrier in a backward compatible way.
For more than 1PRB scheduling: at least eMTC based method is supported.

## Slide 10
Further extend coverage by multi-hop relay
Motivation
Some use cases e.g. underground gas pipeline monitor may require very deep coverage beyond 20dB. However, the commercial end users may require 100% coverage services. Multi-hop relay can be used in this scenario.
Technologies based on NB-IoT is preferred to provide further extended coverage by some operators requests.
Both macro cell and small cell are supported since Rel-15. Network based relay provides a continuous wireless connection solution for IoT, the UEs only needs to support NB-IoT air-interface and the legacy NB-IoT UEs also can get the benefit from network based relay.
Main features
Relay nodes support two types of access：UE and/or Relay nodes (if more than 2 hops).
  Relay nodes at least as layer 3 relay without support of S1 and X2 interface.

## Slide 11
Copyright©2015 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !