## Slide 1
Title: Motivation for New Study Item for Fast Cell Access for NR
Source: Nokia
Document for: Discussion
Agenda Item: 9.1.3
3GPP TSG RAN Meeting #79 RP-180434
Chennai, India, March 19th – 22nd, 2018

## Slide 2: Rel-16 Fast Cell Access SI for NR
In Rel-15, there is an on-going the RAN2-led LTE WI on Enhancing CA Utilization [RP-170805]
  The main goal of this WI is to improve latency of SCell set-up times for all scenarios (IDLECONNECTED transition for first time CA setup and Scell addition in CONNECTED)
  Reducing SCell setup delay (including detection, measurement, configuration and activation) shows improved UE throughput and lower UE power consumption (due to shorter active time)
Learnings from Rel-15 LTE euCA WI
  LTE: Up to 5x throughput when the delay is reduced from 500 ms to 100 ms or below
  LTE: Substantial (e.g. up to 6-7 minutes) of extra small cell measurements (per call) – before break-even point in energy consumption

## Slide 3: Rel-16 Fast Cell Access SI for NR
Small Cell deployments are becoming more common with NR (especially for high frequency bands, which often have naturally limited coverage), leading to use of localized cells in an opportunistic manner
Higher frequencies will cause new problems for accessing cells, requiring faster recovery of serving cell in case of e.g. beam blockage
  Both FR1 and FR2 should be considered in studies to have best NR performance
The lower the latency and the higher the throughput, the shorter the call, leading to net positive effect in UE power consumption, better resource utilization over shorter time and improved user experience
Measurement availability will be critical in fast cell utilization
  E.g. Use of CA is limited by the delays in starting to use SCell(s)
Motivation for NR Fast Cell Access
Macro layer
Small cell layer
UE

## Slide 4: Rel-16 Fast Cell Access SI for NR
Evaluation of LTE vs. NR: UE throughput impact of fast cell access in NR
LTE
LTE Scenario (10MHz + 10MHz)
NR Scenario (10MHz + 40MHz)
5G
NR: Gain between 5x-10x gains in mean user throughput
LTE: Gain between 1.4x – 5x gains in mean user throughput
  In NR, the performance impact of faster cell access may be even larger than in LTE due to the larger system bandwidth and throughput difference between the macro cell and the small cell.

## Slide 5: Rel-16 Fast Cell Access SI for NR
Evaluation of LTE vs. NR: UE power consumption impact of fast cell access in NR
LTE
LTE Scenario (10MHz + 10MHz)
NR Scenario (10MHz + 40MHz)
5G
Positive impact of fast cell access in both LTE and NR:
Faster cell access means more energy-efficiency in data transmission
Clear reduction in energy consumption with shorter delay due to faster offload

## Slide 6: Rel-16 Fast Cell Access SI for NR
Summary of benefits of Fast Cell Access
Traffic arrival
(S)Cell activated
Delay
Throughput
Time
Summary of benefits of fast cell access :
More efficient cell usage (more data scheduled via all cells)
Enabling faster CA/DC/EN-DC configurations and activations
Faster data offloading (e.g. from PCell to other Cell(s))
Better resource utilization in the (e.g. CA/DC/EN-DC) network
Improved user throughput
Enhanced capacity (especially when PCell capacity is limiting and wide bandwidth is available e.g. for SCell)
Fast cell access enhancements are beneficial for several
scenarios, e.g. CA, LAA, LTE DC, MR-DC (any option X)

## Slide 7: Rel-16 Fast Cell Access SI for NR
Proposal: RAN to approve a RAN2-led Rel-16 SI with goal to study how to have as fast as possible (S)cell access
  RAN2 procedures to enable Fast Cell Access, including measurement reporting
  RAN4 evaluation on how to have low latency setup and measurements with balanced with UE power consumption
Key goals
    Fast cell set-up: Setting up and maintaining serving cells as fast as possible
      Low latency measurements of candidate cells
      Low latency serving cell configuration/activation
      Minimized signaling overhead for initial cell setup
    Low overhead serving cell configuration/activation
      Setup UE for UP transmissions as fast as possible
    Expedited recovery from serving cell failure cases
      Recovery from RLF/S-RLF (esp. when MR-DC has been setup, to allow reusing the existing cell configurations also for recovery purposes)
Fast Cell Access: NR SI proposal and goals