## Slide 1: On Measurement Uncertainty and Test Tolerance
ORANGE
3GPP TSG RAN#79 19-22 January 2018 Chennai, India | TDoc RP-180439 Agenda Item 9.2.1

## Slide 2: Background
In the January RAN5 5G-NR Adhoc Meeting #1, several companies suggested to shift responsibilities from RAN4 to RAN5 to define Measurement Uncertainty (MU) for NR UE RF, demodulation and RRM test cases.
In the RAN WG4 Meeting AH-1801 last January, RAN4 agreed with the RAN5 proposal to shift MU responsibilities.
However, the NR testability has been discussed in RAN4, and has been closely related to MU work. It included:
  MU characterization procedure for OTA test methodology
  MU factors definition and procedures required to minimize OTA MU
  Measurement grids (grid type, min. number of measurement points, applicability) as in R4-1801260

## Slide 3: Background
For E-UTRAN:
  Methods to derive Test Tolerances (TT) for RRM and UE radio reception conformance tests, and to establish a system for relating the TT to the MU of Test System are captured for E-UTRA respectively in TR36.903 and TR36.904
For NR
  TTs for both RRM and UE radio reception will be captured in TR38.903
  The Measurement Uncertainty budget for UE RF and RRM testing methodology are captured in TR38.810 and still under discussion
  MU will follow the one derived for OTA in E-UTRA.

## Slide 4: Background
For E-UTRA, and in R4-081664, TRP and TRS OTA performance requirements, measurement uncertainty and test tolerance values are agreed as a package.
However, the test tolerance values are not directly driven from Measurement Uncertainties: taking into account UE Manufacturers concerns on possible impacts on the conformance of the commercial UEs already in the market, a non zero test tolerance, which is not directly driven from Measurement Uncertainty, has been agreed as follows:
A shared risk principle has been applied, leading to a non-zero Test Tolerance

## Slide 5: Background
It is acknowledged that the accurate evaluations performed in RAN4 that led to the definition of the RF performance requirements already take into account the technology limits and some margin due to the implementation issues.
The performance under test is deemed critical (e.g. for regulatory aspects, like the spurious emissions)

## Slide 6: Background
For Operators the measurement uncertainty can introduce the risk of Passing UEs which harm the system performances
For UE manufactures the measurement uncertainty can introduce the risk of blocking a conformant UE
Co-signing operators believe the shared risk approach is not the best way forward, since this introduces a Test Tolerance that reduces the test requirements and significantly increases the risk to harm the system performance.

## Slide 7: New challenges
3GPP 5G candidate for inclusion in IMT-2020
  Need to meet all IMT2020 requirements and test environments: eg; Peak data rate, user experience data rate, latency, reliability
Minimum requirements have been defined to meet IMT2020 requirements
Currently test systems introduce Measurement Uncertainty, from which Test Tolerance are applied to the minimum requirements
  Will 3GPP 5G candidates still meet the IMT2020 requirements in reality if a non zero test tolerance is applied?
For these reasons it is proposed that only a minimal Test Tolerance should be introduced in 5G.

## Slide 8: Proposal
It is proposed not apply the shared risk principle
It is proposed to adopt a minimal Test Tolerance for the UE OTA performance testing in 5G

## Slide 9: References
3GPP TR 38.903: “NR; Derivation of test tolerances for Radio Resource Management (RRM) and User Equipment (UE) radio reception conformance tests".
3GPP TR 36.903: " Evolved Universal Terrestrial Radio Access (E-UTRA) and Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Derivation of test tolerances for Radio Resource Management (RRM) conformance tests".
3GPP TS 36.904: " Evolved Universal Terrestrial Radio Access (E-UTRA) and Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Derivation of test tolerances for User Equipment (UE) radio reception conformance tests".
ETSI ETR 273-1-2: "Improvement of radiated methods of measurement (using test sites) and evaluation of the corresponding measurement uncertainties; Part 1: Uncertainties in the measurement of mobile radio equipment characteristics; Sub-part 2: Examples and annexes".
3GPP TS 36.521-1: "User Equipment (UE) conformance specification, Radio transmission and reception Part 1: conformance testing".