## Slide 1: Motivation for EN-DC enhancements
RP-180457 (related to WID in RP-180456)
Ericsson

## Slide 2: background
During Rel-15, different architecture options are introduced
E-UTRA-NR Dual Connectivity (EN-DC), Option 3:
  Introduced to support fast introduction of NR both in the specifications and the products
In EN-DC, NR is working in a non-stand-alone way as an “extra” carrier to LTE
  Initial access, CP termination, QoS is managed by LTE eNB
  Mobility functionality is split between LTE and NR node
  NR user plane either via LTE eNB or directly to EPC
EN-DC is not necessarily temporal solution but stay over some time

## Slide 3: Fast setup of EN-DC
To get benefits of EN-DC, it is important to be able to setup EN-DC fast
  Otherwise there is risk that the UE has left already the system and NR resources are not utilized
Potential enhancements
  Support early measurement on NR
  Keep EN-DC configuration when UE is in the suspended state

## Slide 4: Control signalling robustness
EN-DC, split SRB was introduced.
  RRC messages can be sent via MeNB and/or SgNB
  This improves robustness in case of radio link problems in LTE/NR
Some simplifications were taken:
  If connection to Master cell group fails, the UE triggers RLF even the connection to the secondary cell group is fine
Intention is to enhance RRC diversity to achieve full benefits of the split SRB

## Slide 5: Network function virtualization
Different network deployments are possible for E-UTRAN (option 3) and NG-RAN depending on whether the control plane (gNB-CU-CP), the user plane (gNB-CU-UP), or both are centralized.
In centralized deployments it is possible to exploit network function virtualization to improve the overall network efficiency [1].
It is important to develop protocol means to allow optimizing signalling when logical network functions are deployed in centralized physical entities.
[1] TR 38.913, Study on scenarios and requirements for next generation access technologies