## Slide 1
Motivation for new WI proposal on Standalone eMTC and Other Enhancements in Rel-16
3GPP TSG RAN Meeting #79
Chennai, India, March 19 - 22, 2018
Nokia, Nokia Shanghai Bell
RP-180460

## Slide 2: Motivation
With the introduction of NR in Rel-15, eMTC is considered part of NR mMTC technology as all mMTC requirements can be satisfied by eMTC. As LTE spectrum is re-farmed for NR, eMTC may be co-deployed with NR to support mMTC services.
However, eMTC can only be deployed in in-band operation mode as part of a LTE carrier. Furthermore, eMTC operates on a narrowband concept, which may not use all available PRBs in different allowable bandwidths.
Therefore, it is desired to introduce stand-alone eMTC that can efficiently utilize all available PRBs and OFDM symbols within the carrier. Furthermore, NR coexistence study should be performed to ensure good coexistence and co-deployment with NR.
Further enhancements to improve spectral efficiency and power consumption are also desired in Rel-16.

## Slide 3: LTE Re-farming to NR
As LTE is re-farmed to NR, an eMTC carrier can be deployed together with NR to support mMTC services.
Legacy eMTC UEs can access the carrier in a backward compatible manner. However, they will not be able to utilize all OFDM symbols and PRBs.
  NOTE: Some PRB(s) outside of a narrowband may be allocated to Rel-15 eMTC UEs supporting flexible bandwidth allocation
Rel-16 and beyond eMTC UEs can use all OFDM symbols and PRBs.
Additional capacity for Rel-16 & beyond devices while maintaining backward compatibility for legacy devices.

## Slide 4: Stand-alone eMTC
Ability to use all OFDM symbols in a subframe [RAN1 lead, RAN2]
  Support using all OFDM symbols for MPDCCH and PDSCH.
More flexible resource allocation for different carrier [RAN1 lead, RAN2]
  Support for more flexible PDSCH/PUSCH resource allocation in the frequency domain to be able to utilize all resource blocks in the carrier.

## Slide 5: Coexistence with NR
Spectrum sharing between eMTC and NR [RAN4 lead]
  Study coexistence and co-deployment of eMTC and NR (e.g. interference, guard-bands, dynamic range).

## Slide 6: Further Improved Spectral Efficiency
CSI-RS support [RAN1 lead, RAN2]
  Study, and if found beneficial, specify support for CSI-RS.
Reduce DCI overhead [RAN1 lead, RAN2]
  Support for a single DL/UL DCI scheduling of multiple PDSCH/PUSCH transport blocks.

## Slide 7: Further Improved Power Consumption
Common System Information parameters for group of cells [RAN2 lead, RAN1]
  Study, and if found beneficial and feasible with a minimum of physical layer changes, specify support for common system information parameters (i.e., paging configuration, cell reselection configuration) for a group of cells.