## Slide 1: Way forward on LTE-NR uplink sharing from UE perspective
Huawei, HiSilicon, Telefonica, Orange, MediaTek
3GPP TSG-RAN WG4 RAN #79
Chennai, India, March 19-22, 2018
Agenda: 9.2.1
RP-180502

## Slide 2: Background
In WGs (working groups), there seems no clear understanding on whether FDM or TDM should be used for LTE and NR uplink transmissions on the shared carrier for uplink sharing from UE perspective.
To ensure the timely completion of the remaining work required for uplink sharing from UE perspective for R15, we would like to make the high level agreement in RAN to provide a clear guidance to WGs.
It is also shown in slides 4-6 that additional work required for UL sharing from UE perspective as compared to network perspective is very limited and manageable.

## Slide 3: Background
The benefits of TDM over FDM are given [1]:
  TDM approach has been considered so far as a solution for UL sharing from network or UE perspective. All agreements for TDM have been made in RAN1 and 2, and RAN4 work has been based on TDM so far, which means WGs already succeeded in striving to agree on the details of a solution by June 2018.
  FDM approach will require large amount of UE power backoff and significant amount of meeting time to work out the actual requirements. It also leads to more complexity for UE implementation such as UL power sharing between LTE and NR.
  Current RAN4 work is based on TDM.
Remaining work is to specify the requirements for each specific band combination, which were agreed as targets for Rel-15.
Any work on a FDM solution would delay the feature to Rel-16. There is the possibility to work on a FDM solution in Rel-16 if there is interest and if benefits are found compared to the TDM solution, while the TDM solution is the only solution that can reasonably be specified in Rel-15.
[1] Huawei, RP-180501, “Discussion on LTE-NR uplink sharing from UE perspective”, 3GPP TSG RAN meeting #79, Chennai, India, March 19-22, 2018.

## Slide 4: Background: RRM requirements and completion level
Impacted requirements |  | NSA from network perspective | NSA from UE perspective
Timing | Te/Tq/TA adjustment | completed | Completed(Same as network perspective)
 | TA_offset | Under discussion | Under discussion
UL carrier reconfiguration delay |  | completed | Completed(Same as network perspective)
Interruption at UL carrier RRC reconfiguration |  | completed | Completed (same as network perspective)

## Slide 5: Background: UE RF requirements and completion level (for at least one band combination)
Impacted requirements | UL sharing from network perspective | UL sharing from UE perspective
Configured transmit power | Basically completed. Will reuse general EN-DC transmit power related requirements | Basically completed(Same as network perspective for TDM operation)
ΔTIB / ΔRIB | Completed | Completed(Same as network perspective)
DESENSE due to IMD and harmonic | Completed | Completed(Same as network perspective)
LTE/NR time mask | N/A | Under discussion and will be used to capture the previous RAN4 agreement on LTE/NR switching time

## Slide 6: Background: BS RF requirements completion level (for at least one band combination)
Potentially impacted requirements | UL sharing from network perspective | UL sharing from UE perspective
All RX requirements | Under discussion. Huawei view is no additional requirements will be needed, assuming timing advance is used to ensure LTE UE and NR UE UL TX received approximately time aligned at the BS for the case of NR 15kHz SCS and 7.5kHz shift | Under discussion. With TDM approach, UE only transmits LTE or NR at one time. This means BS receiver sees no difference between network perspective and UE perspective. Therefore, the same requirements apply as for network perspective

## Slide 7: Way forward
UL sharing from UE perspective for SUL DC band combinations is supported in Rel-15 (complete at least one band combination by the end of R15) based on TDM between LTE UL and NR SUL