## Slide 1: Final report from email discussion on 5G Broadcast evolution
Convener (Lorenzo Casaccia, Qualcomm)
RP-180668
3GPP RAN #80
San Diego, CA, USA
11-14 June, 2018

## Slide 2: Recap from RAN #79: Nomenclature
Terrestrial Broadcast: notion of a downlink-only, ‘large area coverage up to nation-wide’ broadcast on dedicated spectrum, e.g. “TV-like” distribution of content
Mixed mode multicasting: notion of downlink multicast/broadcast with the potential to leverage downlink unicast and/or uplink unicast, with configurable/dynamic coverage ranging between a single cell to a large area, and multiplexed and possibly seamlessly switched with unicast traffic
Identification of basic principles

## Slide 3: Recap from RAN #79: Identification of technical attributes
Terrestrial Broadcast
Proposal to use LTE EnTV as a basis
Broadcast only
DL-only
Large & static transmission areas
  Nationwide to large number of cells
  Requires a standardized “coordinator” across cells
Enhancements (if any) needed to meet 5G requirements from TR 38.913, Clause 9.1
Additional requirements from TR 22.261 if needed
Mixed mode multicasting
“Equivalent” of MBMS into NR
Switched broadcast/unicast
Potentially mixed DL & UL
No “Downlink only”?
Moderate & dynamically configured transmission areas
  Few cells to one cell
Mixed mode should have high commonality with unicast
Common physical layer design (but flexible) to accommodate for different types of broadcast (e.g. from from single cell to moderately large area SFN transmission => there is some debate on this terminology)
Mixed mode multicasting should keep in mind use cases such as IOT and V2X

## Slide 4: Progress since RAN #79
Two drafts produced
  Draft Work Item on 5G Terrestrial Broadcast (RP-180672)
  Draft Study Item on NR mixed mode broadcast/multicast (RP-180669)

## Slide 5: Progress since RAN #79
Physical layer procedures and/or channels required to support broadcast/multicast [RAN1, RAN2]
  Solutions should keep commonality with unicast physical channels and signals, when possible.
  Solutions should be backwards-compatible with Rel-15 NR frame structure, and allow for efficient multiplexing with unicast traffic.
  Solutions should be optimized for non-EnTV use cases that require moderate transmission areas: one to a few cells.
  Strive for a single solution covering single and multiple cells. In case multiple broadcast techniques are found to be beneficial (e.g. single-cell and SFN), strive to keep a common physical layer design, when possible.
  [Support for a downlink-only mode of operation is subject to study]
Network architecture for broadcast/multicast [RAN3, RAN2], including
  Dynamically configured transmission areas, from a single cell to large areas.
  Dynamic switching between unicast, multicast and broadcast, including means for the network to determine when such switch may be beneficial.
  Study the benefits and feasibility of enabling idle mode reception of broadcast/multicast.
For the above items, a variety of use cases such as IOT, V2X, Public Safety, and live video services should be considered.
Support expressed on email by Telstra, UK Home Office, EU Broadcasters
NR Mixed Mode Multicast/Broadcast (NR track)

## Slide 6: Progress since RAN #79
For the broadcast requirements in TR 38.913, and taking as baseline Rel-14 LTE:
  Identify which of the broadcast requirements in TR 38.913 are relevant for dedicated terrestrial broadcast networks [RAN1, RAN2].
  Capture the analysis and potential solutions in a TR.
Study and specify necessary enhancements (if any) needed to meet the identified requirements [RAN1, RAN2].
  The work shall include but is not limited to studying/specifying the following, which will also be specified for non-dedicated networks:
    For support of large cell radius, evaluate new and existing numerologies for deployments with cell radius of up to 100km and introduce necessary improvements into the specification. [RAN1]
    Study and, if necessary, specify enhancements to support speeds of up to 250km/h [RAN4, RAN1].
Support expressed on email by Telstra, UK Home Office, EU Broadcasters
5G Terrestrial Broadcast (LTE track)