## Slide 1: Relationship between LTE V2X & NR V2X Qualcomm
3GPP RAN #80
June 11-14, 2018
San Diego, USA
RP-180678

## Slide 2: From LTE V2X to NR V2X
The question of the relationship between LTE V2X and NR V2X is often asked
These slides attempt to provide clarity on that respect
What is their relationship?

## Slide 3: From LTE V2X to NR V2X
Quote from the TR 38.913
“It is not intended for NR V2X to replace the services offered by LTE V2X. Instead, the NR V2X shall complement LTE V2X for advanced V2X services and support interworking with LTE V2X.”
We also note two different specifications exist for those two types of use cases
3GPP TR 22.885 => Safety V2X use cases
3GPP TR 22.886 => Advanced V2X use cases
Also mentioned by the convenor during the email discussion
  “Principle 1: Advanced V2X services (SA1’s 25 use cases categorised into four groups - Vehicle platooning, Extended sensors, Advanced driving, and Remote driving) are the focus of the Study Item. Technical requirements of these use cases would drive the technical study/design.”
  “Principle 2: TSG RAN already agreed NR-V2X does not replace LTE-V2X but complements it by providing tools to provide additional services not achievable by LTE-V2X. At least from 3GPP perspective, this implicitly means that the BASIC safety-related broadcast messages are transmitted/received only by LTE V2X.”

## Slide 4: How to realize “complementary”?
V2X application types (and applications) are identified by PSID / ITS-AID
  PSID (Provider Service Identifier, IEEE1609.3) ITS-AID (ITS- Application Identifier, ISO 17419-2)
SA2 and RAN2 are already discussing “PSID/ITS-AID based” carrier frequency & transport format support in Rel-15
  Transport format indicates whether, for a given application, Rel-14 or Rel-15 format/64 QAM should be used
    PSID and transport format/carrier frequency mapping is configured at V2X layer (above PDCP in the UE)
This mechanism based on PSID/ITS-AID & transport format/carrier frequency mapping can easily be extended for NR-V2X
This allows, for example, to configure all UEs that safety messages are to be routed on LTE-V2X and advanced use cases messages are to be routed on NR-V2X
APP Layer
V2X Layer
(service layer)
LTE AS
LTE V2X
NR V2X
Msg (PSID, PPPP, QoS class …)
NR AS
Safety msg
Advanced use cases

## Slide 5: What does this mean in terms of interoperability?
Future vehicles will be equipped with both LTE-V2X and NR-V2X
This way, new vehicles can “talk” to old vehicles.
New vehicles can also “talk” to each other and support the advanced use cases
  Obviously old vehicles will not be able to support new functions
From network point of view both LTE-PC5 and NR-PC5 can be scheduled by any NW (i.e. either LTE or NR NW) for Mode 3

## Slide 6: Conclusions
NR V2X and LTE V2X are to be complementary => no overlap in use cases
Signaling mechanisms to avoid overlap in uses cases are conceptually already discussed as part of Rel-15
Future ”NR V2X vehicles” will also be equipped with LTE V2X, which will ensure interoperability