## Slide 1: Motivation for new SI on NR coverage China Telecom
3GPP TSG RAN Meeting #80
La Jolla, USA, June 11-14, 2018
AI 9.1.14
RP-180751

## Slide 2: Motivation (1/2)
The coverage issue has attracted much interest in LTE phase
  In TR 36.824, the system bottleneck in terms of LTE coverage performance was identified, and corresponding coverage enhancements were adopted in Rel-12
  Then, the further coverage enhancements were developed during Rel-13 and Rel-14 work
In NR, continuous and ubiquitous coverage is required for some scenarios with higher carrier frequency than LTE [TR 38.913]
Due to the higher carrier frequency, operators may need to add more sites to ensure sufficiently good coverage comparable to LTE. Adding sites is costly and requires lengthy negotiations with building owners etc. Operators will face great challenges in ensuring sufficient coverage and cost effective deployments for NR.

## Slide 3: Motivation (2/2)
NR Rel-15 standardization will be finalized in June 2018, but the coverage performance of control and data channels, has not been well studied and addressed.
In the Study Item “Study on self-evaluation towards IMT-2020 submission”, performance evaluation of NR will be conducted, however
  Some assumptions associated with practical NR deployment, e.g., scenarios, carrier frequency and antenna configuration, are not fully taken into account
  The coverage of different channels may not be thoroughly evaluated

## Slide 4: Email discussion on NR coverage
As per the agreements in RAN #79, there was an email discussion on NR coverage before RAN #80. In the email discussion 25 companies including 10 operators shared their views and it was summarized that,
  Various scenarios, e.g., urban macro, rural/low mobility large cell, urban micro/dense urban, were proposed for NR coverage study.
  Candidate frequencies, e.g., 800MHz, 1.8GHz, and 3.5GHz for FR1; 30GHz and 40GHz for FR2, were proposed for NR coverage study.
  The majority of companies shared the views that all UL and DL channels should be taken into account.

## Slide 5: Preliminary coverage evaluation
Chart: Coverage Distance(m), 3.5GHz, Uma
| PUSCH 2Mbps | PUCCH format 1 | PRACH format B4 | PDSCH 50Mbps | Common PDCCH | PBCH
Coverage Distance(m) | 137 | 419 | 330 | 279 | 390 | 470
PUSCH seems to be the bottleneck of NR coverage, with large gap to other channels

## Slide 6: Discussion on potential enhancements
If PUSCH is identified as the bottleneck of NR coverage, potential candidate enhancements may include
  Enhanced slot bundling/repetition
    Time interleaving of bundled slots
  Enhanced frequency hopping
  Interference coordination/cancellation

## Slide 7: Proposal
Evaluate the coverage performance of Rel-15 NR for eMBB
  The target scenarios include urban macro, rural/low mobility large cell, and urban micro/dense urban
  The target frequency include: 800MHz, 1.8GHz, and 3.5GHz for FR1; 30GHz and 40GHz for FR2.
  Develop necessary simulation assumptions and performance metrics for coverage study
Identify the target channel(s) to be further enhanced based on the evaluation.
Identify the potential solutions and the specification impacts of each potential solution.
The study should take the output of other SI/WIs into account.

## Slide 8
Thanks！

## Slide 9: Evaluation assumptions
Channel Model | CDL_iii N_Los
Slot format | DDDSU
Carrier frequency | 3.5GHz
BandWidth | 20MHz
SCS | 30KHz
PRACH format B4 SCS | 30KHz
RB Number | 51
BS Antenna | 64T64R
UE Antenna | 2T4R
BS TX Power | 46dBm
UE Tx power | 23dBm
Noise figure | 3.5dB
Noise Spectrum Density | -174dBm/Hz
Penetration Loss | 20dB
Std of shadowing fading | 6dB