## Slide 1: Motivation for Integrated Access and Backhaul WI
RAN#80, LA JOLLA, USA, JUNE 11-14, 2018
AI 9.4.5
RP-180789
AT&T

## Slide 2: Key Objectives of IAB
Deploy small cells without fiber at every site (multi-hop)
No additional radio equipment (use of same hardware and spectrum)
Topology management and node integration
Fast route adaptation and route switching
Simple upgrade from IAB-node to wired donor
Urban Grid Deployment
Sites with fiber
Sites 1 hop away
Sites 2 hops away
Sites 3 hops away

## Slide 3: Key Requirement: Topology and Route Management
Donor node
Relay Node
Hop order 0
Hop order 1
Hop order 2
Hop order 3
A hierarchical topology for IAB has multiple advantages:
Greatly reduced specification impact since NR DL and UL physical channel design, signaling and procedures from Rel. 15 can be reused with minimal required enhancements
Architecture options which support multi-hop and multi-link connectivity between IAB-nodes enable dense deployments in a scalable manner while also remaining robust to short-term blocking events (especially when operating in mmWave spectrum)

## Slide 4: Key Requirement: Protocol Stack and RAN Architecture
    To a lower order a higher order node looks a like UE (MT)
    To a higher order a lower order node looks like a gNB-DU
    A multi-hop network can still preserve the Option 2 CU-DU RAN architecture split
CU
RRC
PDCP
RLC
MAC
PHY
Donor node
F1
Uu
UE
RLC
MAC
PHY
PDCP
RLC
MAC
PHY
RLC
MAC
PHY
Adaptation
Uu
RLC
MAC
PHY
RLC
MAC
PHY
Adaptation
Uu
IAB-node
IAB-node
UE
MT function
DU function
Adaptation layer above RLC
Supports ARQ and QoS
IAB nodes are essentially DUs
No modification to RLC protocol
Easy upgrade to fiber-fed DU
IAB architecture example with 2 hops

## Slide 5: Key Requirement: NSA Support
Early NR deployments will utilize NSA with LTE as the anchor for the UEs and IAB nodes:
Separate the control plane and data plane for the MT function of each DU
Control plane uses a single hop to LTE gNB
Data plane retains the multi-hop architecture
Topology and route management can happen over the control plane, basic functionality for mobile relays
CU
RRC
PDCP
RLC
MAC
PHY
Donor Node
F1
Uu
UE
RLC
MAC
PHY
PDCP
RLC
MAC
PHY
RLC
MAC
PHY
Adaptation
Uu
RLC
MAC
PHY
RLC
MAC
PHY
Adaptation
Uu
IAB Node
IAB Node
UE
LTE gNB stack
LTE UE stack
LTE UE stack
Uu
Uu

## Slide 6: Key Requirement: Half Duplex Requirement, Access/Backhaul Multiplexing
A fundamental assumption is that a given IAB relay node cannot transmit and receive at the same time
As a result, for efficient spectrum utilization and latency reduction, dynamic resource sharing (e.g. TDM/FDM/SDM) needs to be supported (subject to half-duplex constraints at the relay nodes)
  An IAB node is one of these modes (but not both) at a given time:
    Tx: Transmit DL to higher hop orders and UE, and transmit UL to lower hop orders
    Rx: Receive UL from higher hop order and UE and receive DL from lower hop orders
This also impacts the mechanisms for IAB node discovery/measurement, initial access, and link management

## Slide 7: Performance Evaluation of IAB
Understanding improvements in outage and user experienced data rate is critical in order to determine and plan the deployment of IAB
1 out of every 3 sites is fiber fed
1 out of every 7 sites is fiber fed
Site to site distance of 200m
For homogeneous scenario the donor sites and relay sites are deployed on a homogenous grid.
Only certain percentage of sites are fiber fed, e.g. 1 in 3 or 1 in 7
IAB Donor Node
IAB Relay Node

## Slide 8: Performance Evaluation of IAB
For Homogeneous and HetNet IAB scenarios, significant end user throughput is observed, despite half-duplex constraint at the IAB nodes and TDM of access and backhaul links

## Slide 9: Conclusions
IAB is a very robust and powerful concept that allows operators to deploy ultra dense network with 5G small cells
The WI should allow for the following features to be available from the first release of IAB:
    Scalable upgrade to multi-hop networks
    Automatic topology and route management built into the radio access protocol
    No need for additional radio equipment and spectrum (especially in mmWave)
    Has all the hooks to evolve to mobile relays in future releases
Initial evaluation of IAB using simulation and early trials shows promising results
A 1-year WI should be approved to start after the conclusion of the IAB SI in Dec. 2018