## Slide 1: Motivation for New WI RRC_INACTIVE enhancement

## Slide 2: Benefit of RRC_INACTIVE in NR
RRC_INACTIVE provides better power saving compared to RRC_CONNECTED
  Less update of [tracking area]
  In Rel-15, data transmission in RRC_INACTIVE is not supported, i.e., no monitoring of control channel for scheduling
RRC_INACTIVE allows light transition to RRC_CONNECTED compared to RRC_IDLE
  Reduced signaling overhead compared to transition from RRC_IDLE to RRC_CONNECTED

## Slide 3: Better use of RRC_INACTIVE in Rel-16
In NR, the UE is likely to stay in RRC_INACTIVE.
RRC_IDLE
RRC_CONNECTED
RRC_INACTIVE
No RRC Connection
No data transmission
Low power consumption
Small size & short time data transmission
Best-effort transmission
High data throughput
Large size & long time data transmission
Robust transmission

## Slide 4: Potential enhancement
Data transmission in RRC_INACTIVE (RAN2, RAN1)
  To avoid unnecessary transition from RRC_INACTIVE to RRC_CONNECTED
    Especially for small/short UL/DL data transmission
  Objectives include,
    Pre-allocation of UL resource for RRC_INACTIVE
    Contention-based UL transmission in RRC_INACTIVE
    RAN paging enhancement for DL data transfer in RRC_INACTIVE

## Slide 5: Potential enhancement
Fast go-to-sleep (RAN2)
  To achieve more power saving gain by minimizing the stay time in RRC_CONNECTED
  Objective includes,
    UE assisted RRC_INACTIVE transition at the end of data burst in RRC_CONNECTED