## Slide 1
Motivation for new SI on Network Assistance for Network Synchronization in NG-RAN
www.huawei.com
3GPP TSG RAN Meeting #80
La Jolla, USA, June 11-14, 2018
Agenda Item: 9.2.3
Huawei, HiSilicon
RP-181137
Notes: 讲解：
我希望向大家汇报三方面的情况。
行业趋势与华为战略
2013年经营业绩
未来（行业有希望，运营商选择我们，员工热情奋斗）

## Slide 2
Motivation
The study on Network Assistance for Network Synchronization (NANS) in LTE was completed and candidate solutions were captured in TR 36.898.
  Solution 1 is a network based solution reusing the existing signaling during handover based on a deployed frequency mechanism.
  Solution 2 is based on achieving synchronisation of neighbouring base stations by means of detecting reference signals transmitted over the air and detected via an UL receiver.
  Solution 3 focuses on enhancing RIBS by compensating the inter-cell propagation delay utilizing TA during mobility.
  Solution 4 focus on enhancing RIBS by compensating the inter-cell propagation delay based on exchange of location information over S1/X2/OAM to compensate line of sight propagation delay.
In Rel-16, 5G should see some benefits by extending the scope of NANS to NG-RAN (NR and E-UTRA).
  As discussed and agreed for IAB, time synchronization between IAB nodes is very essential. IAB may have additional requirement on network synchronization, which includes in-band wireless backhaul and multi-hops backhauling.
  And since currently there is no RIBS support for NR, the solution 2, 3, & 4 evaluated in SI should not be applicable for NR. Further enhancements need to be considered.

## Slide 3
Proposed Objectives
The objectives of this extended SI is to study further the feasible network based solutions to achieve network synchronization in NG-RAN.
  Consider the TR 36.898 as starting point for E-UTRA with also now some consideration on TDD.
  Study the possible radio network based methods to provide a low cost way for the operators to synchronize their NR (e.g. IAB) networks where the current synchronization mechanism(s) does not apply.
  Avoid duplication of functionalities with respect to specified functions, in order to maintain costs and complexity to the minimum.
  Solutions providing a synchronisation accuracy comparable with existing solutions and meeting current requirements should be taken into account.

## Slide 4
Copyright©2015 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !