## Slide 1
Title: Motivation for New Work Item for MR-DC Enhancements
RP-181159
Document for: Discussion
Agenda Item: 9.2.2
3GPP TSG RAN Meeting #80 RP-180xxx
La Jolla, CA, USA, 11 - 14 June 2018

## Slide 2: Learnings from Rel-15 LTE euCA WI
In Rel-15, there is an on-going the RAN2-led LTE WI on Enhancing CA Utilization [RP-170805]
  The main goal of this WI is to improve latency of SCell set-up times for all scenarios (IDLECONNECTED transition for first time CA setup and Scell addition in CONNECTED)
  Reducing SCell setup delay (including detection, measurement, configuration and activation) shows improved UE throughput and lower UE power consumption (due to shorter active time)
  LTE: Up to 5x throughput when the delay is reduced from 500 ms to 100 ms or below
  LTE: Substantial (e.g. up to 6-7 minutes) of extra small cell measurements (per call) – before break-even point in energy consumption

## Slide 3: Speed up transition to MR-DC and CA
Connections are many times short, meaning that UE goes to IDLE before DC or CA is setup
The lower the latency and the higher the throughput, the shorter the call, leading to net positive effect in UE power consumption, better resource utilization over shorter time and improved user experience
Measurement availability will be critical in fast cell utilization
  E.g. Use of CA is limited by the delays in starting to use SCell(s)

## Slide 4
Evaluation of LTE vs. NR: UE throughput impact of fast cell access in NR
LTE
LTE Scenario (10MHz + 10MHz)
NR Scenario (10MHz + 40MHz)
5G
NR: Gain between 5x-10x gains in mean user throughput
LTE: Gain between 1.4x – 5x gains in mean user throughput
  In NR, the performance impact of faster cell access may be even larger than in LTE due to the larger system bandwidth and throughput difference between the macro cell and the small cell.

## Slide 5
Summary of benefits of fast MR-DC and CA setup
Summary of benefits of fast cell access :
More efficient cell usage (more data scheduled via all cells)
Enabling faster CA/DC/EN-DC configurations and activations
Faster data offloading (e.g. from PCell to other Cell(s))
Better resource utilization in the (e.g. CA/DC/EN-DC) network
Improved user throughput
Enhanced capacity (especially when PCell capacity is limiting and wide bandwidth is available e.g. for SCell)
Fast cell access enhancements are beneficial for several
scenarios, e.g. CA, LAA, LTE DC, MR-DC (any option X)

## Slide 6: Avoiding RLF in MR-DC
In EN-DC, split SRB was introduced to provide additional robustness and diversity
Secondary link can be utilized when the master link fails
Goal of enhancement is to avoid RLF when split SRB is setup while operating under MR-DC. Also CA scenario can be considered.

## Slide 7: Summary: Rel-16 MR-DC Enhancement WID goals
Proposal: RAN to approve a RAN2-led Rel-16 WI with goal to improve the MR-DC and CA utilization and robustness for NR
  RAN2 procedures to enable Fast MR-DC utilization, including measurement reporting, cell configuration and access/re-establishment procedures
  RAN4 requirements for setup latency and measurement performance with acceptable UE power consumption impacts
Key goals
    Measurement reporting: Early and fast reporting of measurements information availability from neighbor cells to reduce delay setting up MR-DC and/or CA.
    Efficient and low latency serving cell configuration/activation/setup: Minimizing signalling overhead and latency needed for initial cell setup, additional cell setup and additional cell activation for data transmission.
    Fast recovery: Support fast recovery of MCG link e.g. by utilizing the SCG link and split SRBs while operating under MR-DC.