## Slide 1: Motivations on NR DL 256QAM support for FR2
China Telecom
3GPP TSG RAN Meeting #81 RP-181616
Queensland, Australia, Sept 10-14, 2018 (revision of RP-)
Agenda: 9.1.4

## Slide 2: Background
The DL 256QAM support for FR2 has been discussed intensely for several meetings in Rel-15 in RAN4.
In the latest RAN4 meeting, companies made a conclusion for the DL 256QAM feature in Rel-15 and also agreed to further study or define the UE and BS requirements in Rel-16. The agreements are as bellow.
  Define the 256QAM feature as optional feature in Rel-15
  No BS and UE requirement will be defined in Rel-15
  RAN4 recommend RAN plenary to consider to approve the SI/WI to study/define the UE and BS requirements in Rel-16
  It is up to RAN plenary to decide the approval of SI/WI proposal.

## Slide 3: Motivation: Scenario
High receiving SINR can be achieved under the distinctive channel conditions with almost stationary or limited mobility UE. These scenarios include
  Homes
  Roof-above or indoor
  Commercial centre or official building
  Backhaul from macro base station to lamp site or CPE
    Especially, the path loss in the backhaul scenario is almost with LOS and stationary channel condition. High receiving SINR can be guaranteed by adjusting the beam direction point at each other from point to point.
DL 256QAM can be applied and benefit for the networks in some specific scenarios with distinctive channel condition.

## Slide 4: Motivation: Feasibility
Many simulations results for EVM performance for DL 256QAM were contributed by companies in Rel-15
  Different simulation results with positive or negative views were proposed in the contributions [1-4]
  Contributions [1] and [2] showed when SNR>~25dB, the 256QAM will achieve gain by comparing to 64QAM.
It can be observed that under specific assumptions or scenarios, DL 256QAM can provide the improvement by comparing to 64QAM
[1] R4-1807874, “Link level simulation results for BS EVM requirements evaluation for 256QAM in FR2”, Nokia, Nokia Shanghai Bell
[2] R4-1807520, “256QAM support for FR2”, Huawei, HiSilicon
[3] R4-1806715, “On 256QAM for FR2”, CATT
[4] R4-1806296, “Views on 256QAM support for NR FR2”, Intel Corporation
[5] R4-1804987, “On EVM Requirement for FR2”, Ericsson

## Slide 5: Objective
Given much studies have been made in Rel-15, it is proposed to consider the WI in Rel-16, meanwhile capture a summarization for the study of Rel-15 in the WI. The objectives include
  Core part
    Summarize the feasibility and performance benefit study for FR2 DL 256QAM supporting in Rel-15 NR.
    Define the UE capability for supporting DL 256QAM
    Define the specific core requirements for BS and UE
      The requirements for BS include but are not limited to associated regulatory requirements on Tx modulation quality, Tx power dynamic range etc.
      The requirements for UE include but are not limited to associated regulatory requirements on Rx maximum input power level, FRC etc.
  Performance part
    Specify the necessary UE and BS performance requirements for NR DL 256QAM in FR2 including.
      Demodulation performance requirements
      CQI requirements