## Slide 1: Motivation for introducing early HARQ feedback for UL data in Rel-16 NB-IoT
3GPP TSG RAN Meeting #81
Gold Coast, AU, Sep 10 - 13, 2018
Agenda Item: 10.7.2
RP-181635
Sequans

## Slide 2: Early HARQ feedback for UL data
Early HARQ feedback for UL data was introduced in the Rel-15 WI for Even Further Enhanced MTC for LTE
To allow eNB to indicate to a UE that UL data has been successfully received and may enable early termination of uplink transmission (and downlink monitoring).
Early termination of downlink monitoring was introduced only for FD-FDD or TDD but not for HD-FDD
for HD-FDD, reusing the same solution that was specified for FDD would have required increasing the Uplink Compensation Gap (UCG)
  Discussions on alternative solutions for HD-FDD were postponed due to lack of time
overview

## Slide 3: Early HARQ feedback for UL data
Similar to eMTC HD-FDD the main challenge is to signal an early HARQ feedback without increasing the Uplink Compensation Gap (UCG)
As a workaround, eNB may aim at a higher BLER and under allocate UL repetitions. Then, if necessary allocate another set of repetitions (DCI with NDI=0)
  Such approach was proposed by QC in R1-1708797 [1]
However, with such approach, the UE would be required to acquire additional DCI messages, Thus the power consumption is not yet optimized.
For NB-IoT

## Slide 4: Early Transmission Termination Signal (ETTS)
As demonstrated and analyzed in [2], [3], using ETTS, the UE can simultaneously synchronize and acquire HARQ feedback well within the 40ms UCG
  moreover, the UCG duration can be actually reduced.
In compare to an eNB implementation that aims to achieve a traditional 10% BLER, the proposed ETTS solution can gain up to 45% decrease in power consumption.
In compare to the workaround proposed by QC in R1-1708797 [1], the proposed ETTS can gain up to 28% decrease in power consumption.
To avoid standard complexity, a known signal e.g. WUS like signal can be used as ETTS.
For NB-IoT
Time-sequence diagram of UL transmissions with ETTS

## Slide 5: Proposal
Include the introduction of Early HARQ feedback for UL data in the objectives of the Rel-16 WI for Additional enhancements for NB-IoT (NB_IOTenh3)
Similar enhancement can be considered for HD-FDD eMTC, if time allows
References:
[1] R1-1708797 “Uplink HARQ-ACK feedback”; Qualcomm Incorporated
[2] R1- 1808921 “Early UL Transmission for NB-IoT and HD-FDD eMTC” ; Sequans Communications
[3] RP-181771 “Early UL Transmission Termination Analysis”; Sequans Communications