## Slide 1: Generalizing 2-step RACH LG Electronics

## Slide 2: Discussion in RAN
RAN#80 has discussed 2-step RACH feature in the context of URLLC, NR-U, and NOMA.
However, due to the complexity in RAN1 aspects, and no clear use case was identified, RAN#80 removed 2-step RACH from the objectives of the SIDs.
  Only NR-U SID vaguely describes support for 2-step RACH.

## Slide 3: Discussion in RAN2
Though not explicitly stated in SID (RP-181339), RAN2 has focused on RACH enhancement in NR-U SI.
  Enhancement of 4-step RACH
  Introduction of 2-step RACH
Some companies felt that 2-step RACH should not be limited to NR-U but should be applicable to other use cases, e.g. NOMA, URLLC, for efficient use of RAN2 resource.
RAN2 also agreed that all legacy RACH triggers could be applicable to 2-step RACH.
  Access to CONNECTED, handover, data arrival, SI request, BFR, etc.

## Slide 4: Proposal for 2-step RACH
Deprioritize 2-step RACH in NR-U study item, because;
  SID does not have clear objectives on 2-step RACH
  No clear use case has been identified
  Benefits of 2-step RACH has not been justified
If RAN allows to study 2-step RACH in NR-U;
  MAC procedure should not be designed specific to NR-U use case but should be generalized to be applicable to other use cases;
    However, PHY procedure may be designed specific to NR-U considering the workload in RAN1