## Slide 1: Motivation for efficient QoS handling for IABs
RP-181734
RAN#81, Gold Coast, Australia
10-14 September, 2018
Telstra
RP-181734

## Slide 2
Current LTE relay solutions are unsuitable for high traffic use cases
  Donor eNode-B sees the relay and its traffic as a single UE
  Suitable for coverage use cases, but not capacity
An IAB must efficiently handle high traffic scenarios
  With very wide bandwidths, mmWave is suited to solving capacity problems
  IABs need to maximise traffic carrying capability to be suitable for expected deployment scenarios
RP-181734

## Slide 3: Oversimplified worked example
eNodeB
LTE Relay
Link
Service
Voice: 12RBs
Data: 60RBs
Voice: 6RBs
Data: 20RBs
Voice: 6RBs
Voice: 6RBs
Data: 20RBs
Voice: 6RBs
Data: 20RBs
Voice: 6RBs
Data: 20RBs
Data: 20RBs
UE
Voice: 6RBs
Data: 20RBs
gNodeB
IAB
Link
Service
Voice: 6RBs
Data: 20RBs
Voice: 6RBs
Voice: 12RBs
Data: 60RBs
Voice: 12RBs
Data: 60RBs
Voice: 6RBs
Data: 20RBs
Data: 20RBs
MT
The donor eNodeB is unable to see UEs on service side
LTE relay looks like another UE and so receives the same resources in total as any another UE directly connected to the donor
The donor gNodeB should be aware of UEs on the service side
This would enable the IAB-Node MT function to be provided with sufficient resources to meet its serving UE and downstream MT function demands
RP-181734
NB: resource numbers simplified for illustrative purposes

## Slide 4: IAB architecture must efficiently support high traffic cases
Desired outcome
  The final IAB architecture (TR38.874) must support both high traffic as well as coverage extension use cases
Observations
  In-market LTE relays are unsuitable for high traffic as the donor eNB sees the relay as a single UE and is unable to see per-bearer QoS attributes
  Overdimensioning is a very inefficient means to fulfil QoS obligations
  Providing the IAB gNB donor with full visibility of per-bearer QoS attributes will yield a more efficient outcome
Proposal
  The final selected IAB architecture must efficiently support high traffic use cases by ensuring the gNB donor has full visibility of per-bearer QoS attributes for all UEs under the service of an IAB
RP-181734