## Slide 1
Introduction of B1C signal
in BeiDou System
China Academy of Information and Communications Technology(CAICT), China
September, 2018

## Slide 2
The standardization work of B1I signal of BeiDou Navigation Satellite System (BDS) in 3GPP started from 2014. Till 2015, the related progresses can be separated into three categories which includes technical standards, functional and performance standards and test standards as follows：
Background
Technical standards
3GPP TS 25.331 -- Radio Resource Control (RRC) Protocol specification
3GPP TS 25.413—UTRAN Iu interface Radio Access Network Application Part (RANAP) signalling
3GPP TS 25.172 -- Requirements for support of Assisted Galileo and Additional Navigation Satellite Systems (A-GANSS) Frequency Division Duplex (FDD)
3GPP TS 25.173 -- Requirements for support of Assisted Galileo and Additional Navigation Satellite Systems (A-GANSS) Time Division Duplex (TDD)
Test standards
3GPP TS 37.571-1 -- Universal Terrestrial Radio Access (UTRA) and Evolved UTRA (E-UTRA) and Evolved Packet Core (EPC); User Equipment (UE) conformance specification for UE positioning; Part 1: Conformance test specification
3GPP TS 37.571-2 -- Universal Terrestrial Radio Access (UTRA) and Evolved UTRA (E-UTRA) and Evolved Packet Core (EPC); User Equipment (UE) conformance specification for UE positioning; Part 2: Protocol conformance
3GPP TS 25.305 -- Stage 2 functional specification of User Equipment (UE) positioning in UTRAN
3GPP TS 36.171 -- Evolved Universal Terrestrial Radio Access (E-UTRA); Requirements for Support of Assisted Global Navigation Satellite System (A-GNSS)
3GPP TS 43.059 -- Functional stage 2 description of Location Services (LCS) in GERAN
3GPP TS 45.005 -- GSM/EDGE Radio transmission and reception
3GPP TS 37.571-3 -- Universal Terrestrial Radio Access (UTRA) and Evolved UTRA (E-UTRA) and Evolved Packet Core (EPC); User Equipment (UE) conformance specification for UE positioning; Part 3: Implementation Conformance Statement (ICS)
3GPP TS 37.571-4 -- Universal Terrestrial Radio Access (UTRA) and Evolved UTRA (E-UTRA) and Evolved Packet Core (EPC); User Equipment (UE) conformance specification for UE positioning; Part 4: Test suites
3GPP TS 37.571-5 -- Universal Terrestrial Radio Access (UTRA) and Evolved UTRA (E-UTRA) and Evolved Packet Core (EPC); User Equipment (UE) conformance specification for UE positioning; Part 5: Test scenarios and assistance data
3GPP TS 51.010-7 -- Mobile Station (MS) conformance specification; Part 7: Location Services (LCS) test scenarios and assistance data
3GPP TS 25.423 -- UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling
3GPP TS 25.433 -- UTRAN Iub interface Node B Application Part (NBAP) signalling
3GPP TS 25.453 -- UTRAN Iupc interface Positioning Calculation Application Part (PCAP) signalling
3GPP TS 36.305 -- functional specification of User Equipment (UE) positioning in E-UTRAN
3GPP TS 36.355 -- LTE Positioning Protocol (LPP)
3GPP TS 44.031 -- Mobile Station (MS) - Serving Mobile Location Centre (SMLC) Radio Resource LCS Protocol (RRLP)
3GPP TS 44.071 -- Mobile radio interface layer 3 LCS specification
3GPP TS 48.031 -- Location Services (LCS) Serving Mobile Location Centre - Serving Mobile Location Centre (SMLC - SMLC) SMLCPP specification
3GPP TS 49.031 -- Location Services (LCS) Base Station System Application Part LCS Extension (BSSAP-LE)
Functional and performance standards
3GPP TS 25.306 -- UE Radio Access capabilities
Notes: 3GPP图标，之前的标准首页

## Slide 3
Background
In 2017, China Satellite Navigation Office published “Beidou Navigation Satellite System Signal in Space Interface Control Document—Open Service Signal B1C (Version 1.0)”.
This document defined the characteristics of the open service signal B1C transmitted from the BDS space segment to the BDS user segment.
Reference : China Satellite Navigation Office, “Beidou Navigation Satellite System Signal in Space Interface Control Document—Open Service Signal B1C (Version 1.0)”, www.beidou.gov.cn/xt/gfxz/201712/P020171226741342013031.pdf , Dec. 2017.

## Slide 4
The main reasons that B1C signal is suggested in BDS 3GPP are:
（1）B1C signal will be the main core signal of BDS. The third generation of BDS “BDS-3”will use B1C signal to provide global navigation services.
（2）B1C signal uses same frequency as GPS L1，which satisfies the “civil signal compatibility and interoperability ” requirements of satellite navigation systems.
（3）The double channel of B1I+B1C, the TTFF（Time TO First Fix）of BDS will be shorten.
Motivation

## Slide 5
Difference between B1I and B1C
Signal Type | Constellat-ion | Carrier Frequency | Modulati-on Mode | Received Power Level | NAV Message
B1I | MEO/IGSO satellite: D1; GEO satellite: D2 | 1561.098MHz | QPSK | -163dBW（with 0 dBi RHCP receiving antenna ） | NAV messages are formatted in D1 and D2 with rates 50bps and 500bps respectively
B1C | MEO/IGSO satellite | 1575.42MHz | BOC | MEO: -159dBW IGSO: -161dBW （with 0 dBi RHCP receiving antenna ） | NAV messages are formatted in B-CNAV1，1800 symbols per frame，symbol rate is 100sps，repeated every 18 seconds

## Slide 6
Proposals
Proposal 1: Using B1C signal in 3GPP-R16. B1C should be involved in both 4G and 5G.
Proposal 2: Still retain the B1I signal, and analyze the impact of B1C in RAN2.
Proposal 3: Under the suggestions of the meeting, determine which 3GPP item the B1C should be contained.

## Slide 7
THANK YOU