## Slide 1: Highlights on NR UE feature list
Ericsson
RP-181875
Ag. 9.6

## Slide 2: 2-20 beam correspondence
Motivation
  Exploiting beam correspondence allows measurement and reporting from DL beam management procedures to support UL beamforming
    Avoids excessive air interface load from UL beam management procedures based on SRS beam sweeping (per UE)
    Simplifies network operation
  All UEs must be capable of a certain degree of beam correspondence to be able to access the network
    Transmit PRACH/MSG3 in the same direction as the detected SS/PBCH block
  Additional UL beam management procedures (SRS beam sweep) to support high gain (narrow) UL beamforming is an optimization
Proposal:
  Mandatory without capability signaling for FR2

## Slide 3: 2-32 / 2-35 basic csi feedback
Motivation
  UE complexity driven by the number of simultaneously calculated CSI reports, not the number of configured ones
    Beam management reports consumes CSI-ReportSettings. Typical configuration in FR2 require one Report Setting for CSI, one for P2 beam report and one for P3 beam sweep 3 CSI report settings needed, at least for the aperiodic case
    CSI on PUSCH is one of most coverage-limited channels. Beneficial to dynamically optimize CSI accuracy vs UCI overhead tradeoff by configuring different CSI Reporting Settings (WB/SB CQI/PMI, Type I/Type II/non-PMI CSI) Maximum number of 4 CSI Report Settings per time-domain behavior likely too small
  For FR1, even when reciprocity-based operation is used, Type I CSI feedback capturing all antenna ports of the array is needed for fallback to ensure good performance also on cell edge 32 Tx Type I CSI codebook should be mandatory
Proposals
  2-32:
    32 Tx Type I codebook is mandatory for FR1
  2-35:
    3 configured CSI reporting settings is mandatory, at least for aperiodic time-domain behavior
    Increase the maximum number of configured CSI Report Settings to 8

## Slide 4: 2-33 CSI-RS capability
Motivation
  UE complexity driven by the number simultaneously active CSI-RS resources/ports, not the number of configured ones
    Introduction of Components 4 & 5 (simultaneous resources/ports) supersedes the need to limit configured CSI-RS resources/ports
    Restricting the number of configured CSI-RS resources can severely impact network performance and gNB flexibility
    CSI-RS resources are configured per BWP, too low capability necessitates RRC reconfiguration upon BWP switch
Proposals
  2-33:
    Component 1:16 configured CSI-RS resources is the smallest possible value
    Component 2: Remove component on maximum number of configured ports, this impacts neither complexity nor memory
    Component 3: 4 configured CSI-IM resources is the smallest possible value
    Component 5: 32 simultaneous NZP CSI-RS ports is the smallest possible value for FR1, 8 is smallest value for FR2

## Slide 5: 2-51 TRS
Motivation
  For FR2, up to 64 SSBs, corresponding to different beams, can be configured in a cell. Each beam should be associated to a TRS for tracking in a corresponding configured TCI state
    Otherwise, RRC reconfiguration is needed even when the UE moves within the cell!
    It is already mandatory for the UE to support 64 configured TCI states
  The number of “active” TRSs a UE can simultaneously track is reported as separate capability in Component 3.
  Note that one TRS is configured using 2 or 4 CSI-RS resources. The maximum number of CSI-RS resources that can be configured also provides an upper bound on the maximum number of TRSs
Proposals
  2-51:
    Component 4: 64 configured TRS per CC is the smallest possible value
    Component 5: 64 configured TRS across CCs is the smallest possible value

## Slide 6: 2-55 srs tx switch
Motivation
  The FG name for 2-55, “SRS Tx switching”, is misleading, since it controls the configuration of SRS transmission for DL CSI Acquisition purpose, with or without actual antenna switching
    A UE can report support of Tx antenna switching (1T2R, 2T4R, 1T4R) or support of only SRS transmission without switching (T = R)
    A UE supporting ‘T=R’ should be capable of sounding on a fixed set of antennas according to its reported capability in FG 2-53
  Reciprocity-based DL beamforming is central to NR design
    Support of SRS transmission, without antenna switching, for DL CSI acquisition purpose crucial for NW performance
    Support of basic antenna switching (1T2R) will give a significant capacity boost and enable multi-layer transmission also in reciprocity-based operation
Proposal:
  2-55 is Mandatory with UE capability signaling for FR1
    Rename the FG to “SRS transmission for DL CSI acquisition”
    Mandatory with capability signaling to support ‘1T2R’ and ‘T = R’
    Clarify that ‘T=R’ implies sounding using the maximum number of ports/resource a UE supports (which may be a subset of Rx antennas)