## Slide 1: Power limits for EN-DC
Source: Ericsson
Agenda item: 9.2.1
Document for: Discussion
3GPP TSG-RAN Meeting #81 RP-181919
Gold Coast, Australia, 10 – 14 September 2018

## Slide 2: Specification of Pcmax
In this contribution we consider power limits for inter-band EN-DC
Specification in 38.101-3 of the configured maximum transmission power (“Pcmax”) for inter-band EN-DC operation
  Maximum UE power when UE transmission(s) of the MCG overlap in time with transmission(s) of the SCG
  Defines when scaling/dropping of the NR transmission is allowed for UEs supporting dynamic power sharing (38.213), type 1
  Defines the limit above which UEs not supporting dynamic power sharing can expect single TX transmissions (38.213), type 2
Specification in 38.101-3 of requirements on the measured maximum transmission power
Replace the agreed CR (R4-1811484)

## Slide 3: The for inter-band EN-DC
Determines if scaling/dropping of the NR transmission is allowed (type 1)
as defined in 38.213 is the linear value of a configured maximum transmission power for EN-DC operation (level to be specified in 38.101-3)
Power back-off for CGs independent for inter-band EN-DC
Should be a fixed threshold for inter-band since the LTE power cannot be increased even if the NR would be dropped (for back-off is independent)
Depends only on the EN-DC power class and P-Max (if present)
  Scaling/dropping of NR transmission allowed only if the total UE power exceeds this threshold

## Slide 4: Problem with the agreed CR for inter-band EN-DC
The can be configured in a range (the agreed CR in R4-1811484)
  Scaling/dropping of NR is allowed down to a lower limit determined by the minimum required maximum power on each CG
Scaling/dropping allowed at a total power lower than the EN-DC power class also for UEs exceeding minimum requirement on maximum power

## Slide 5: Maximum power on the two CGs (Pcmax,c)
The configured maximum power Pcmax,c on each CG is specified as a range unlike the specification of
  The (computed) configured power for LTE (MCG) is modified with PLTE but is otherwise unchanged (lower and upper limits)
  The (computed) configured power for NR (SCG) is modified with PNR but is otherwise unchanged

## Slide 6: The measured total EN-DC power
Specification of requirements on the configured power measured at the antenna port (denoted Pumax in RAN4 specifications)
Specified with a tolerance of the total power including possible NR scaling/ dropping when measured
  The scaling does not affect the computed values (Pcmax,c and PHR)
This measurement also verifies the EN-DC power class
Tolerances depend on the ranges defined for the configured power on the two CGs
Distinguish between two cases for total power (use the PLTE and the PNR)
  Measurement when scaling shall not occur, two CGs/signals always present
  Measurement when scaling may occur, possibly only one CG/signal present if the NR transmission is dropped

## Slide 7: Measurement when scaling does not occur
Set PLTE and the PNR such that (below scaling threshold)
Upper and lower limits of measured power (including tolerance) determined by both CGs
Lower and upper limits are sums of the powers of the two CG since scaling does not occur

## Slide 8: Measurements when scaling may occur
Set PLTE and the PNR such that (above scaling threshold)
Lower limit of measured power (including tolerance) determined by MCG since the SCG may be dropped
The upper limit determined by the sum but in most cases limited by the EN-DC power class (the sum if allowed A-MPRs on both CG are very large, then no scaling)
Wider tolerance range than the case in which scaling is not allowed

## Slide 9: Scaling/dropping of the NR CG
RAN1 agreement (AH 1801):
  when dynamic power sharing is used, if total power for LTE and NR in FR1 exceeds X_total [ ], UE reduces NR transmission power or drops NR transmission so that total power does not exceed X_total
The 38.213 says that ”the UE reduces [NR] transmission power” but the terms “reduces” and “drops” have the same implication/meaning
Verification of the total UE power in RAN4 specifications
  Verification of scaling (reduction) or dropping would require a separate power measurement on the NR CG, but would not be aligned with RAN1 agreement

## Slide 10: Conformance tests (RAN5)
The two cases (with and without scaling) allow RAN5 reuse the current test method with continuos ”UP” commands on both CG until power saturates
If scaling does not occur (not power limited) then both CGs will increase monotonously, tolerance can be verified
If scaling can occur the NR might increase intially and then decrease even if UP commands sent on the NR CG

## Slide 11: Conclusion
Specify the configured (total) UE maximum transmission power as a threshold rather than in terms of a range that allows scaling/dropping at a total power level significantly lower than the EN-DC power class
The measured total power is verified in 38.101-3, the tolerances depend on the allowed power ranges of the CGs
  Verification of scaling (reduction) or dropping would require a separate power measurement on the NR CG, but would not be aligned with RAN1 agreement
Proposed changes to 38.101-3 in RP-181918 (replacing the agreed R4-1811484)