## Slide 1
3GPP TSG RAN meeting #81 RP-181984
Gold Coast, Australia, September 10 – 13, 2018
Agenda Item: 9.3.16
Source: ZTE
Title: Considerations on NR SI for beyond 52.6 GHz
Document for Discussion

## Slide 2: Introduction
In RAN#80, A new SI, Study on NR beyond 52.6 GHz (800090, FS_NR_beyond_52GHz) has been approved in RP-181435
Based on its SID, objectives including:
  Available Spectrum
  regulatory requirements
In the contribution, ITU-R spectrum allocation and some survey of regulatory requirements in China are shared, and two proposals are given for skeleton.

## Slide 3: ITU-R
WRC-19 1.13 Items[1] (for high frequency bands of IMT-2020)
  ITU-R will conduct and complete in time for WRC-19 the appropriate studies to determine the spectrum needs for the terrestrial component of IMT in the frequency range between 24.25 GHz and 86 GHz, taking into account
  In 2016, ITU-R SG5 built Task Group 5/1 (TG5/1) to be responsible for the development of spectrum conditions of candidate bands.
Candidate frequency bands | candidate frequency bands of requirement additional conditions
24.25-27.5 GHz | 31.8-33.4 GHz,
37-40.5 GHz | 40.5-42.5 GHz
42.5-43.5 GHz | 47-47.2 GHz
45.5-47 GHz | 
47.2-50.2 GHz | 
50.4-52.6 GHz | 
66-76 GHz | 
81-86 GHz | 
[1] RESOLUTION 238 (WRC-15),Studies on frequency-related matters for International Mobile Telecommunications identification including possible additional allocations to the mobile services on a primary basis in portion(s) of the frequency range between 24.25 and 86 GHz for the future development of International Mobile Telecommunications for 2020 and beyond

## Slide 4: Survey of regulatory requirements in China
low transmission power and short distant unlicensed applications
  Frequency range: 59-64 GHz
  Specific requirements can be referenced from 38.805
Vehicle Radar ranging application since 2005 [1]
  Frequency range: 76-77GHz
  Peak EIRP: 55dBm
Amateur Radio [2]
  Frequency range: 75.5-76GHz, 76-81GHz:
[1]《关于发布〈微功率(短距离)无线电设备的技术要求〉的通知》(信部无〔2005〕423号)
423# notification on technical requirements of low transmission power (short distant) in 2005
[2] (82)无发文53号：关于颁发《业余无线电管理暂行规定》的通知
53# issue on temporary provisions of amateur radio management

## Slide 5: China
Frequency Allocations in Radio Regulations from 52.6GHz to 100GHz
Service | The Frequency Band (GHz)
MOBILE | 59.3-64, 65-66, 66-71, 71-74, 74-76 81-84, 84-86, 92-94, 94.1-95, 95-100
FIXED | 59.3-64, 64-65, 65-66, 71-74, 74-76 81-84, 84-86, 92-94, 94.1-95, 95-100
Broadcast | 74-76
RADIOLOCATION | 59.3-64, 66-71, 76-77.5, 77.5-78, 78-79, 79-81, 92-94, 94-94.1, 94.1-95, 95-100
Other services including SPACE RESEARCH, RADIONAVIGATION, SATELLITE related services, Amateur, RADIO ASTRONOMY | 
China current allotment
ITU-R WRC-19 1.13

## Slide 6: Proposal
Proposal 1, In the related spectrum’s chapter, ITU-R TG5/1 defined some methods to satisfy WRC-19 Agenda Item 1.13 in each of the frequency bands referred to in Resolution 238 (WRC-15) and a range of conditions for protection measures for different services, as well as regulatory and procedural considerations in CPM, both 66-76 GHz and 81-86 GHz should be considered or referenced in the report.
Proposal 2, In the related spectrum’s chapter, Regulatory requirements in some specific countries, such as China, EU, US and so on, can be reflected.

## Slide 7: Thank you