## Slide 1
Status Report of RAN WG2 to TSG-RAN #82
3GPP TSG RAN#82 Sorrento, Italy, December 2018
RAN2 Chair: Richard Burbidge (Intel)

## Slide 2: LTE – Release 15
Technically endorsed CR to mandate setting FGI 103 and 104 (R2-1818598)
  Implements RAN#81 decision to mandate FGI 103/104 (RP-182137)
  The UE category from which the FGIs are mandated is left open to be finalized in RAN

## Slide 3: NR – Release 15 (1)
RAN2 has returned to the normal process of submitting separate CRs for separate issues
  In contrast to Q3 where the ASN.1 review for NR SA meant that RAN2 submitted a single CR containing all EN-DC and NR SA corrections.
  Separate CR per issue important to ensure that the problem, the correction, and the consequences can be fully captured on the coversheet.
Significant number of corrections were agreed and significant time consumed in the meeting
  Approximately 3-3.5 days in the main session and 2 days in parallel sessions at each of the October and November meetings

## Slide 4: NR – Release 15 (2)
No CRs were agreed with non backwards compatible (NBC) changes to the ASN.1
To fully understand the impact of a CR and to judge the criticality to implement, it is necessary to look at the impact analysis on the coversheet for the following information:
  The functionality affected by the CR
  The impact if only the UE or the network is implemented according to the CR
  The consequences if the CR is not agreed at all
As tasked by RAN#81 in RP-182074, (Cat B) CRs were agreed to add support for overheating indication for NR standalone (R2-1819179, R2-1019180)

## Slide 5: NR – Release 15 late drop
Corrections to EN-DC and NR SA were prioritised
  As a consequence the time available for the late drop was impacted
Good progress was made during and between the 2 meetings but not enough to declare completion
Current status:
  Stage 2 CR to 37.340 complete and submitted for approval (R2-1819036)
  Stage 3 draft CRs to 38.331 and 36.331 have been created and will be progressed by email to the February meeting
  2 other email discussions on specific topics (capabilities and QoS aspects) will also continue to the February meeting
  Functional completion in Q1 19 should be possible
For discussion and decision in RAN:
  To move late drop completion target by 3 months to March 19?
  To move late drop ASN.1 freeze date by 3 months to June 19?

## Slide 6: NR – Release 16
IAB Study Item (RAN2 led)
  38.874 v 1.0.0 is provided to RAN for a 1 step approval
  The conclusions of the TR includes several recommendations for the scope of an IAB work item WI.
  Study item is complete from RAN2 perspective
NR-U Study Item (RAN1 led)
  Study Item complete from RAN2 perspective
UE capability signalling Study Item (RAN2 led)
  Treated at RAN2#103bis but not at RAN2#104 due to prioritisation of NR Rel-15 corrections and late drop.
All other Rel-16 SIs/WIs handled as per their time budget allocation

## Slide 7: RAN2 time planning for Rel-16 – NR Situation from RAN#81
This table reflects the situation as captured in the time budget from RAN#81 (approved in RP-182180)
Notes: Present

## Slide 8: RAN2 time planning for Rel-16 - LTE+NR Situation from RAN#81
This table reflects the situation as captured in the time budget from RAN#81 (approved in RP-182180)
Includes the LTE capacity that is used by NR SIs/WIs
Shows some availability of TUs towards the end of Rel-16
Notes: Present

## Slide 9: RAN2 capacity issues for Rel-16 Proposed update for discussion (1)
Late drop
  With assumption that late drop completion and ASN.1 review will be shifted by 3 months addition time should be allocated to late drop in Q2 19
SA2/SA3 work requiring time in RAN2 but without associated RAN SI/WI in the current plan
  Potential work from SA3 SIs (e.g. longer MAC-I, protection of NSSAI in msg5)
  RAN aspects of SA2 WI on SRVCC (WI proposed in RAN#82)
  NB-IoT/MTC connected to 5GC (WI proposed at RAN#82)
  Possible other items as well?
UE cap SI
  Not treated at RAN2#104 but proposed not modify future TU allocation

## Slide 10: RAN2 capacity issues for Rel-16 Proposed update for discussion (2)
Next slide shows a proposed update to the RAN2 time budget as a starting point for discussion during this meeting
Conclusions
  Time needed for the SA2/3 related items needs careful consideration
  No capacity for any additional WIs/SIs beyond those already in the plan
  Q2 will be heavily over budget unless changes are made to existing items

## Slide 11: RAN2 NR R16 TUs - proposed update
Notes: Present

## Slide 12: RAN2 NR + LTE R16 TUs - proposed update
Notes: Present

## Slide 13: Summary and concluding remarks
Another extremely busy quarter with focus and priority on NR Rel-15 corrections.
Late drop not complete – needs to be prioritised in Q1 and Q2 2019
If SA2/3 related items are to be accommodated then no capacity for any additional WIs/SIs beyond those already in the plan
Q2 2019 is likely to be heavily over budget

## Slide 14: Special Thanks
Hu Nan (RAN2 VC)
Johan Johansson (RAN2 VC)
Kyeongin Jeong (V2X session chair)
Brian Martin (NB-IoT session chair)
Emre Yavuz (MTC session chair)
Nathan Tenny (Positioning session chair)
Diana Pani (LTE legacy, Inobear, NTN session chair)
Tero Henttonen (LTE mobility session chair)
Henning Wiemann (NR L1 parameters chair)
Juha Korhonen (MCC support)
Meeting hosts: Chinese Friends and North American Friends