## Slide 1
Motivation for a new WI on RAN aspects of integration of NB-IoT and eMTC in 5G system
www.huawei.com
3GPP TSG RAN Meeting #82
Sorrento, Italy, December 10 - 13, 2018
Agenda Item: 9.1.3
Huawei, HiSilicon
RP-182601

## Slide 2
Motivation
In Rel-13, eMTC and NB-IoT were standardised in RAN WGs to address improved indoor coverage, support for massive number of low throughput devices, low delay sensitivity, ultra low device cost, low device power consumption and (optimised) network architecture. They were further enhanced in Rel-14 and Rel-15.
The corresponding system architecture aspects have been designed for EPC for both Cellular IoT (Rel-13) and Cellular IoT extensions (Rel-14). EPC provides also features useful for IoT/MTC which have been defined over multiple releases: power saving functions, overload control, high latency communication, monitoring, service capability exposure, etc.
Rel-15 has standardised 5G CN and specified E-UTRA connectivity to 5G-CN, however not for NB-IoT and eMTC specific aspects.
SA2 has completed the "Study on Cellular IoT support and evolution for the 5G System" and has agreed on a work item to introduce 5G-CN enhancements to enable Cellular IoT functionalities for 5G capable devices that support eMTC and/ or NB-IoT.
An incoming LS from SA2 kindly ask RAN working groups to update RAN specifications accordingly in RP-182700.

## Slide 3
Objective
This RAN Work Item is motivated by the separation in rel-16 of the high layer impacts (RAN2/RAN3) with the RAN1 on-going work for a clear CR introduction with the ASN.1 changes in NB-IoT / eMTC and as benefit a dedicated allocation of TUs should be done. The high layer work is bind to SA2, then if any delays or major issue occur in SA2/RAN3/RAN2 work it may be clever to not penalized the completion of RAN1 work and reciprocally
The objective of this work item is to introduce support of CIoT functionalities in 5G CN support for NB-IoT and eMTC.
NB-IoT Connectivity to 5G-CN
eMTC specific aspects of E-UTRA Connectivity to 5G-CN
Enhancements to enable Cellular IoT functionalities in 5G-CN as per SA2 WI, in particular;
  Support for infrequent small data transmission
  Frequent small data communication
  Power saving functions
  Management of Enhanced Coverage
  …
The following slides provide a preliminary analysis of the RAN impact of SA2 WI
We propose to conditionally approved the WID to SA decision on approval of SA2 WI by end of TSG week

## Slide 4
SA2 Objectives
SA2 has agreed the WI with the below objectives in S2-1812837 aiming at specifying 5GS enhancements to enable Cellular IoT functionalities for 5GS capable devices that support also WB-EUTRA (eMTC) or NB-IoT or both:
- Support for infrequent small data transmission
- Frequent small data communication
- High latency communication
- Power saving functions
- Management of Enhanced Coverage
- Overload Control for small data
- Support of the Reliable Data Service
- Support of common north-bound APIs for EPC-5GC interworking
- Network parameter configuration API via NEF
- Monitoring
- Inter-RAT mobility support to/from NB-IoT
- Support for Expected UE Behaviour
- QoS Support for NB-IoT
- Core Network selection and steering for Cellular IoT
- Group Message Delivery using unicast NIDD
- MSISDN-less MO SMS
- Interworking with EPS for the Cellular IoT functionalities listed above

## Slide 5
Potential impact of 5G CIoT on RAN WGs
Objective | Impact | WG | Comments | Apply to NB-IoT or eMTC?
Support for infrequent small data transmission | yes | RAN2/RAN3 | Equivalent of EPS control plane optimisation | Both NB-IoT and eMTC
Frequent small data communication | yes | RAN2/RAN3 | Equivalent of EPS user plane optimisation | Both NB-IoT and eMTC
High latency communication | No |  | Only CN impacts | Both NB-IoT and eMTC
Power saving functions | yes | RAN2/RAN3 | Equivalent of EPS eDRX and PSM | Both NB-IoT and eMTC
Management of Enhanced Coverage | yes | RAN2/RAN3 | Equivalent of EPS authorisation of coverage enhancements | Both NB-IoT and eMTC
Overload Control for small data | yes | RAN2/RAN3 | Equivalent of EPS overload control for small data (e.g. overload control for control plane data, …) | Both NB-IoT and eMTC
Support of the Reliable Data Service | No |  | Assume only impact on CN | Both NB-IoT and eMTC
Support of common north-bound APIs for EPC-5GC interworking | No |  | Only CN impacts | Both NB-IoT and eMTC
Network parameter configuration API via NEF | No |  | Only CN impact | Both NB-IoT and eMTC

## Slide 6
Potential impact of 5G CIoT on RAN WGs – Cnt’d
Objective | Impact | WG | Comments | Apply to NB-IoT or eMTC?
Monitoring | No |  | Only CN impacts | Both NB-IoT and eMTC
Inter-RAT mobility support to/from NB-IoT | yes | RAN3 | Equivalent of EPS Inter-RAT mobility e.g. separate set of UE capabilities … | NB-IoT only
Support for Expected UE Behaviour | yes | RAN3 | Equivalent to EPS UE differentiation | NB-IoT only
QoS Support for NB-IoT | yes | RAN2/RAN3 | Equivalent of EPS Inter-UE QoS for NB-IoT UEs using Control Plane CIoT EPS Optimisation | NB-IoT only
Core Network selection and steering for Cellular IoT | yes | RAN2/RAN3 | New feature | Both NB-IoT and eMTC
Group Message Delivery using unicast NIDD | No |  | Expect CN impacts only | Both NB-IoT and eMTC
MSISDN-less MO SMS | No |  |  | Both NB-IoT and eMTC
Interworking with EPS for the Cellular IoT functionalities listed above | No |  |  | Both NB-IoT and eMTC

## Slide 7
SA2 Supporting companies [S2-1812837]

## Slide 8
Copyright©2015 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !