## Slide 1: WF on CR(s) for 2Rx exception for NR vehicle UE
SAMSUNG, LG Electronics, Volkswagen AG
3GPP TSG-RAN #82 Meeting
Sorrento, Italy, 10-13 Dec, 2018 Agenda Item: 9.3.16
RP-182798

## Slide 2: 1. CR to TS 38.101-1

## Slide 3: Agreement 1: Definitions and notes in TS 38.101-1
Section 3 in TS 38.101-1
“An UE embedded in a vehicle, permanently connected to an embedded antenna system that radiates externally for NR operating bands”
Note: Vehicular UE does not refer to other UE form factors placed inside the vehicle.
Section 7 in TS 38.101-1 (Table 7.3.2-1)
NOTE 1:Four Rx antenna ports shall be the baseline for this operating band, except for 2 Rx vehicular UE.

## Slide 4: 2. CR to TS 36.300

## Slide 5: Agreement 2: SPID agreement in TS 36.300
Define SPID as shown below:
Table I.2-4: Network local configuration in idle and connected mode for SPID = 253
Configuration parameter | Meaning
Automotive device subscriber | The selection provides information that subscriber is using an automotive device and is permitted to utilise a minimum of two Rx antenna ports for the NR bands where four Rx antenna ports are baseline as given in TS 38.101-1 [86]