## Slide 1: Motivation for new SI: Study on Flexible and Full Duplex for NR
LG Electronics
3GPP TSG RAN Meeting #83
Shenzhen, China, March 18-21, 2019
RP-190265

## Slide 2
Introduction
Trends in NR
  Support duplexing flexibility with and without cross-link interference mitigation schemes
  Explosive Increase in Demand for Data Traffic
    Traffic volume/burst and DL/UL traffic asymmetry
  Ultra Low Latency required
  Support Various Usage Scenarios by a single cell: eMBB, URLLC, mMTC
Enabling Technologies
  Advanced cross-link interference mitigation schemes such as IC receivers
  Dynamic and flexibility of frequency resource utilization
    Support flexible DL/UL resource allocation with FDM manner
    - e.g., multiplexing between eMBB DL and URLLC UL with FDM manner
    - e.g., multiplexing between mMTC UL and eMBB/URLLC DL with FDM manner
  Full duplex functionality
    Support simultaneous DL/UL resource allocation for spectral efficiency enhancement and latency reduction
NR requires further enhanced solution with high spectral efficiency and low latency

## Slide 3
Motivation
As service requirement with asymmetric UL and DL traffic increases, and the ratio between UL and DL traffic changes over the time, the static spectrum for UL and DL is not efficient to support dynamic asymmetric traffic.
Dynamic Duplexing flexibility in NR band are essential.
Service type | UL/DL ratio -average
Online video | 1:37
Software download | 1:22
Web browsing | 1:9
Email | 1:4
Social Network Service | 4:1
P2P video sharing | 3:1

## Slide 4
Motivation
Limitation in TDM between DL/UL
  TDM between DL and UL leads higher latency in both DL and UL due to time partitioning between DL and UL
  Symmetric DL/UL partitioning to address URLLC may not be effective from spectral efficiency perspective particularly when traffic patterns are either DL heavy or UL heavy
Further enhancements in spectral efficiency
  By allowing full duplex functionality at one spectrum, enhanced spectral efficiency can be achieved (ideally by 2x)

## Slide 5
Flexible Duplex for NR (1/2)
Flexible Duplex with FDM manner
  Handling Mixed Usage Scenarios
    - e.g., multiplexing between eMBB DL and URLLC UL with FDM manner
    - e.g., multiplexing between mMTC UL and eMBB/URLLC DL with FDM manner
  Sub-band wise DL/UL adaptation required
  Occurrence of DL’s OOB power in UL reception at gNB
  Occurrence of inter-cell cross-link Interference between gNBs and UEs
Potential gains from flexible duplex with FDM manner
  DL or UL resource availability at any time  possibly reduce latency for URLLC applications
  Multiplexing becomes easy for different usage scenarios
<Example of flexible duplex with FDM manner>

## Slide 6
Flexible Duplex for NR (2/2)
Power of DL’s emission in UL reception in Flexible Duplex with FDM multiplexing
  Observation #1: About 50dB suppression can be achieved with sufficient guard band and antenna SIC only even though without any filtering on Tx signals
# of antennas (Tx, Rx) | (1,1)
System bandwidth | 80MHz
Occupied bandwidth | 72MHz
Subcarrier spacing | 60kHz
# of subcarriers in a RB | 12
# of allocated RBs | 4 RBs (2.5072~2.51)
Measurement resolution | 100kHz
<System parameters>

## Slide 7
Full Duplex for NR (1/2)
<Example of full duplex operation at gNB>
Full Duplex at gNB
  Efficient adaptation for time variant DL/UL data traffic
    Spectral efficiency enhancement via fully utilized frequency resources
    Overall latency reduction via always on UL transmission opportunity
    Easier multiplexing among different usage scenarios with different DL/UL traffic patterns
  gNB with Full Duplex capability required
  Occurrence of self-Interference at gNB
  Occurrence of inter-cell cross-link interference between gNBs
  Occurrence inter/intra-cell cross-link interference among UEs
Potential gains from full duplex
  Expected spectral efficiency enhancement
* N X M, where N, M are the number of transmit and receive antennas, respectively.

## Slide 8
Full Duplex for NR (2/2)
Residual power after antenna and RF domain self-interference cancellation
  Observation #2: about 65dB cancellation after antenna and adaptive RF domain self-interference cancellation
# of antennas (Tx, Rx) | (1,1)
System bandwidth | 80MHz
Occupied bandwidth | 72MHz
Subcarrier spacing | 60kHz
# of subcarriers in a RB | 12
# of allocated RBs | 100 RBs (2.494~2.566)
Measurement resolution | 100kHz
<System parameters>
65dB SI reduction
with antenna and RF SIC

## Slide 9
Flexible and Full Duplex in IAB Nodes
  Flexible and Full duplex operation can solve half duplex constraint at IAB nodes
<Example of flexible duplex with FDM manner at IAB node>
<Example of full duplex at IAB node>

## Slide 10
Conclusions
  Flexible and/or full duplex operation is feasible with appropriate techniques such as guard band, advanced receiver, antenna/analog/digital domain self-interference cancellation, etc.
  Flexible and/or full duplex operation provides substantial benefits in terms of spectral efficiency and latency reduction
  Proposal: Study enhanced mechanisms for better duplexing flexibility and full duplex operations in NR band

## Slide 11: Thank You