## Slide 1
RAN4 Chairman: Xutao Zhou
RAN4 Vice Chairman: Xizeng Dai
RAN4 Vice Chairman: Hiromasa Umeda
RAN4 Secretary: Kyoungseok Oh
Status Report RAN WG4 to TSG-RAN #84
3GPP TSG RAN #84 RP-190783
Newport Beach California, US, 13– 17 May, 2019

## Slide 2: Executive Summary – Rel-15 NR
With significant TUs spent in Q2, all open issues for Rel-15 (including the late drop) core requirements as captured in the NR exception sheet were completed.
For performance part of Rel-15 SA and NSA, significant progress was achieved in Q2.
  Most of TBDs are removed from the specifications(38.101-1, 38.104 and 38.133), while there still are remaining TBDs especially for RRM test cases.
Performance part of Rel-15 late drop will start in the next quarter according to RAN-agreed schedule
As tasked by RAN, beam correspondence and maximum uplink duty cycle have been concluded in RAN4 in Q2.
Further updated RAN4 feature list by capturing the latest RAN4 decisions are supposed to be discussed and approved in RAN #84

## Slide 3: Executive Summary – Rel-16 NR
Good progress in Rel-16 NR WI/SI for both spectrum and non-spectrum.
  Most of other WG led Rel-16 WI with RAN4 core requirements impacts have been started in RAN4.
  The following RAN4 led Rel-16 WIs approved in RAN #83 are on hold in Q2
    RF requirements for FR1
    RF requirements for FR2
  For other WG led Rel-16 items, If RAN4 impact is identified and no RAN4 TU for 2019 Q3 and 2020 Q1 was requested before, early request for RAN4 TU are encouraged
  For spectrum related items including basket items, RAN4 has agreed CRs to Rel-16 38 series Technical specifications. CR packs to Rel-16 NR specifications have been submitted for approval in RAN #84 as scheduled.

## Slide 4: Executive Summary – LTE & MSR
LTE maintenance up to Rel-15 and Rel-15 performance
  Number of maintenance CRs for Rel-15 WI performance parts has been reduced.
Rel-16 LTE & MSR
  Good progress in Rel-16 LTE and MSR items including spectrum and non-spectrum items

## Slide 5: Statistics
Meeting | Date | Location | Host | Delegates registered/attendees | Documents requested/uploaded
RAN4 #90bis | 8th – 12th April 2019 | Xi’an, CN | CF3 | 431/324 | 2443/2774
RAN4 #91 | 13th – 17th May 2019 | Reno, US | NF3 | 450/387 | 2546/2337
Chart: 
| #90 | #90bis | #91
Delegates | 372 | 324 | 387
Chart: 
| #90 | #90bis | #91
Contributions | 2584 | 2774 | 2337

## Slide 6: NR

## Slide 7: Completion of ongoing WI/SI
WI to be completed – Rel-16 spectrum related WIs
  Endorsed CR packs include the CR to eAAS specifications (37.105, 37.145-1 and 37.145-2) which were endorsed in RAN4 due to eAAS specifications are not included in the WID.
  Endorsed CR packs are supposed to be approved in RAN #84 based on the approval of revised WID which includes eAAS specifications in the WID.
Title | SR | CR packs | Endorsed CR packs
Band n14 | RP-190979 | RP-191242 | RP-191243
Band n18 | RP-190927 | RP-191244 | RP-191245
Band n30 | RP-190981 | RP-191246 | RP-191247
Band n48 | RP-190909 | RP-191248 | RP-191249
Band n65 | RP-190860 | RP-191250 | 
Adding BW for band n50 | RP-191111 | RP-191251 | 
LTE/NR spectrum sharing in Band 41/n41 | RP-190929 | RP-191252 | 

## Slide 8: NR specifications
CR packs including the CR for Rel-15 NR specifications agreed by RAN4
Big CRs approach will be continually used in Q3 2019
RP‑191236 | RAN4 CRs to NR Access Technology part 1
RP‑191237 | RAN4 CRs to NR Access Technology part 2
RP‑191238 | RAN4 CRs to NR Access Technology part 3
RP‑191239 | RAN4 CRs to NR Access Technology part 4
RP‑191240 | RAN4 CRs to NR Access Technology part 5

## Slide 9: Rel-15 NR – Tasked by RAN
Beam correspondence
  Based on RAN WF (RP-182879), RAN4 concluded correspondence beam correspondence tolerance requirements (R4-1907611) as
  Test procedure for beam correspondence were also concluded and captured in TR38.810
  Simulation results were captured in TR 38.817-01 for further information
  Further discussion and decision is needed for side condition for SSB and CSI-RS in future RAN4 meetings.
Operating band | Max ∆EIRPBC at 85%-tile ∆EIRPBC CDF (dB)
n257 | [3]
n258 | [3]
n260 | [3.2]
n261 | [3]
Note: The requirements in this table are verified only under normal temperature conditions as defined in Annex E.2.1 | 

## Slide 10: Rel-15 NR – Tasked by RAN
Maximum duty cycle for FR2
  As in LS (R4-1907458) to RAN2 and RAN5, 15 % value should be allowed for UE capability maxUplinkDutyCycle-FR2 in addition to values what were in WF from plenary, i.e. possible declarable values are 15%, 20%, 25%, 30%, 40%, 50%, 60%, 70%, 80%, 90% and 100%
  Further conclusions including evaluation period and UE behaviour were also captured in above LS.

## Slide 11: Rel-15 NR – Feature List
Updated UE feature list was also discussed in RAN4 #91. Latest updated UE feature list was approved in RAN4. The major updates are
  Maximum uplink duty cycle
  FG2-9 (UE power class)
Further discussion on “TSG-RAN decision” column is expected in RAN #84

## Slide 12: Rel-16 NR – NR-U
Initial agreements on band plan for 5GHz was approved, i.e., defining 20MHz, 40 MHz, 80 MHz, 100MHz CBW for band n46.
  Other bandwidth options (10MHz, 60MHz and 160MHz) and mandatory support of 100MHz are FFS.
No consensus reached for 6GHz band plan
Response LS to RAN1 on request of introducing 10MHz with some restrictions in NR-U WI was approved.
LS to ETSI on in carrier leakage requirements was approved in R4-1907850
For SS raster, consensus on below common understanding was reached.
  It is agreed to define NR-U sync raster based on the global NR raster design in Rel-15.
  RAN4 intension is to reduce the number of SS entry per 20MHz for NR-U
  Whether to restrict the SSB placement in the middle or edge will be defined in RAN4 considering the cell search performance
WF for RRM requirements for NR-U was approved

## Slide 13: Rel-16 NR – CLI and RIM
Based on the co-existence study, RAN4 concluded summary and recommendation for CLI operation in different scenarios.
Initial agreements for RRM requirements for SRS-RSRP and CLI-RSSI
TR for co-existence study (RP-191357) are submitted in RAN #84 for approval

## Slide 14: Rel-16 NR – NR mobility enhancement
Feasibility study for handover with simultaneous Rx/Tx and RACH-less handover have been concluded
Progress on handover delay for conditional handover.

## Slide 15: Rel-16 NR – 5G V2X and NR sidelink
    Simulation scenarios and parameters for NR V2X have been agreed
    Response to RAN1 on feasible AGC settling time performance. No consensus reached for IBE model
    Some initial agreements for NR V2X RRM

## Slide 16: Rel-16 NR – IAB
    RAN4 agreed to introduce dedicated specification for IAB at least for RF and EMC. FFS on whether to include RRM in dedicated IAB spec or existing RRM spec
    RAN4 agreed that no impact to existing UE and BS RF requirements and performance requirements due to introduction of IAB
    Simulation assumptions for IAB co-existence study
    WID will be revised by adding new spec and removing existing UE and BS spec from impacted specs (RP-191036)

## Slide 17: Rel-16 NR – Others
    UE power saving
  Initial agreements on switching delay and interruption time for MIMO layer adaption
MR-DC
  No input for RF in Q2.
  No TU allocated for RRM in Q2.
FR2 DL 256QAM
  Simulation assumptions for feasibility study was approved

## Slide 18: Rel-16 NR –Spectrum WI
Spectrum-related WIs including basket WIs were going well in Q2.
Completed items are summarized in slide 7
Band n259
  Band plan for n259 is 39.5 GHz – 43.5 GHz
  Intra-band CA requirements shall apply for inter-band CA configurations between n260 and n259 including intra-band capabilities
Spectrum sharing for band 41/n41
  It was concluded to introduce new NR band (n90) to achieve spectrum sharing in 2496 MHz – 2690 MHz
  Agreement on RF requirements for new band
Power class 2 for EN-DC (TDD+TDD)
  Agreements on RF requirements for PC2 for EN-DC

## Slide 19: Rel-16 Basket WI Status
Rel-16 NR Basket WI Status Report
Above revised WIDs have been endorsed by RAN4
WI Title | Status Report | Revised WID
NR intra-band CA | RP-191191 | RP-191194
NR inter-band CA/DC for 3 bands DL with 2 bands UL | RP-191351 | RP-191352
NR inter-band CA for 3 bands DL with 1 band UL | RP-191152 | RP-191153
EN-DC for 2 bands DL with 2 bands UL (1 LTE band + 1 NR band) | RP-191317 | RP-191316
EN-DC for 3 bands DL with 2 bands UL (2 LTE bands + 1 NR band) | RP-191123 | RP-191124
EN-DC for 4 bands DL with 2 bands UL (3 LTE bands + 1 NR band) | RP-191192 | RP-191195
EN-DC for 5 bands DL with 2 bands UL (4 LTE bands + 1 NR band) | RP-191204 | RP-191205
EN-DC for 6 bands DL with 2 bands UL (5 LTE bands + 1 NR band) | RP-191152 | N/A
Inter-band CA/DC for 2 bands DL with up to 2 bands UL | RP-191349 | RP-191350
EN-DC of LTE inter-band CA for up to 4 bands DL with 1 band UL + NR inter-band CA for 1 band DL with 1 band UL | RP-190950 | RP-190949
SA SUL, NSA SUL, NSA SUL with ULSUP | RP-191125 | RP-191126

## Slide 20: Rel-16 NR – SI
7-24 GHz
  Initial analysis on RF technologies feasibility study
  Agreements on WF for BS RF requirements, UE RF requirements and BS EMC
  Example frequency ranges and example frequencies were selected
  Initial agreements on set of deployment scenarios
MIMO OTA
  Approved channel model for FR1 and FR2
  Initial agreements for environmental condition for FR1 and FR2
  Initial agreements for test methodologies
High power for EN-DC (FDD + TDD)
  RAN4 agreed to start with LTE max 23 dBm + NR max 23dBm for study. Different solutions are proposed for further study
  Completion level (45%) is behind the schedule (100%)
  2 quarters extension are requested.

## Slide 21: LTE

## Slide 22: Rel-16 LTE – eMTC and NB-IoT
eMTC5 – sets of agreements for
  Co-existence with NR
  Support of quality report in Msg3 and connected mode
  UE-group WUS
  MPDCCH performance improvement
  Preconfigured UL resources
  Mobility enhancement
  Use of RSS for measurement improvement
NB-IOTenh3 - sets of agreements for
  Co-existence with NR
  UE-group WUS
  Multi-carrier operation
  Preconfigured UL resources

## Slide 23: Rel-16 LTE – Others
DL MIMO efficiency enhancement
  Response LS on transient period for antenna switching or frequency hoppiong was approved
Even further mobility enhancement
  WF on handover delay requirements
LTE high speed
  WF for RRM requirements, UE demod performance and BS demod performance
  LS to RAN2 on capability and signaling for LTE high speed
  LS to RAN2 on UE demodulation performance enhancement indicator for HST-SFN scenario

## Slide 24: Rel-16 LTE Spectrum related WI
410 – 430MHz E-UTRA FDD band(s) WI is completed
Power class 2 UE for LTE band 31 and 72
  Scope is changed to cover only HD-FDD UE categories M1 and M2
Rel-16 LTE Basket WI Status Report
  Above revised WIDs have been endorsed by RAN4
WI Title | Status Report | Revised WID
LTE intra-band CA | RP-191190 | RP-191193
LTE inter-band CA for 2 bands DL with 1 band UL | RP-191084 | RP-191085
LTE inter-band CA for 3 bands DL with 1 band UL | RP-191119 | RP-191120
LTE inter-band CA for x bands DL (x=4, 5) with 1 band UL | RP-190907 | RP-190906
LTE inter-band CA for 2 bands DL with 2 band UL | RP-191121 | RP-191122
LTE inter-band Carrier Aggregation for x bands DL with 2 bands UL | RP-190947 | RP-190946
Additional LTE bands for UE category M1 and/or NB1 | RP-190951 | N/A
Additional LTE bands for UE category M2 and/or NB2 | RP-190952 | N/A

## Slide 25: MSR

## Slide 26: Rel-16 MSR
Introduction of GSM, UTRA, E-UTRA and NR capability set(s) to the MSR specs
  Work plan is approved
  Draft CRs for core part was endorsed
  WF on capability set was agreed for performance part

## Slide 27: Action to RAN
It was proposed to maintain the UTRA FDD specifications for BS co-existence requirements for frequency range of NR bands in RAN #83 in RP-190683
The confirmation was somehow missing in the meeting report of RAN #83.
Re-confirmation of stopping maintain UTRA FDD specification due to introduction of NR bands is needed in RAN #84
=> ACTION: In REL-16 and future releases, RAN4 will no longer define BS co-existence requirements in RAN4 UTRA FDD specifications for frequency ranges of NR bands. Is this ok for RAN?

## Slide 28: New Rel-16 Proposals

## Slide 29: New WI/SI proposals – Spectrum
  Spectrum related proposal for NR (8)
  WI: Introduction of 30MHz BW in band n1 (Huawei)
  WI: Introduction of 1900MHz SUL band for NR (Huawei)
  WI: Dual Connectivity (EN-DC) with x (x=3,4,5, 6) bands DL (max.3 NR) and 3 bands UL (max. 2 NR) (ZTE)
  WI: RF requirements for EN-DC with equal to or larger than 3 uplink CCs (Huawei)
  WI: NR inter-band Carrier Aggregation for 4 bands DL with 1 band UL (Ericsson)
  WI: Introduction of NR supplementary DL band n29 (DISH)
  WI: SUL+SDL paired bands and corresponding EN-DC band combinations (Vodafone)
  SI: Study on new NR band 6.425-7.125GHz (Huawei)
Spectrum related proposals for LTE (1)
  WI: LTE-LAA based Access in 6GHz Spectrum

## Slide 30: New WI/SI proposals – Non-Spectrum
The following items were discussed in RAN #83. RAN tasked RAN4 to further discuss the scope by e-mail before RAN #84
  WI: Rel-16 RRM
    E-mail discussion on the scope is summarized in RP-191024
  WI: Rel-16 Demod and CSI
    E-mail discussion on the scope is summarized in RP-191025
  WI: NR support for High speed train scenario
    E-mail discussion on the scope is summarized in RP-191026
Other proposals
  WI: Power class 5 for FR2
  SI: Enhanced test methods for NR FR2
  SI: Measurement gap enhancement for NR

## Slide 31: RAN4 TU summary
 | Q3 2019 |  | Q4 2019 |  |  |  | Q1 2020 |  | 2020 Q2 |  |  |  | 2020 Q3 | 
 | RF | RD | RF | RD | RF | RD | RF | RD | RF | RD | RF | RD | RF | RD
Total NR | 24 | 15 | 24 | 15 | 24 | 15 | 24 | 15 | 24 | 15 | 24 | 15 | 24 | 15
Rel-15 NR Core | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rel-15 NR Perf | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rel-16 | 23.8 | 8 | 22.6 | 10 | 23.1 | 10 | 13.1 | 9 | 0.75 | 10 | 0.25 | 10 | 0.25 | 8.5
Available TU for NR | -1.8 | 4 | 1.4 | 4 | 0.9 | 4 | 10.9 | 6 | 23.25 | 5 | 23.75 | 5 | 23.75 | 6.5
Total LTE | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Maintenance LTE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rel-16 | 3 | 4 | 3 | 4.5 | 4 | 5.5 | 1.75 | 3.5 | 1 | 3 | 1 | 3 | 0.5 | 0.5
Available TUs for LTE | 0 | -1 | 0 | -1.5 | -1 | -2.5 | 1.25 | -0.5 | 2 | 0 | 2 | 0 | 2.5 | 2.5
Total | -1.8 | 3 | 1.4 | 2.5 | -0.1 | 1.5 | 12.15 | 5.5 | 25.25 | 5 | 25.75 | 5 | 26.25 | 9
RAN4 led Rel-16 for RD can be started in Q3 with prioritization on RRM core
RAN4 led Rel-16 for non-spectrum related RF can be started in Q4 assuming spectrum related proposals will be approved as usual

## Slide 32: RAN WG4 Schedule in 2019
Meeting | Date | Location | Host
3GPP RAN4-AH-1906 (Cancelled) | 24 – 28 Jun 2019 | TBD | 
3GPPRAN4#92 | 26 – 30 Aug 2019 | Ljubijana | EF3
3GPPRAN4#92bis | 14 – 18 Oct 2019 | CN | CF3
3GPPRAN4#93 | 18 -22 Nov 2019 | Reno | NF3

## Slide 33: Thanks to
NR specifications rapporteturs and their companies for their extraordinary effort of coordinating the RAN4 discussions and also editing RAN4 NR specifications:
  Ville Vintola (Qualcomm): 38.101-1/2/3
  Johan Sköld (Ericsson): 38.104
  Yang Tang (Intel): 38.133
  Haijie Qiu (Samsung): 38.101-4
  Steven Chen (Huawei): 38.141-1/2
  Aijun Cao and Rui Zhou (ZTE): 38.113
  Christian Bergljung (Ericsson): 38.124
  Petri Vasenkari (Nokia): 38.307
Vice chairmen Xizeng Dai and Hiromasa Umeda for preparation and session chairing
Kyoungseok Oh for efficient secretary support
AH chairs and WI rapporteurs for coordinating the offline/ad-hoc discussions
Delegates for enthusiastic contributions
CF3 and NF3 for meeting hosting