## Slide 1: KPNs preferred areas for release17
RP-190862
TSG RAN#84 – Newport Beach, CA, USA, 3-6 June 2019

## Slide 2: Welcome to vertical sectors
5G to address vertical sectors
  More and more vertical sectors are coming to 3GPP with new requirements that stretch what is currently possible
  It is KPN’s opinion that Release 17 should include further improvements that fulfil these requirements and enable new vertical use cases
Maritime
Automotive
Public Safety
Railway
Industry
Logistics
AV production
Unmanned Aerial Vehicles
Medical
Logistics
UAVs

## Slide 3: NR Performance improvements
Even higher bitrates
  Some applications need uncompressed media (e.g. 12 Gbps for uncompressed UHD video)
  Trade-off between compression and latency
  Best quality needed for post-processing
Even lower latency
  Time sensitive networking with very small intervals (e.g. 0.5 ms)
  Challenging end-to-end latency requirements at application layer (e.g. < 4 ms mouth to ear latency)
Better availability
  For many verticals availability always and everywhere is crucial
  What can we do to improve availability?

## Slide 4: 5G local broadcast capabilities with NR
Vertical applications with many recipients of the same information in a targeted area benefit from local broadcast
  Mission critical push-to-talk
  IoT applications (e.g. smart streetlights, digital signage)
  Energy distribution networks
Broadcast in a dedicated area
  Not broadcast across the country, but broadcast in a city or specific residential area
  Dynamic control of geographic area

## Slide 5: Use of sidelink for indoor coverage
Indoor coverage problem
  Indoor coverage can be an issue (metallic environment in factories, mmwave obstructions by walls, furniture, people)
  Planning an indoor network is not always possible (e.g. cabling in existing houses, dynamically changing environment)
Relaying as a solution
  Cable-less solution to extend coverage
  Combine relay function in a UE to avoid separate boxes
  Relay UE can be more powerful than ordinary UEs (e.g. TV with mains-power or ambulance with better antenna and battery relaying to ambulance workers in the house)
gNB
5GC

## Slide 6: High accuracy positioning indoor and outdoor
Better accuracy needed for NR positioning
  Many applications (e.g. automated guided vehicles) require accurate positioning
  Industry requirements indicate accuracy of up to 20 cm
Issue is indoor positioning
  New global navigation satellite systems (e.g. Galileo) can achieve required accuracy
  The challenge is indoor positioning