## Slide 1: FUJITSU Views on Rel-17 RAN Enhancements
FUJITSU LIMITED
3GPP TSG RAN Meeting #84
Newport Beach, USA, June 3-6, 2019
RP-190955

## Slide 2: Timeline of Rel-17
2019
2020
2021
Rel-15
RAN1
RAN2 / RAN3
Rel-17 ASN.1
RAN1
RAN2 / RAN3
Rel-16 ASN.1
Late drop ASN.1
Release 16
Release 17
RAN1
RAN2 / RAN3
Release 18
Support 15-month Rel-17.

## Slide 3: FUJITSU views on Rel-17
Continuing items
MIMO/eMBB | NR Unlicensed band
V2X | URLLC/IIoT
New features
New spectrum
Intelligent techniques
NR-IoT
Manufacturing | Surveillance |
Wearable
devices
NR-WLAN
NR + WLAN
FR 1
FR 2
New spectrum
Frequency
Above 52.6 GHz
52.6 GHz
114.25 GHz
AI/ML in RAN
Service/traffic prediction

## Slide 4: Overview of potential Rel-17 SIs/WIs
FR1
(450 MHz – 7.125 GHz)
FR2
(24.25 GHz – 52.6 GHz)
Above 52.6 GHz
(52.6 GHz – 114.25 GHz)
eMBB enh.
(incl. MIMO)
V2X enh.
(incl. non-V2X D2D)
URLLC/IIoT enh.
NRU enh.
NR IoT
AI/ML in RAN
NR WLAN
Work item / Study item
Work item
Work item
Study item / Work item
Study item / Work item
Study item
Study item
Work item

## Slide 5: Above 52.6 GHz
eMBB/IAB
with high data rate
URLLC
with more available resource and more controlled interference
Positioning
with high accuracy
V2X/D2D
in ITS/as a cable-less high speed connection
Abundant resource
on band >52.6 GHz
FR1
FR2
>52.6
GHz
450 MHz
7.125 GHz
24.25 GHz
52.6 GHz
114.25 GHz

## Slide 6: Above 52.6 GHz
2020
2021
RAN1-led SI on > 52.6GHz
Rel-18
V2X/D2D @ >52.6GHz
Positioning @ >52.6GHz
IAB @ >52.6GHz
SI phase I: Carefully study hardware restrictions
Phase noise/PA efficiency etc.
SI phase II: Study waveform/ numerology/ maximum bandwidth of single carrier etc.
Separated WIs for specific topics later on.
NR-U @ 60GHz
Design radio access techniques.
Rel-17
WI on eMBB/MIMO enh.
WI on > 52.6GHz
Measured phase noise
100kHz
1MHz
-90.04 dBc/Hz
-88.36 dBc/Hz
f0=80GHz
Factors related to SCS selection:
Phase noise distribution
CP overhead
To guarantee the coverage, consider:
Increase antenna number.
Improve PA efficiency.
Carefully study of hardware restrictions is necessary

## Slide 7: NR-IoT
NR-IoT
Capability/cost of IoT devices
URLLC/IIoT
NB-IoT
eMTC
Manufacturing | Surveillance |
Wearable
devices
NR-IoT in Rel-17:
Provide solution with acceptable device cost for the IoT application area between LPWA and URLLC.
2020
2021
RAN1-led SI on NR-IoT
Rel-18
Scopes of NR-IoT SI, including:
Carefully identify use cases and the corresponding performance requirements.
Study how to reduce the complexity/cost of the NR-IoT devices.
Study how to increase the battery life of the NR-IoT devices.
Rel-17
Work item on NR-IoT

## Slide 8: NR-WLAN RAN-level integration (NW-RI)
  Problem Statement
    Rel-15 NR-WLAN integration: only supporting NW-level integration
      Difficulty in sophisticated RAN operation (quasi-zero error rate, fast mobility support)
  Requirement
    RAN-level integration: Already deployed WLAN system into 5G-NR with small impacts
  Concept: RAN-edge (gNB) processing for XA control
    (1) New I/F for integration (2) Data distribution/duplication (DDD) (3) 0 loss/ms mobility (OLM)
XA (X-Automation)
NW-RI (NR-WLAN RAN-level integration)
5GC
5G NR
WLAN
WLAN
(1)I/F
(2)DDD
5G NR
5G NR
(3)OLM
XA control

## Slide 9: AI/ML in the RAN
Use cases of
artificial intelligence and machine learning (AI/ML) in the RAN
Assistance for coordination between the management, 5GC and NG-RAN domains.
Support for AI/ML-based high layer control of RAN operations.
Support for AI/ML-based RAN level traffic prediction to enhance device power saving and improve paging performance.
Standardization impacts
For data collection to support AI/ML:
Identification of relevant measurement quantities, events and faults for collection and utilization.
New procedures for configuration and collection of UE measurements, RAN node measurements and signaling procedures for distributed and central analyses.
Study the data formats for suitable applying machine learning in the RAN.
New schemes to assure the privacy and security of data.
New procedures and information exchange required for the different use cases

## Slide 10
SUMMARY

## Slide 11: Summary
Support 15-month Rel-17.
  The Rel-17 SIs/WIs should be carefully planned to make sure the scopes of Rel-17 SIs/WIs are able to match 15-month timeline.
The following SIs/WIs should be approved for Rel-17 RAN enhancements:
  Continuing items
    Work item of further enhancement of MIMO/eMBB.
    Work item of further enhancement of URLLC/IIoT.
    Work item of enhancement of V2X including non-V2X D2D scopes.
      A study phase may be required for non-V2X D2D scopes.
    Enhancement of NR un-licensed band.
  New items
    Study item/work item of above 52.6 GHz.
    Study item/work item of NR-IoT.
    Study item/work item of NR-WLAN RAN-level integration.
    Study item of support AI/ML in the RAN.

## Slide 13: Appendix : Details of Proposed Potential SIs/WIs

## Slide 14: Study item/work item of beyond 52.6 GHz
RAN1-led SI on beyond 52.6 GHz after RAN study item finishes. This SI includes
  SI phase I: study on hardware restriction, such as phase noise distribution and PA efficiency, should be carefully examined with given transmission power and bandwidth.
  SI phase II: study waveform/ numerology/ maximum bandwidth of single carrier.
    If CP-OFDM or SC-FDMA – like waveform is adopted, the design of NR @FR1/FR2 should be re-used as much as possible.
Separated WIs are preferred after RAN1-led SI finishes.
  Licensed band design goes to eMBB/MIMO enhancement WI (1st priority in Rel-17)
  After Licensed band design completes or later than Licensed band design (2nd priority, maybe, after Rel-17),
    Un-licensed band design goes to NR-U enhancement WI.
      To save standardization efforts in WGs, licensed band design should be reused as much as possible.
    IAB-related design goes to IAB enhancement WI.
    D2D-related design goes to D2D/V2X enhancement WI.
    High accuracy positioning-related design goes to positioning enhancement WI.

## Slide 15: Study item/work item of NR-IoT
RAN1-led SI of NR-IoT should be supported in Rel-17, followed by a WI.
The SI/WI should focus on IoT use cases between ‘URLLC/TSN’ and ‘eMTC/NB-IoT’, i.e. mid-end IoT devices (e.g. surveillance cameras, wearable devices etc. ).
Scopes of the SI includes:
  Identify use cases and the corresponding requirements.
  Study techniques which are able to reduce the complexity of NR IoT devices compared with NR eMBB devices.
  Study techniques which are able to increase the life of battery compared with NR eMBB devices.
    Reduced maximum bandwidth of single carrier, e.g. 10MHz.
    Support data transmission in in-active mode, e.g. contention-based transmission/grant free.

## Slide 16: Study item/work item of NW-RI
Study the necessary specifications needed for NW-RI:
New I/F for integration of 5G-NR without less WLAN impact
Data distribution/duplication function (DDD) for high-reliability
0 loss/ms (OLM) mobility support

## Slide 17: WIs for continuing topics in Rel-17
The work in the following areas should be supported in Rel-17,
WI for further enhancement of MIMO/eMBB, including
  Leftovers of Rel-16, i.e. multi-TRP transmission for URLLC
  Enhancement of beam management, aiming at overhead reduction and flexibility improvement.
  MIMO uplink enhancement, e.g. frequency-selective precoding, improved beam management mechanism, and enhanced codebooks and control signaling for improving DL-UL reciprocity operation.
WI for further enhancement of URLLC/IIoT, including
  Study/enhance URLLC over FR2 (not including multiple-TRP scenario).
  Study/enhance URLLC in TDD scenarios.
  Enhance URLLC transmission mechanism for improving PHY layer transmission efficiency to further increase data rates and/or number of URLLC users simultaneously served by one gNB.
  Increase the efficiency of the coexistence scenario of URLLC/IIoT traffic and eMBB traffic.
  Leftovers of Rel-16 (if any).

## Slide 18: WIs for continuing topics in Rel-17 (Cont’)
The work in the following area should be supported in Rel-17:
WI for NR-U enhancement, including
  Optimize the performance when NR-U gNBs are deployed in a standalone mode.
  Support NR-U gNB works as a master gNB.
  Optimize NR-U from the point of view to utilize NR-U carrier provide IoT/vertical services.
  Rel-16 leftovers (if any).
  Possibly extend NR-U to the band beyond 52.6 GHz (after SI(s) for beyond 52.6GHz).
SI/WI for enhancement of V2X (D2D), including
  Enhance V2X to increase the reliability, latency, transmission efficiency of Rel-16 sidelink.
  Further develop Rel-16 sidelink to support other D2D services not based on V2X, e.g. public safety.