## Slide 1: 3GPP TSG-RAN Meeting #84 Tdoc RP-190966 Newport Beach, California, USA, June 3rd – 6th 2019 Agenda Item: 8 – Proposals for Release 17 Source: Ericsson On Rel-17 Aerials work scope

## Slide 2: Background
Serving aerial vehicles via cellular networks a significant opportunity
  Amount of aerial vehicles are expected to grow at the same time as NR is deployed
NR features ultra-lean transmissions, low latency support, and spectrum flexbilities
  Potentially very well suitable for the aerial use case
A Study Item followed by a RAN2-lead Work Item was done for LTE in Rel-15
  TR 36.777 captures the findings of the Study Item
  The Work Item centered on improving the efficiency and robustness for the aerial use-case
  Features were introduced concerning:
    Subscription-based identification of Drone authorized users
    Reporting of height, location, flight path plan and measurement report triggering of multiple cells
    UE-specific power control

## Slide 3: Overall directions
Follow up the LTE Rel-15 SI/WI to introduce features to ensure that the aerial use-case is supported in 5G NR systems from an early release
Introduce features that allow for drone in NR networks with small impacts on baseline deployments
Focus on the holistic view; i.e from drone take-off to the skies to landing again
  Support of both idle mode and connected mode mobility

## Slide 4: Possible use cases
Drones in rescue areas
  Drone sent to rescue area as a first respondant to provide situational awareness
Automated flights for service purposes (e.g. Package delivery)
Monitoring of critical infrastructure
Flying cameras

## Slide 5: Key design topics
Key problems to address are interference, mobility and network-awareness of drone status
The main technical areas are
  Idle mode [RAN2]
    Idle mode mobility enhancements such as broadcasting height thresholds for flying mode states similar to mobility states
  Connected mode [RAN2]
    RRM measurement parameter scaling (e.g. Time-to-trigger)
    Controlling the amount of RRM measurement reporting
  Aerial-specific reporting [RAN2]
    Height, location and flight path reporting