## Slide 1: mMTC Evolution in Rel 17
NR mMTC Evolution and
LTE-M/NB-IOT Evolution

## Slide 2: NR mMTC Rel 17 Evolution
Proposal: Approve a Rel 17 NR mMTC Study Item
    Duration all of Rel 17
    Targeted normative work starting in Rel 18
Study should at least include:
    Use cases and requirements
    Complexity reduction techniques
    Power consumption reduction techniques
    Coverage enhancement techniques
    Capacity enhancement techniques
Delicate balance between complexity vs capabilities and target markets

## Slide 3: NR mMTC Rel 17 Evolution
NR mMTC solution MUST be complementary
  mMTC market has a wide capability vs complexity range
  Large gap between LTE-M/NB-IOT and NR eMBB e.g. HD video
  LTE-M/NB-IOT must continue to be seen as the ONLY 5G LPWA solution
Capability
(speed, latency, …)
Complexity
(Cost, Size, …)
NR eMBB
NB-IOT
LTE-M
NR
mMTC
LPWA
eMBB

## Slide 4: NR mMTC Rel 17 Evolution
Use case and requirements e.g.
    UE configuration - Support Worldwide SKU , focus on HD-FDD and TDD
    Band support - focus on FR1 including unlicensed.
    Support SA or NSA or both
    Data Rates - Cell Edge Rate >10 Mbps
    Latency requirements, Spectral Efficiency,
    Battery life – focus on good idle mode performance
    Coverage requirements – only useful if cell edge min throughput can be maintained
Study possible complexity reductions e.g.
    Reduce some mandatory features e.g. SCS, antennas
    Latency and speed
    Minimum bandwidth - encourage to reuse NR SSB and beam management
    Lower power class
Sierra’s View in Blue Italics

## Slide 5: NR mMTC Rel 17 Evolution
Study power consumption reduction techniques (beyond those already studied) e.g.
    Idle mode improvements: eDRX, PSM, Wake-up Signal, Go-to-sleep signal
    RRC connection reduction techniques: Pre-allocated resources, EDT, Release Assistance
Study Coverage enhancement techniques e.g.
    Repetitions – within constraint of minimum data rate
    Interleaving, RV cycling, RV repetition, HARQ enhancements
Capacity enhancement techniques e.g.
    Sub-PRB, modulation order, MIMO, NOMA, EDT

## Slide 6: LTE-M/NB-IOT Rel 17 Evolution
Proposal: Careful selection of a limited number of Rel 17 features
    (i.e. a very smaller WID or even no WID)
Commercialization is well behind standardization
    Many release 13 features are still being commercialized
    The 3 evolution releases (14,15,16) have addressed the missing features and concerns
    Historically, commercialization beyond 3 releases is very low
Lifecycle or longevity is a KEY requirement for this market
    Continue to promote:
      LTE-M/NB-IOT are the ONLY 5G LPWA solutions
      NR will not deprecated LTE-M/NB-IOT
    Co-existence with NR is critical to support that messaging

## Slide 7: LTE-M/NB-IOT Rel 17 Evolution
High-level feature selection criteria
  Avoid features that …
    Require new UE silicon or module H/W changes
    Reduce the complementary nature of LTE-M and NB-IOT
    Require new UE categories => slows market adoption
  Accept features that …
    Improve NR co-existence (remain items from Rel 16)
    Are well defined with limited scope

## Slide 8: Thank you
13811 Wireless Way :: Richmond, British Columbia, Canada, V6V 3A4
sierrawireless.com