## Slide 1: On FR2 UE Tx Spurious Emission requirements
Intel
3GPP TSG-RAN Meeting #84 RP-191029
Newport Beach, CA USA, June 3rd – 6th, 2019
Agenda Item: 9.2.1
Document for: Approval

## Slide 2: Background
CEPT (The European Conference of Postal and Telecommunications Administrations) finalizes its recommendation 74-01 [1] based on spectrum sharing and compatibility studies [2].
  Spurious emission limits for terminals operating above 24.25 GHz using AAS and beamforming with integrated antennas with following emission limits (see 2.1.8, highlighted)
A2.1 LIMITS
Table 1: Spurious domain emission limits for the land mobile service, maritime mobile service and short range devices
Reference number | Type of equipment | Frequency of the spurious domain emission f | Limits: mean power or, when applicable, average power during bursts duration in the reference bandwidth
… |  |  | 
2.1.7 | Base Stations using AAS and beamforming with integrated antennas operating above 24.25 GHz (Note XX) | 9 kHz  f  1 GHz | -36 dBm (Note 4) (Note XX)
 |  | 1 GHz < f  18 GHz | -30 dBm (Note 4) (Note XX)
 |  | 18 GHz < f  Fupper (see recommend 3) | -20 dBm/10 MHz (other limits apply for specific frequency separations, see Figure 7) (Note 4)
2.1.8 | Terminals operating above 24.25 GHz using AAS and beamforming with integrated antennas | 9 kHz  f  1 GHz | -36 dBm (Note 4)
 |  | 1 GHz < f  7.25 GHz | -30 dBm (Note 4)
 |  | 7.25 GHz < f  Fupper (see recommend 3) | -13 dBm/MHz and -10 dBm/100 MHz (Note 4) (Note 5)

## Slide 3: Background
3GPP (38.101-2) specifies -30dBm/MHz emission limit in 1GHz f <12.75GHz.
FCC has -13dBm/MHz emission limit in spurious domain in all frequency range [3]
CEPT specifies -13dBm/MHz above 7.25GHz with additional -10dBm/100MHz limit
A comparison with key difference in highlighted frequency range between 3GPP and CEPT
Frequency range | 3GPP 38.101-2 Tx emission limit | CEPT emission limit | FCC emission limit
9KHz f30MHz | N/A | -36dBm (See reference BW recommend 3 in appendix) | -13dBm/MHz
30MHz f1GHz | -36dBm/100KHz | -36dBm/100KHz | -13dBm/MHz
1GHz f7.25GHz | -30dBm/MHz | -30dBm/MHz | -13dBm/MHz
7.25GHz f12.75GHz | -30dBm/MHz | -13dBm/MHz and -10dBm/100MHz | -13dBm/MHz
12.75GHz f2nd harmonic | -13dBm/MHz | -13dBm/MHz and -10dBm/100MHz | -13dBm/MHz
2nd harmonic f | N/A | -13dBm/MHz and -10dBm/100MHz | -13dBm/MHz
Frequency range | 3GPP 38.101-2 Tx emission limit | CEPT emission limit | FCC emission limit
 | N/A | -36dBm (See reference BW recommend 3 in appendix) | -13dBm/MHz
 | -36dBm/100KHz | -36dBm/100KHz | -13dBm/MHz
 | -30dBm/MHz | -30dBm/MHz | -13dBm/MHz
 | -30dBm/MHz | -13dBm/MHz and -10dBm/100MHz | -13dBm/MHz
 | -13dBm/MHz | -13dBm/MHz and -10dBm/100MHz | -13dBm/MHz
 | N/A | -13dBm/MHz and -10dBm/100MHz | -13dBm/MHz
Table 1 Spurious emission limit comparison among 3GPP, CEPT and FCC
Note: The ‘’ and ‘<’ sign are not differentiated here for presentation purpose. The exact signs for each frequency segment should reference to corresponding spec or regulations.

## Slide 4: Observations and proposals
Observation 1: CEPT has different spurious emission requirements above 7.25 GHz for FR2 UEs from 3GPP.
Observation 2: CEPT emission limits are specified based on spectrum sharing and compatibility studies [2]
IF frequency above 6GHz is commonly used in mmWave UEs’ implementations to provide signal transformation between baseband and carrier frequency:
  CEPT emission limits make common architecture using IF frequency for mmWave devices more feasible
  Existing 3GPP requirement may unnecessarily tight emission limit of-30dBm/MHz from 7.25GHz to 12.75GHz
Proposal 1: RAN4 should align with CEPT on Tx spurious emission limits in 38.101-2 in Rel-15
Observation 3: Certain national/regional regulations have already adopted current 3GPP FR2 Tx spurious emission limits
Considering observation 3, we propose
Proposal 2: Add national/region regulations for spurious emission requirements as additional spurious emission requirements with NS signaling in 38.101-2 in Rel-15

## Slide 5: Proposed CR to 38.101-2
A accompanying CR has been submitted to this meeting
General spurious emission limit changes (text in red)
Frequency Range | Maximum Level | Measurement bandwidth | NOTE
30 MHz  f < 1000 MHz | -36 dBm | 100 kHz | 
1 GHz  f < 12.75 7.25 GHz | -30 dBm | 1 MHz | 
12.75 7.25 GHz ≤ f ≤ 2nd harmonic of the upper frequency edge of the UL operating band in GHz | -13 dBm | 1 MHz | 
 | -10dBm | 100MHz | 
Table 6.5.3-2: Spurious emissions limits
Add additional spurious emission limits with new NS_202 and CA_NS_202 (text in red)
Frequency Range | Maximum Level | Measurement bandwidth | NOTE
30 MHz  f < 1000 MHz | -36 dBm | 100 kHz | 
1 GHz  f < 12.75 GHz | -30 dBm | 1 MHz | 
12.75 GHz ≤ f ≤ 2nd harmonic of the upper frequency edge of the UL operating band in GHz | -13 dBm | 1 MHz | 
Table 6.5.3.2.3-1: Additional requirements (NS_202 and CA_NS_202)

## Slide 6: Proposed CR to 38.101-2
Add NS_202 for single CC UL and CA_NS_202 for CA UL (text in red)
  mandatary for all FR2 Bands (including new bands in the future)
No impact on RAN2 specifications, 8 NS signaling can be supported for each band
Network Signalling label | Requirements (subclause) | NR Band | Channel bandwidth (MHz) | Resources Blocks (NRB) | A-MPR (dB)
NS_200 |  | Table 5.2-1 |  |  | N/A
NS_201 | 6.5.3.2.2 | n258 |  |  | 6.2.3.2
NS_202 | 6.5.3.2.3 | Table 5.2-1 |  |  | N/A
NR Band | Value of additionalSpectrumEmission |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
n257 | NS_200 |  | NS_202 |  |  |  |  | 
n258 | NS_200 | NS_201 | NS_202 |  |  |  |  | 
n260 | NS_200 |  | NS_202 |  |  |  |  | 
n261 | NS_200 |  | NS_202 |  |  |  |  | 
NOTE: additionalSpectrumEmission corresponds to an information element of the same name defined in sub-clause 6.3.2 of TS 38.331 [13]. |  |  |  |  |  |  |  | 
Table 6.2.3.1-1: Additional maximum power reduction (A-MPR)
Table 6.2.3.1-2: Mapping of Network Signaling label
Network Signalling value | Requirements (subclause) | NR Band | Channel bandwidth (MHz) | Resources Blocks (NRB) | A-MPR (dB)
CA_NS_200 |  | Table 5.2-1 |  |  | N/A
CA_NS_201 | 6.5.3.2.2 | n258 |  |  | 6.2A.3.2
CA_NS_202 | 6.5.3.2.3 | Table 5.2-1 |  |  | N/A
Table 6.2A.3.1-1: Additional maximum power reduction (A-MPR)
NR Band | Value of additionalSpectrumEmission / NS number |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
n257 | CA_NS_200 |  | CA_NS_202 |  |  |  |  | 
n258 | CA_NS_200 | CA_NS_201 | CA_NS_202 |  |  |  |  | 
n260 | CA_NS_200 |  | CA_NS_202 |  |  |  |  | 
n261 | CA_NS_200 |  | CA_NS_202 |  |  |  |  | 
NOTE: additionalSpectrumEmission corresponds to an information element of the same name defined in clause 6.3.2 of TS 38.331 [13]. |  |  |  |  |  |  |  | 
Table 6.2A.3.1-2: Value of additionalSpectrumEmission

## Slide 7: References
ERC Recommendation 74-01
ERC Recommendation (19)02, “Unwanted Emissions – Guidance and methodologies when using typical equipment performance in sharing/compatibility studies”.
FCC Code of Federal regulations (CFR), Title 47, telecommunications, Part 30.203