## Slide 1: 3GPP TSG-RAN Meeting #84 Tdoc RP-191053 Newport Beach, California, USA, June 3rd – 6th 2019 Agenda Item: 8 Source: Ericsson On Rel-17 Public Safety

## Slide 2: Public Safety Scenarios and Requirements
Scenarios
    Within terrestrial cellular network coverage or partial network coverage
      E.g., urban indoor fire fighting
    Without terrestrial cellular network coverage
      E.g., forest fire fighting in a remote mountain area 20 miles from the nearest network, search and rescue in a disaster area
Requirements
  Mission Critical Service Requirements [MCPTT (TS 22.179), MCData (TS 22.281), MCVideo (TS 22.282) and MCCoRe (TS 22.280)]
    One-to-one and one-to-many communications
    Low latency, high availability and reliability
    Priority and pre-emption
    In-coverage and out-of-coverage operation modes
  Accurate positioning [TR 22.872, TS 22.261]
  Energy efficiency [TS 22.261]

## Slide 3: 3GPP for Public Safety
3GPP LTE RAN started adding features to support public safety communication services since Rel-11
    High Power UE for Band 14 [TS 36.101, TR 36.837]
    D2D (Proximity-based services) [TS 23.303]
    Multicast and broadcast [TS 22.468 , TR 36.890]
  Some necessary components for public safety already covered in 3GPP NR RAN Rel-15/16
    One-to-one and one-to-many communications
      Rel-15/16 Regular NR Uu in cellular network coverage
      Rel-16 V2X/SL for direct communications in and out-of-coverage
    Rel-16 Single/multi-hop IAB relaying for cellular network coverage extension
    Rel-16 positioning for emergency calls
  Public safety related SA2 new SIs
    Study on System enhancement for Proximity based Services in 5GS [SP-190186]
    Architectural enhancements for 5G multicast-broadcast services [SP-190253]

## Slide 4: NR Rel-17 for Public Safety
Additional necessary components covered in separate items
  Sidelink
    UE-to-UE relay for NLOS out-of-coverage scenarios
  Multicast and Broadcast
    For efficient group communications (call/data/video) within terrestrial cellular network coverage
  IAB
    Portable/mobile IAB for “cells on wheels/wings” or ad-hoc/temporary networks
    Enhancement for coverage extension in rural areas at low frequency (UE-to-Network relay)
  Drones
    For improving situational awareness, e.g., send drones to the rescue area first while the first responders are on their way, real-time video delivering
  Positioning
    For infrastructure-less accurate 3D positioning for first responders, e.g., a burning residential building with broken power supply
Cells on wheels
UE
UE
UE
UE
gNB
UE
UE

## Slide 5: Conclusions and References
No dedicated SI/WI needed for public safety
    Leverage on as many synergies as possible with MBB to support the PS use case
    Additional necessary components for PS can be covered in separate Rel-17 study/work items, e.g., SL, multicast/broadcast, IAB, drones, positioning, etc.
  Detailed discussions can be found in our contributions
    RP-191054 NR Rel-17 Sidelink Features
    RP-191169 Introduction of Broadcast/Multicast for NR
    RP-190971 On Rel-17 IAB scope
    RP-190966 On Rel-17 Aerials work scope