## Slide 1: Way Forward on PDCCH Skipping
Apple Inc.
3GPP TSG RAN Meeting#84
Newport Beach, USA, June 3-6, 2019
RP-191109
AI 9.4.6

## Slide 2: Background (1)
RAN1 completed UE power saving SI in RAN#83, RAN2 continued the SI until RAN#84
R16 UE Power Saving WID with partial RAN1 centric scope was approved in RP-190727 in RAN#83
The objectives are subject to further update in RAN#84. The update will be based on recommendations from the completion of RAN2 study and remaining RAN1 recommendations based on the conclusion of RAN1 study (copied from RP-190727)

## Slide 3: Background (2)
RAN1 study shows the benefit of PDCCH Skipping (copied from TR38.840 ):
  Reduction of PDCCH monitoring can also be achieved with explicit/implicit information for UE to skip monitoring PDCCH. A related approach, such as power saving signal/channel triggering/enabling PDCCH monitoring or "go-to-sleep" signaling where the gNB can signal the UE to go to the DRX OFF state or skip the PDCCH monitoring, is considered. Power saving gain in the range of 9%~83% is observed, with latency increase in the range of 0.1%~75% and overhead of 0% - 1% with one source showing 124% latency increase. Generally, the gain is higher for scenarios with CDRX configuration with larger DRX inactivity timer duration and for lower traffic load, and higher latency increase is associated with higher gain.

## Slide 4: Background (3)
RAN2 study shows the minimum MAC impact on PDCCH Skipping, if any (copied from TR38.840)
  The common understanding is that such feature should be a physical layer procedure with minimal impact, if any, on the MAC layer.
  DCI-based PDCCH monitoring skipping is aimed to operate on a short time scale (i.e. shorter time scale then the L2 DRX). Under this condition, it has not been identified that DCI-based PDCCH monitoring skipping duplicates the DRX functionality.
  If enabled, it is assumed that DCI-based PDCCH monitoring skipping can be configured with or without DRX.

## Slide 5: Proposal
Support PDCCH skipping in RRC_CONNECTED mode in Rel-16.

## Slide 6: Thanks!