## Slide 1: Motivation of D2D support in Rel-17
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #84 RP-191143
Newport Beach, USA, June 3-6, 2019

## Slide 2: Vision of 5G
5G is expected to change every aspects of modern society
  Smart city, education, health, industry, transportation, environment, entertainment, finance, agricultures…
Agriculture
Health
Education
Transportation
Finance
Environment
Wearable devices
Home
AR
VR
Entertainment
Cloud
Mobile device
Industry

## Slide 3: Rel-17 D2D Direct Communication and Discovery
User-oriented system evolution –
  Better user experience is one important aspects in marketing NR and further development
  Enhancement of Sidelink for D2D
    Direct communication –
      Achieve high data rate and low latency
      Increase the radio resource reuse through sidelink
    Discovery –
      Support of applications of proximity services (e.g., social media, peer discovery)
      Assistance in coverage extension of direct communication
Extended 5G vertical domain through sidelink enhancement for D2D
  D2D communications between different devices types
  Extended user applications through D2D direct communication

## Slide 4: Requirements for D2D
Spec | Requirements
TS22.278 | D2D discovery for both commercial and PS services should be supported; D2D communication should be supported at least for PS services.
TS22.261 | UE-to-network relay should be supported: Connection between remote UE and relay UE can be 3GPP RAT or non-3GPP RAT； UE using simultaneous indirect and direct network connection should be supported; Connection between remote UE and relay UE can be licensed or unlicensed band; 5G system with satellite access should be considered.
TS22.125 | D2D broadcast communication should be supported for UAV: Support direct UAV to UAV local broadcast communication at relative speeds of up to 320kmph with variable message payloads of 50-1500 bytes.

## Slide 5: Sidelink Enhancement for D2D
NR proximity service requirements | Sidelink Enhancement for D2D
Sidelink discovery | The sidelink discovery requirements in V2X is limited to application triggered peer discovery for unicast and groupcast For commercial cases (e.g. advertisements) or public safety cases (e.g., disaster alarm), the discovery message needs to be transmitted frequently. Efficient resource utilization is essential.
UE-to-network and UE-to-UE relay | UE-to-network and UE-to-UE relay are essential in extending the range of the communication. There is clear requirement of relay from SA2.
Sidelink communication | D2D has different deployment scenarios and requirements compared with those of V2X. The D2D deployment scenarios are mostly indoor with low mobility and high penetration loss. The power consumption needs to be low for D2D comparing to that of V2X. The sidelink link adaptation and interference management for D2D are different to those of V2X.

## Slide 6: Motivation of NR sidelink for D2D
SA2 requirements of sidelink enhancement for D2D
  TS22.278 defined requirements on discovery for both commercial and PS
    Discovery procedure and related messages are up to upper layers in NR V2X
  TS22.261 defines requirement on support of UE-to-Network relay
    UE relaying resource (pool) configuration is not supported in Rel-16 V2X work
Sidelink Enhancement
  Evaluation of deployment scenarios of D2D for public safety and commercial services
    Indoor scenarios with large penetration loss
    Outdoor scenarios with extended coverage
  Sidelink enhancement in support of D2D communication –
    Coverage extension – PSSCH beamforming
    Higher data rate - multi-antenna operation and carrier aggregation
  D2D proximity discovery
    D2D discovery in support of applications (e.g., social media)
    D2D discovery to assist direct communication – network-to-UE and UE-to-UE relay
    Multi-carrier discovery – NR and LTE discovery
  Device power saving

## Slide 7: Objectives of NR Support of D2D
Objectives of NR support of D2D
  Evaluation of deployment scenarios of D2D for public safety and commercial services
    Indoor scenarios with large penetration loss
    Outdoor scenarios with extended coverage
  Extend the V2X SL framework to support D2D services for PS and commercial use cases
    Optimization of NR resource utilization through direct communication
  Study the sidelink enhancement in support of coverage extension of D2D direct communication
    UE-to-network relay -
      Multiple connectivity of UE-to-Network relay
    UE-to-UE relay
    Sidelink beamforming and beam management for FR1 and FR2
  Study the enhancements of sidelink MIMO schemes for high data rate D2D direct communication
  Study D2D proximity discovery
    Study NR sidelink physical layer structures, procedure(s), and L2/L3 protocols for D2D proximity discovery in single and multi-carrier
    Study the interaction between NR D2D discovery and LTE D2D discovery
    Study the D2D proximity discovery in assistance of UE-to-network relay and UE-to-UE relay
  Study the device power saving techniques for D2D discovery and directly communication