## Slide 1: Motivation of NR Positioning Enhancements in Rel-17
RP-191147
3GPP TSG RAN WG Meeting #84
Newport Beach, California, USA
June 3 – 6, 2019
Agenda Item: 8
China Academy of Telecommunications Technology (CATT)

## Slide 2
In RAN#83, R16 NR Positioning SI was completed and R16 NR Positioning WI was started.
  Target regulatory and commercial performance requirements for R16 were defined
  Three NR positioning evaluation scenarios (Indoor office, UMi, UMa) were defined for system level analysis
  It was concluded feasible to achieve the target regulatory and commercial target performance requirements for horizontal positioning accuracy for the evaluation scenarios
  On-going R16 NR Positioning WI focuses on the RAT-dependent positioning techniques recommended by R16 NR Positioning SI, namely, DL-TDOA, DL-AoD, UL-TDOA, UL-AoA, RTT and E-CID
R16 NR Positioning SI/WI

## Slide 3
Motivations of R17 NR Positioning Enhancements
5G positioning performance requirements
Absolute positioning
  Horizontal: accuracy 10m to 0.3m with 95% confidence and 95% to 99.9% availability
  Vertical: 3m to 2m with 95% confidence and 95% to 99.9% availability
Relative positioning
  Horizontal: 0.2m with 95% confidence and 99% confidenceVertical: 0.2m with 95% confidence and 99% confidence
Time latency (time to first fix): from seconds to ms
  Target R16 positioning performance
  Horizontal positioning error < 3m (80%) (indoor ) and < 10m (80%) (outdoor)
  Vertical positioning error < 3m (80) (indoor) and error < 3m (80) (outdoor)
  Time latency (time to first fix) < 1 second
Huge gap between R16 target positioning performance identified [TR 38.855] and the 5G positioning performance requirements [TS 22.261] in terms of positioning accuracy, availability and confidence level, etc.
Very little effort spent on vertical positioning in R16, although the vertical positioning accuracy was included in R16 performance target
Huge gap

## Slide 4
5G NR positioning needs to support more use cases with greater accuracy and scalability beyond R16 (High-speed UEs, etc.)
Many promising techniques for positioning enhancements were actually proposed during R16 NR Positioning SI [TR 38.855], but not adopted due to very tight time schedule, e.g.,
  NR Carrier phase based positioning
  Multipath mitigation techniques, such as LOS detection, multiple measurements reporting for both delay and angle information
  Phase difference of arrival based positioning
  Received signal waveform reporting
  Cooperative positioning
  NR Positioning for UEs in RRC_IDLE/INACTIVE modes
  Positioning techniques with low complexity in UE implementation
Motivations of R17 NR Positioning Enhancements

## Slide 5
RAN1 centric objectives
  Identify the target commercial use cases and the performance requirements for NR positioning enhancement according to 5G positioning services defined in TS 22.261 and TS 22.104 [RAN1]
  Extend R16 NR positioning evaluation scenarios for evaluating the identified commercial use cases [RAN1]
  Investigate advanced techniques for positioning enhancements with the consideration of accuracy, availability, reliability, scalability, TTFF etc. The NR positioning enhancements to be investigated may include, but not limited to, the positioning techniques proposed during Rel-16 SI/WI [RAN1]
  Extend downlink and uplink positioning reference signals, and if necessary, define new downlink and uplink positioning reference signals, for supporting the positioning enhancements [RAN1]
  If necessary, define new the UE and gNB positioning measurements supporting the positioning enhancements [RAN1]
  If necessary, define new physical-layer procedures to support UE/gNB measurements supporting the positioning enhancements [RAN1]
Objectives of R17 NR Positioning Enhancements

## Slide 6
RAN2 centric objectives
  Extend the functional interfaces, signalling and procedures including UE reporting, to support NR RAT-dependent positioning for the NR positioning enhancements listed in RAN1 objectives [RAN2]
  Define extensions of LPP protocol for NR RAT-dependent positioning enhancements [RAN2]
RAN3 centric objectives
  Define extensions of LPPa protocol for NR RAT-dependent positioning enhancements [RAN3]
RAN4 centric objectives
  Define corresponding core requirements for NR positioning enhancements [RAN4]
  Define corresponding performance requirements and test cases for NR positioning enhancements [RAN4]
Objectives of R17 NR Positioning Enhancements