## Slide 1: Motivation of Further MIMO Enhancements in Rel-17
CATT
RP-191148
3GPP TSG RAN WG Meeting #84
Newport Beach, California, USA
June 3 – 6, 2019
Agenda Item: 8

## Slide 2: Motivation
UL MIMO performance is lagging behind DL
  The core features of NR UL MIMO are inherited from that of LTE
  No major UL enhancement over years and the UL system has been stagnant over several releases (LTE and NR)
  Limited UL coverage and lower throughput compared to DL, potential performance bottleneck
UL MIMO enhancement motivated by
  New deployment scenarios
  New use cases
  New carrier frequency
  New system bandwidth

## Slide 3: New deployment Scenarios
Beyond 52.6GHz:
  Higher dimension digital MIMO precoding due to reduced wavelength and more compact antenna array
  Advanced analog beamforming with greater number of beams, coverage, flexibility, and overhead reduction
Ultra-high-density scenario
  Very high user density and low mobility
  Very high UL data rate requirement due to e.g. video surveillance, uploading, AR/VR, wireless data center access etc
IAB:
  Higher-order MIMO (e.g. beyond 4Tx) to achieve high data rate
V2X:
  Multi-beam related enhancements in FR2 e.g. panel TX identification and selection, fast RX panel/RSU selection and switching

## Slide 4: New Deployment Scenarios
Multi-panel UE
  NR currently only supports single panel UL transmission, to a single TRP
  Enhancement on multi-panel joint transmission, potentially to one or different TRP, are promising for spectral efficiency and link robustness
  Applicable in eMBB and URLLC
Indoor deployment
  Frequency-selective precoding due to much wider system bandwidth than LTE
AI & ML
  Network operation is becoming too complicated as the number of configuration parameters keep increasing;
  RAN-side overhead causing severe congestion/latency/interference
  A decentralized network topology, toward self-learning, prediction, and adaptation toward better energy-efficiency, overhead reduction, faster and more agile beam management

## Slide 5: Potential Enhancement Areas
UL frequency selective precoding
Higher-order UL-MIMO beyond 4Tx
  (e.g. V2X UE/RSU, IAB, beyond 52.6GHz), including SRS and PUSCH enhancements
Higher-order MU-MIMO
  Targeting ultra-density indoor deployment
Beam management enhancements with multi-panel TX and multi-panel/TRP RX
  Targeting FR2 considering multi-panel, multi-site and multi-RSU scenario
Study and evaluate decentralized network topology, protocol and interfaces that enable self-learning, prediction and adaptation based on AI/ML
  Targeting overhead reduction (e.g. RS overhead, CSI/beam management overhead) as a first stage

## Slide 6: Draft Rel.17 Enhancement Scope
Evaluate, identify and specify UL MIMO enhancements in both digital and analog beamforming
  Specify frequency-selective UL precoding
  Specify higher-dimension UL-MIMO beyond 4port (e.g. V2X UE/RSU, IAB, beyond 52.6GHz), including SRS and PUSCH enhancements
  Specify advanced analog beamforming targeting FR2 considering multi-panel, multi-site and multi-RSU scenario
    Fast TX panel identification, switching, coordination, including possibly multi-panel coherent joint transmission
    Fast Rx panel/TRP selection and switching at network side (e.g. V2X RSU selection)
  Evaluate and specify, if sufficient gain is found, higher-order UL MU-MIMO targeting ultra-density indoor deployment
Study decentralized network topology, protocol and interfaces that enable self-learning, prediction and adaptation based on AI/ML