## Slide 1: Agenda Item : 8 Source : Samsung Title : Further Enhancement on MIMO for NR: Motivation Document for : Discussion and Decision
3GPP TSG RAN meeting #84 RP-191177
Newport Beach, USA, June 3-7, 2019

## Slide 2: Key areas for MIMO enhancement in Rel.17
Main theme: to enable new use cases, driven by potential needs from real deployment scenarios, such as
  Improved and more diverse scenarios for FR2
  Improved UL coverage (as well as throughput)
Enabling new use cases over Rel.16
  Overall efficiency of multi-beam operation – especially reducing overhead and latency
  UL throughput and coverage enhancement via:
    Enhanced support for UE multi-panel, and
    UL SU-MIMO including DL-UL reciprocity
Rel.15/16 left-over issues on multi-TRP enhancement
  Remaining issues (if any) for PDSCH and/or PDCCH
  Other channels: PUSCH, PUCCH

## Slide 3: Multi-beam operation with lower overhead & latency
FR2 is a relatively new frequency band for mobile applications
  Typically common use case is Fixed Wireless Access (FWA), e.g. indoor
  Rel.15/16 NR beam management may benefit from foundational enhancements to better support “extended” and potentially challenging use cases
Examples of “extended” use cases for multi-beam operation:
  Dense urban with high-speed UEs @FR2 (e.g. highway scenarios):
    Reduced overhead and latency for beam (re)selection to mitigate beam failure events
    Minimize involvement of higher-layer (especially RRC)
  Future extension @ FR4:
    Larger number of narrow beams to overcome increased path-loss
    Efficiency in beam selection becomes more important

## Slide 4: Multi-beam operation with lower overhead & latency
Simplified framework: as flat (vs. hierarchical) as possible, e.g.
  Avoid unnecessary abstraction, e.g. port vs. resource vs. resource set
  More dynamic and reliable beam selection for CONNECTED UEs
    Mobility, propagation condition, traffic
    “Interference awareness” becomes more important
  Enabling much simpler MIMO operation especially @FR2
Is this NR hierarchy necessary? Does it really reduce overhead?
  Beam (cf. BM) vs. measurement (CSI-RS) port
  CSI-RS resource vs. CSI-RS resource set (does it simplify QCL?)
  CSI-RS resource vs. CSI-RS port?
    # ports, T-F resource/location
    Hence CSI-RS resource vs. CSI-RS port
  BM vs. CSI acquisition?
  More hierarchy  RRC (“top”) heavy
Beam failure recovery (BFR): minimizing its overhead/latency vs. minimizing its usage?
  Will BFR (known for imposing high overhead/latency) be used frequently if beam selection can be more reliable and dynamic?

## Slide 5: UL enhancement: UL multi-panel support
Some study on the following issues has taken place in Rel.16 on the following aspects
  Specification entity associated with panel as a functional entity
  Possible use cases
  Options for panel-specific beam indication and relevant issues
  Note: Rel.15 specification facilitates spec-transparent use of UE multi-panel array for reception and transmission
Goals and plan for Rel.17:
  Start with study on the following:
    Potential use cases, especially “extended” use cases over Rel.15 (application and transmission schemes)
    Potential spec-based enhancements and their benefits over Rel.15
  Then identify specification features and their details for Rel.17 (and after)

## Slide 6: UL enhancement: UL multi-panel support
Transmission schemes:
  Focus on fast panel switching/selection (FPS) and simultaneous TX over multi-panel (STxMP)
  Both FPS and STxMP facilitate diversity-based transmission
  STxMP can also be used for spatial multiplexing
Potential use cases (applications) for general UL coverage enhancement
  Overhead and latency reduction
    Reduce occurrence of BFR: especially relevant since UL is the weaker link
    UL diversity gain, e.g. panel selection, CDD over panels
  Mitigating UL coverage loss due to maximum permission emission (MPE) regulation
    Spec-transparent solutions may already use multi-panel to minimize transmit power reduction via duty cycle or back-off
    PHY layer spec support could be beneficial to further ensure that the regulation is met without large UL coverage penalty
  Gain from spatial multiplexing can be studied but is unclear in general

## Slide 7: Enhancement for Multi-TRP: Rel.15/16 unaddressed issues
Multi-TRP transmission for high reliability and low latency
  Verify evaluation methodologies including performance metrics to study potential gain from PDSCH (leftover from Rel-15/16)/PDCCH/PUSCH/PUCCH
    Include both FR1 and FR2
    Note: Evaluations in TR38.824 had been done for CF 4GHz and 700MHz
  Study (and specify, if needed) CSI enhancements (over Rel-15 in case of no enhancements from Rel-16)
  Further enhancements on A/N feedback for both joint/separated UCIs
  Consider up to 8 Rx antenna ports at UE side
    Study performance gain from larger numbers of cooperative measurement/transmission set size
2 TRPs
3 TRPs
1x
3 TRPs
1.8x
Mean UPT
2.6x
95% UPT
UPT gains from larger number of cooperative TRPs

## Slide 8: UL SU-MIMO
General UL coverage and throughput enhancement for FDD:
  TPMI signaling for frequency selective precoding with two-part DCI
    Variable subband TPMI payload for part 2
  Dual-stage codebook for at least 4 SRS ports
High resolution precoding for systems with DL-UL (partial) reciprocity
  TPMI functions as a W1 indicator for UE to calculate W=W1C for each scheduled PRB
  Achieving “unquantized Type II CSI” (hi-res) performance for UL
  Small overhead – only requires indication of “precoder group” W1

## Slide 9: UL MIMO: frequency selective (FS) precoding
Chart: 4Tx UL CB
| Avg. UPT | 5% UPT
N = 1 | 1 | 1
N = 2 | 1.0203 | 1.0198
N = 4 | 1.1024 | 1.3261
N = 6 | 1.1716 | 1.4739
N = 8 | 1.2165 | 1.7279
Chart: 4Tx UL CB
| Payload
N = 1 | 5
N = 2 | 10
N = 4 | 20
N = 6 | 30
N = 8 | 40
Chart: NR Type I 4Tx CB, L = 1
| Avg. UPT | 5% UPT
N = 1 | 1 | 1
N = 2 | 1.0064 | 1.0414
N = 4 | 1.0909 | 1.2319
N = 6 | 1.1592 | 1.53
N = 8 | 1.2046 | 1.8965
Chart: NR Type I 4Tx CB, L = 1
| Payload
N = 1 | 5
N = 2 | 7
N = 4 | 11
N = 6 | 15
N = 8 | 19
UMi-4GHz
4Tx: (N1, N2) = (2, 1)
N = 1, 2, 4, 6, 8 TPMIs
FS precoding shows good gain over WB precoding:
  ~20% gain in average user perceived throughput (UPT), and ~70-120% gain in cell-edge UPT

## Slide 10: UL MIMO: Hi-res precoding for reciprocity
Chart: 
| Avg. UPT | 50% UPT | 5% UPT
4Tx UL CB | 1 | 1 | 1
4Tx dual-stage CB | 1.0563 | 1.0649 | 1.378
W1+LC | 1.2684 | 1.4343 | 4.8385
Chart: 
| Avg. UPT | 50% UPT | 5% UPT
8Tx dual-stage CB | 1 | 1 | 1
W1+LC | 1.2323 | 1.3259 | 3.94
Dual-stage codebook shows ~6% and ~38% gain in mean and cell-edge user perceived throughput (UPT), respectively, when compared with 4Tx UL codebook.
For both 4-Tx and 8-Tx, W1+LC (hi-res partial reciprocity) shows good gain over dual-stage codebook:
  ~25% gain in mean UPT and ~4-5x cell-edge UPT
UMi-4GHz
4Tx: (N1, N2) = (2, 1)
8Tx: (N1, N2) = (4, 1)
W1: indicating 4 DFT beams