## Slide 1: Motivation of flexible UL-DL Resource Allocation and Interference Mitigation
3GPP TSG RAN Meeting #84
Newport Beach California, USA, June 3-6, 2019
RP-191295
Source: LG Electronics
Document for: Discussion
Agenda Item: 8

## Slide 2: 1. General Motivation and Scenarios
Motivations
  Better adaptability to the DL/UL resource allocation based on different DL/UL traffics situations
    NR aims to support duplexing flexibility in both paired and unpaired spectrum.
    Rel-16 NR CLI WI covers inter-cell UE-to-UE CLI in a semi-static manner via L3 CLI measurement/report
    In future releases, more dynamic/flexible resource adaptation between DL and UL is necessary, e.g.,
      allowing simultaneous transmission between DL and UL to minimize resource unavailability for URLLC traffic
      supporting different types of traffic demand (e.g., DL/UL-heavy traffic, sporadic data, URLLC traffic) for each UE in a cell
  Better latency by relaxing DL-UL half-duplex constraints
    In Rel-16, gNB – IAB node – UE links are operated with half duplex constraints
    To reduce the latency and relax the half-duplex constrains, more flexible resource allocation and simultaneous Tx/Rx at IAB node should be adopted
  Potential throughput enhancement by allowing in-band simultaneous TX-RX in a same carrier

## Slide 3: 1. General Motivation and Scenarios
Scenarios for potential enhancements
  Distributed RUs with RU-wise independent Tx/Rx
  gNB in-band inter-UE full duplex
  Half duplex based IAB node with SDM/FDM
  Full duplex based IAB node

## Slide 4: 2. Scenarios for Potential Enhancements
gNB in-band full duplex
① Intra-cell TRP to TRP CLI
② Intra-cell UE to UE CLI
Distributed RUs with RU-wise independent Tx/Rx
FDMed Flexible Duplex
① In-band self interference in a gNB
② Intra-cell UE to UE CLI

## Slide 5: 2. Scenarios for Potential Enhancements
Half duplex based IAB node with SDM/FDM and/or Full duplex based IAB node
Half Duplex IAB with SDM/FDM
Full Duplex IAB
③ CLI on access and backhaul link
① In-band self interference in a gNB
③ CLI on access and backhaul link