## Slide 1: On simulation results for 70GHz towards IMT-2020 submission
Intel Corporation
RP-191447
3GPP TSG RAN #84
Newport Beach, USA, June 3 – 6, 2019
AI: 9.3.1

## Slide 2: Background
In email reflector 3GPP_TSG_RAN_AHG1@LIST.ETSI.ORG, there has been a discussion whether or not to include system level simulation results for 70GHz to TR37.910 and IMT-2020 submission.
The TR37.910 and IMT-2020 submission can include the features according to Rel-15/Rel-16 specifications.
The simulation results for 70GHz (FR4?) have used FR2 numerology SCS60 as per Rel-15/16 specification.
  From Intel’s point of view, The simulation results for 70GHz using FR2 numerology SCS60 or 120 are simply wrong since it is not practically feasible.
  It can give a wrong impression that 3GPP NR can support 70GHz carrier frequency by Rel-15/16 specifications.

## Slide 3: Link Level Simulation Parameters
Parameter | Value
Bandwidth | 800 MHz
Subcarrier spacing/ SC chip rate | CP-OFDM: 120/240/480/960/1920kHz subcarrier spacing
Carrier Frequency | 60 GHz
MIMO Configuration | 2x2 with TPMI cycling (Rank 1) from DL codebook
Channel Model | TDL-A 5ns, 3km/h
MCS | QPSK (1/2), 16QAM (3/4) and 64QAM (3/4)
Channel estimation | realistic CE
PN model | 3GPP TR38.803 example 2 PN model
PN compensation method | ideal CPE compensation (CP-OFDM)
Additional RF impairments | Not modeled
PN profile example 2 in [1] is used for LLS
PN profile example 1 in [1] is a interpolated results between PN profile for 45 GHz and 70 GHz.
[1] TR38.803, “Study on New Radio Access Technology: Radio Frequency (RF) and co-existence aspects”
[2] IEEE 802.11-15-0390r1 “Considerations on Phase Noise Model for 802.11ay”
PN profile example 1 from 38.803 showing increase of PN @ 70 GHz compared to 29.55 GHz

## Slide 4: CP-OFDM Link Performance Comparison
Note: Ideal CPE removal is performed by estimating ideal common phase noise for each OFDM symbol and removing them prior to demodulation processing.
SNR (dB)
SNR (dB)
BLER
BLER
Observation: Even with more optimistic PN profile (i.e. Example 2 in previous slide), the current FR2 numerology SCS120 doesn’t work at all even with ideal CPE (Common Phase Estimation).

## Slide 5: IMT-2020 Requirements for Indoor Hotspot
For Indoor Hotspot Test Environment, three IMT-2020 configurations are defined by ITU-R in [1]:
  Configuration A: CF = 4 GHz, Simulation BW = 20 MHz (TDD)/10+10 MHz (FDD)
  Configuration B: CF = 30 GHz, Simulation BW = 80 MHz (TDD)/40+40 MHz (FDD)
  Configuration C: CF = 70 GHz, Simulation BW = 80 MHz (TDD)/40+40 MHz (FDD)
Minimum IMT-2020 Performance Requirements for Indoor Hotspot Test Environment for configurations A, B and C as outlined in [2]:
Indoor Hotspot – eMBB | Downlink (bit/s/Hz) | Uplink (bit/s/Hz)
5th Percentile User Spectral Efficiency | 0.3 | 0.21
Average Spectral Efficiency | 9 | 6.75
[1] ITU-R M.2412, “Guidelines for evaluation of radio interface technologies for IMT-2020.”
[2] ITU-R M.2410, “Minimum requirements related to technical performance for IMT-2020 radio interface(s).”

## Slide 6: IMT-2020 Requirements for Indoor Hotspot
Meeting the minimum performance requirements [2] in any one of the evaluation configurations A, B OR C is sufficient for Indoor Hotspot as per [1, Section 8.4]:
Testing performance of Indoor Hotspot at 70GHz is therefore not a requirement for IMT-2020 self-evaluation.
“Evaluation configurations are defined for the selected test environments.... For the cases when there are multiple evaluation configurations under the selected test environment, one of the evaluation configurations under that test environment can be used to test the candidate RITs/SRITs. The technical performance requirement corresponding to that test environment is fulfilled if this requirement is met for one of the evaluation configurations under that specific test environment.”
[1] ITU-R M.2412, “Guidelines for evaluation of radio interface technologies for IMT-2020.”
[2] ITU-R M.2410, “Minimum requirements related to technical performance for IMT-2020 radio interface(s).”

## Slide 7: Summary and proposal
Summary
  Even with more optimistic PN profile (i.e. Example 2 in previous slide), the current FR2 numerology SCS120 doesn’t work at all even with ideal CPE (Common Phase Estimation).
  The simulation results for 70GHz using FR2 numerology are simply wrong since it is not practically feasible.
  Other numerologies than FR1/FR2 SCS15/30/60/120 are not supported up to Rel-16 NR specifications.
  Testing performance of Indoor Hotspot at 70GHz is not a requirement for IMT-2020 self-evaluation.
Proposal
  Do not include simulation results at 70GHz in TR37.910 and IMT-2020 submission