## Slide 1: Views on NR Rel-17
China Telecom
June 4, 2019
3GPP TSG RAN Meeting #84
Newport Beach, USA, June 3-6, 2019
Agenda: 8
RP-191449

## Slide 2: Outline
NR coverage enhancement
Network energy saving
NR-WLAN dual connectivity
RAN enhancement for Multi-USIM UE
Other topics interested

## Slide 3: NR coverage enhancement : Motivation
The coverage issue has attracted much interest in LTE phase
  In TR 36.824, the system bottleneck in terms of LTE coverage performance was identified, and corresponding coverage enhancements were adopted in Rel-12
  Then, the further coverage enhancements were developed during Rel-13 and Rel-14 work
In NR, continuous and ubiquitous coverage is required for some scenarios with higher carrier frequency than LTE [TR 38.913]
Due to the higher carrier frequency, operators may need to add more sites to ensure sufficiently good coverage comparable to LTE. Adding sites is costly and requires lengthy negotiations with building owners etc. Operators will face great challenges in ensuring sufficient coverage and cost effective deployments for NR.

## Slide 4: NR coverage enhancement : Link level analysis
Coverage evaluation at 3.5GHz in Urban-Macro scenario
The coverage of control and data channel is unbalanced
PUSCH will still be the limited factor in terms of coverage in higher frequency
Chart: 
| PUSCH 1Mbps | PUCCH format 1 | PRACH format B4 | PDSCH 50Mbps | Common PDCCH | PBCH
Coverage Distance(m) | 261 | 670 | 530 | 449 | 626 | 756

## Slide 5: NR coverage enhancement : Field test
China Telecom has launched field test of standalone NR in 3.5GHz
  O2O: 3.5GHz incurs about 7-9dB higher pathloss than 1.8GHz
  O2I: the O2I penetration loss of one wall for 3.5GHz is about 5-8dB higher than 1.8GHz
UE position | LTE UL Throughput | NR UL Throughput
1 (8366) | 40Mbps | 94Mbps
2 (8342) | 24Mbps | 28.6Mbps
3 (8315) | 841Kbps | 663Kbps

## Slide 6: NR coverage enhancement : Email discussion
As per the agreements in RAN #79, there was an email discussion on NR coverage before RAN #80. In the email discussion 25 companies including 10 operators shared their views and it was summarized that,
  Various scenarios, e.g., urban macro, rural/low mobility large cell, urban micro/dense urban, were proposed for NR coverage study.
  Candidate frequencies, e.g., 800MHz, 1.8GHz, and 3.5GHz for FR1; 30GHz and 40GHz for FR2, were proposed for NR coverage study.

## Slide 7: NR coverage enhancement : Objectives of new SID
The objectives of this study item are to identify the achievable coverage of Rel-16 NR for specific scenarios and to study potential coverage enhancement solutions for both FR1 and FR2. The detailed objectives are as follows.
Evaluate Rel-16 NR coverage performance based on link level simulations for the following scenarios
  FR1 (both paired and unpaired spectrum) and FR2 (unpaired spectrum)
  eMBB and VoIP (considering latency requirement for voice calls)
Compare Rel-16 NR coverage with LTE coverage for
  FR1 (both paired and unpaired spectrum)
  eMBB and VoIP (considering latency requirement for voice calls)
Based on the above evaluation, identify the target scenarios/channel(s) for coverage enhancement
Study solutions for increasing coverage for both FR1 and FR2 considering
  Reduction/elimination of coverage imbalances
  Backward compatibility
  See more details in attachment 1.

## Slide 8: Network energy saving : Motivation
In traditional LTE network, the power consumption from base station reaches to 70% of total power consumption. Energy cost in the network has been a continuous high focus among operators.
Although NR is designed to be more power friendly comparing to LTE, some measurement and evaluation have shown that NR network power consumption will be 3~4 times higher than LTE.
Thus, further enhancement on NR network energy saving would be necessary in Rel-17.
Parameter | LTE value |  | NR value |  | Note
1 BS | 3 RRU | 1 BBU | 3 AAU | 1 BBU | 
Peak power (W) | 780 | 130 | 2910 | 200 | 260W/RRU 970W/AAU
Total power(W) | 910 |  | 3110 |  | 
Total cost (CNY)/year | 6.8k |  | 23.1k |  | 0.85CNY/kWh
Estimation of power consumption and cost: LTE vs. NR

## Slide 9: Network energy saving : Technical solutions
Enhancement on minimizing time/frequency/space domain transmission resource allocations. (e.g. optimization on cell DTX, power control and TxRU switching)
  TxRU switching: Little system performance degradation when reducing transmission ports from 64 to 32
Enhancement on intra/inter RAT networking energy saving. (e.g. Energy information interaction between Macro and Micro base stations with ‘smart’ network planning)
64T
32T
Chart: System performance in UMA scenario, ISD=500m
| Avg.UPT | 5%-tile UPT
64TxRU | 1 | 1
32TxRU | 0.92 | 0.85

## Slide 10: Network energy saving : Objectives of new SID
The objectives of the work item is to introduce the support for the potential solutions for enhancement on NR network energy saving by
Study on the potential solutions to enhance NR network energy saving include:
  Dynamic TRX on/off with enhanced CSI measurement to reduce impact on user experience
    Network decides if switching off TRX by referring to UE reports of all the possible configured CSI measurement results in order to reduce impact on user experience.
  Efficient cell activation/de-activation procedure with introduction of energy saving mode
    This solution is for the scenario in which LTE providing basic coverage and NR offloading the data traffic from LTE.
    NR can activation/de-activation according to the network load by introducing long cycle signals such as SSB or RMSI.
  Latency aware scheduling enhancement to improve the sleep ratio and duration
    Optimize the date packets integrated transmit and reduce the fragment transmit by introducing signals for BS to obtain the service latency requirement from the Core Network.
  Enhancement on intra/inter RAT networking energy saving. (e.g. Energy information interaction between Macro and Micro base stations with ‘smart’ network planning)
Narrow down the solutions according to the study conclusion and clarify the necessary modifications to the corresponding specifications with not limit to RAN1-4 specifications.
  See more details in attachment 2.

## Slide 11: NR-WLAN dual connectivity : Motivation
LTE has laid solid foundation on tight interworking with WLAN, i.e. LTE-WLAN Aggregation (LWA), RAN Controlled LTE-WLAN interworking, and LTE/WLAN Radio Level Integration with IPsec Tunnel (LWIP), to enable operators to take full advantage of the unlicensed spectrum and WLAN network.
Likewise, NR-WLAN dual connectivity would also bring benefit on throughput, peak data rate, mobility and network management.
During NR study phase, the scenarios of NR-WLAN integration have been roughly discussed, however no further work done due to time issue.
IEEE have also made one of way towards 5G by tight interworking with NR [1].
  Action B3: IMT-2020 – external body proposal
    Support development of a 3GPP proposal incorporating references to the use of IEEE 802.11, or an IEEE 802 Access Network
  Action A: IEEE “5G” specification
[1] EC-16-0119-01-5GSG IEEE 802 EC 5G / IMT-2020 Standing Committee Report

## Slide 12: NR-WLAN dual connectivity : Objectives of new WID
Scenarios of NR-WLAN dual connectivity
Solutions to realize NR-WLAN dual connectivity, LTE solutions (LWA, RCLWI, LWIP) can be baseline, down selection may be needed.
Investigate potential enhancements compared with LTE baseline:
  CP enhancement, e.g. fast WLAN addition, retain WLAN connection while NR is out of coverage
  UP enhancement, e.g. direct UP connection between WLAN and 5GC.
  Cooperation with SA working groups as well as IEEE may be required.
  See more details in attachment 3.

## Slide 13: RAN enhancement for Multi-USIM UE : Motivation
Multi-USIM devices have been more and more popular in different countries. However, the support for multi-USIM is currently handled in an implementation-specific manner.
SA2 has already start working on multi-SIM for Release-16, following-up RAN2 work should be done in Rel-17 in order to complete the standardization work of related RAN functions.
  A mechanism for delivering paging destined to USIM A while the UE is actively communicating with USIM B
  A mechanism allowing for suspension (or release) and resumption of an ongoing connection in the 3GPP system associated with USIM A, so that the UE can temporarily leave to the 3GPP system associated with USIM B
It is expected that specification work for Multi-USIM UE in RAN comprise the following:
  SA2 scope with RAN impacted shall also be studied in RAN
  new NR RAN specific solutions for the support of Multi-USM UE
  See more details in attachment 4.

## Slide 14: RAN enhancement for Multi-USIM UE : Potential scope
Scenarios to be considered:
  Different UE low layer capabilities, single Rx / single Tx , dual Rx / single Tx UE and dual Rx / dual Tx implementation should be considered.
  Both Inter-MNO and intra-MNO scenarios should be considered.
  Both LTE and NR, i.e. SIM A NR，SIM B NR; SIM A LTE, SIM B LTE; SIM A NR, SIM B LTE, should be considered.
Define RAN solutions for Multi-USIM UE in co-operation with SA2:
  Mechanisms for receiving paging or perform measurement for USIM A while the UE is actively communicating with USIM B in single connection or DC configuration.
  Mechanisms allowing for suspension (or release) and resumption of an ongoing connection in the 3GPP system associated with USIM A, so that the UE can temporarily leave to the 3GPP system associated with USIM B.
  Mechanisms for avoidance of paging collisions occurring in the UE between USIM A and USIM B.
  Power control and UE capability coordination for voice service in USIM A and data service in USIM B.

## Slide 15: Other topics interested
Capacity enhancement
MIMO enhancement
URLLC enhancement
NR V2X enhancement
IIoT enhancement
NR UDC
NR QoE management and optimization

## Slide 16: Thanks!